## Slide 1
Teri Dykhuis
PIP-II Independent Project Review
12-14 December 2017
Environment, Health, Safety, and Quality (ESH&Q) Strategy
Project Management

## Slide 2: Outline
Vision/Commitment
Documentation
NEPA
Summary

## Slide 3: About me
Role on Project
  PIP-II Associate Project Manager/ESH&Q
  PIP-II NEPA Subproject Manager
Relevant Experience
  ESH Specialist/ESH&Q Section for 17 year
  Fermilab NEPA Program Manager; integrally involved in all NEPA related activities at Fermilab for the past 17 years
  ESH Professional for 31 years
  Environmental Engineer

## Slide 4: ESH&Q Vision/Commitment
Project team is committed to construct PIP-II in a safe, environmentally respectful, and cost efficient manner that meets our stakeholder’s needs
  Maintain a safe workplace for our workers, subcontractors, site occupants and guests
  Protect human health within our boundaries
  Achieve and maintain compliance with all applicable ESH&Q requirements

## Slide 5: ESH&Q Documentation
Documents that support the project’s current state of ESH&Q development and are necessary for CD-1 per DOE Order 413.3B: Program and Project Management for the Acquisition of Capital Assets
  Preliminary Security and Vulnerability Report (Docdb #143)
  Integrated ESH&Q Management Plan (Docdb #141)
  Preliminary Hazards Analysis Report (Docdb #140)
  Quality Assurance Program (Docdb #142)
Charge #5

## Slide 6: ESH&Q Documentation
  No unique security issues presented by the PIP-II Project
  Activities planned are unclassified and no safeguards and security issues are forseen
  PIP-II will comply with DOE and Fermilab Unclassified Foreign Visits and assignment program
  PIP-II will be executed as a construction project within the Fermilab, FRA, and DOE framework
  All PIP-II buildings will be located at Fermilab and will follow Facility Site Access requirements
Preliminary Security Vulnerability Assessment

## Slide 7: ESH&Q Documentation
  All work associated with the project will be conducted in a manner that ensures protection of the workers, the public, and the environment
  Project will utilize an Integrated Safety Management System (ISMS) to integrate safety systematically into work activities
  Line managers, supported by the ESH&Q organization, will provide consistent guidance and enforcement of the ESH&Q program that governs the activities of workers at Fermilab and partner locations
  Project will comply with the NEPA
  Design reviews and safety assessments of facility systems and operations will be conducted during preliminary and final design to minimize waste generation and evaluate opportunities for pollution prevention
  The Project Conventional Facilities will be constructed utilizing the federal Guiding Principles for High Performance and Sustainable Buildings
  All ESH&Q requirements will be flowed down to subcontractors via contract documents
Integrated Environment, Safety and Health Management

## Slide 8: PIP-II Safety Framework
PIP-II FPD
PIP-II
PM
PIP-II
PD
PIP-II
CC
PIP-II Subcontractors
PIP-II
L2
PIP-II L2
ES&H Plan
Approves
Approves
Approves
Implementation
PIP-II Project Team complies with and promotes the Safety Plan
Safety built into work performed
PIP-II ES&H Coordinator drafts, reviews, and assesses ES&H Plan

## Slide 9: ESH&Q Documentation
  Focus of the PHAR is:
  qualitatively evaluate each hazard area by identifying the initiator hazard and its consequences,
  establish a pre-mitigation risk category,
  recognize design features to mitigate that risk and then
  establish a post mitigation risk category
  The hazard evaluation process is a qualitative assessment of potential impacts in terms of:
  hazards
  initiators
  likelihood estimates
  preventive or mitigating features and
  public, environmental, and worker consequence estimates
  The results of these evaluations confirm that the potential risks from operations and maintenance are acceptable
Preliminary Hazard Analysis

## Slide 10: ESH&Q Documentation
  Resources available for development of the PHAR included:
  Fermilab staff,
  PIP-II L2 Managers, and
  lessons learned from the DOE accelerator community
  The identified hazards were further developed in the PHAR by considering the proposed ESH&Q design enhancements as the design evolved
  The risks associated with the hazards were reanalyzed and in certain cases operational controls to develop a post-mitigation risk category were also included
Preliminary Hazard Analysis

## Slide 11: ESH&Q Documentation
  The PHA process was initiated by developing a Conceptual Design Baseline Hazards List:
  Construction
  Natural Phenomena
  Environmental
  Waste
  Fire
  Electricity
  Noise/Vibration/Thermal/Mechanical
  Cryogenic/Oxygen Deficiency
  Confined Space
  Ionizing Radiation Exposure, inside of the accelerator or beamline enclosure
  Chemical/Hazardous Material
  Accelerator/Beamline Hazards
  Ionizing Radiation Hazards, outside accelerator or beamline endlosure
  Lasers & other Non-ionizing Radiation Hazards
  Material Handling
Preliminary Hazard Analysis

## Slide 12: ESH&Q Documentation
Prompt radiation
Residual (activated components)
Contamination
Airborne Contamination
Hazard Initiator(s): Beamline component failure, insufficient shielding, procedural violation
Hazard Consequence: Potential for excessive radiation dose and possible injury or death
Preliminary Hazard Analysis for Ionizing Radiation Exposure, inside the accelerator or beamline enclosure

## Slide 13: ESH&Q Documentation
  MITIGATING FACTORS (Design):
Well-designed shielding for accelerators to reduce dose to ALARA levels.
Interlock systems, e.g. if interlock broken, emergency beam shut-off capability, audible/visual alarms
Redundant interlock systems for beamline enclosures
Redundant radiation safety critical devices (e.g., transfer line beam stops, beamline safety shutters) will be evaluated
Real-time beam loss monitoring system.
Shielding around beamline, multi-legged entrance maze to minimize leakage; single-block concrete construction wherever possible, tongue-and-groove to eliminate line-of-sight.
Public areas (e.g., walk ways) should not be exposed to significant radiation fields produced by machine operations or by equipment
  MITIGATING FACTORS (Operational):
Radiological protection program incorporating requirements of 10 CFR 835, Accelerator Safety Order
Strict configuration control of shield and interlock systems
Routine area monitoring of dose levels by passive dosimeters for neutrons and gammas on the experimental floor (and other occupied areas subject to radiation)
Radiological safety training, e.g. Radiation Worker, General Employee Radiological Training, etc.
Facility Specific Safety Orientation and ESH&Q Orientations
Work Planning and control procedures for work in radiation areas or with radioactive materials
ALARA designs and committee reviews
Safety protocols for workers using or machining lead
Time delays for entry into enclosures (cool down)
Preliminary Hazard Analysis for Ionizing Radiation Exposure, inside the accelerator or beamline enclosure

## Slide 14: ESH&Q Documentation
  Risk Assessment Prior to Mitigation:
  Consequence = High
  Probability = Occasional
  Risk Category = High
  Risk Assessment Following Mitigation:
  Consequence = High
  Probability = Remote
  Risk Category = Moderate
Preliminary Hazard Analysis for Ionizing Radiation Exposure, inside the accelerator or beamline enclosure

## Slide 15: ESH&Q Documentation
Preliminary Hazard Analysis for Ionizing Radiation, Outside Accelerator Enclosure
Hazard Initiator(s): Accelerator or beamline component failure, insufficient shielding, procedural violation, air monitoring system failure, surface radiation monitoring system
Hazard Consequence: Potential for radiation dose and possible injury or death to personnel, potential radiological release

## Slide 16: ESH&Q Documentation
  MITIGATING FACTORS (Design):
Well-designed shielding for accelerators to reduce dose to ALARA levels.
Passive shielding and real-time beam loss monitoring system for surface.
Public areas (e.g., walk ways) should not be exposed to significant radiation fields produced by machine operations or by equipment, including magnetic or RF fields
  MITIGATING FACTORS (Operational):
Radiological protection program incorporating requirements of 10 CFR 20
Strict configuration control of shield and interlock systems
Routine area monitoring of dose levels by passive dosimeters for electrons on the experimental floor (and other occupied areas subject to radiation
Implement groundwater monitoring system
Implement air activation monitoring system
Work planning and control procedures for work in radiation areas or with radioactive materials
Preliminary Hazard Analysis for Ionizing Radiation Exposure, Outside Accelerator Enclosure

## Slide 17: ESH&Q Documentation
  Risk Assessment Prior to Mitigation:
  Consequence = High
  Probability = Occasional
  Risk Category = High
  Risk Assessment Following Mitigation:
  Consequence = High
  Probability = Remote
  Risk Category = Moderate
Preliminary Hazard Analysis for Ionizing Radiation Exposure, inside the accelerator or beamline enclosure

## Slide 18: ESH&Q Documentation
Hazard Initiator(s): Electrical shock/arc flash from exposed conductors, defective equipment, substandard equipment or improper procedure.
Hazard Consequence: Death, permanent injury, equipment damage
Facility
Experimental
Job built Equipment
Low Voltage/High Current
High Voltage/High Power
Maintenance
Arc flash
Electrical shock
Cable tray overloading/mixed utilities
Exposed 110v
Stored energy (capacitors & inductors
Preliminary Hazard Analysis for Electrical Hazards

## Slide 19: ESH&Q Documentation
  MITIGATING FACTORS (Design):
Design to NFPA 70 and 70 E National Electric Code
Provide adequate power distribution to reduce need for extension cords
Provide segregated power and utility distribution; no over-loading (cable/utility trays)
Electrical and mechanical equipment rooms adequately sized and accessible from outside of ring.
Electrical distribution/disconnect equipment located in unobstructed areas (physically marked to provide clear access/maintain clearances),
Protect equipment and cables from mechanical and other hazards
Conduct arc flash calculations, determining PPE requirements, and label all electrical panels and switches
Assess need and feasibility for remote operation of high voltage switches and breakers to prevent human contact during opening and closing
Implement Lockout/Tagout capability into design of energized equipment
  MITIGATING FACTORS (Operational):
Non-NRTL equipment inspected and certified by competent person
Engineering and beamline design reviews
Operation of equipment at <50 volts where feasible
SBMS procedures for electrical safety
Electrical safety training
Operational procedures to keep electrical equipment unobstructed
Inspection program
Preliminary Hazard Analysis for Electrical Hazards

## Slide 20: ESH&Q Documentation
  Risk Assessment Prior to Mitigation:
  Consequence = Moderate
  Probability = Probable
  Risk Category = High
  Risk Assessment Following Mitigation:
  Consequence = Moderate
  Probability = Occasional
  Risk Category = Moderate
Preliminary Hazard Analysis for Ionizing Radiation Exposure, inside the accelerator or beamline enclosure

## Slide 21: ESH&Q Documentation
Pre- and post-mitigation risk category for each of the 15 hazard types found with PIP-II
Preliminary Hazard Analysis
PHA Hazard Identifier | Hazard | Pre-Mitigation Risk Category | Post Mitigation Risk Category
PIP-II PHA-1 | Construction | High | Moderate
PIP-II PHA-2 | Natural Phenomena | Low | Routine
PIP-II PHA-3 | Environmental | Moderate | Low
PIP-II PHA-4 | Waste | Moderate | Low
PIP-II PHA-5 | Fire | Moderate | Low
PIP-II PHA-6 | Electrical | High | Moderate
PIP-II PHA-7 | Noise, Vibration, Thermal, Mechanical | Moderate | Low
PIP-II PHA-8 | Cryogenic & Oxygen Deficiency | High | Moderate
PIP-II PHA-9 | Confined space | Moderate | Low
PIP-II PHA-10 | Ionizing Radiation exposure, inside accelerator enclosure | High | Moderate
PIP-II PHA-11 | Chemical | Moderate | Low
PIP-II PHA-12 | Accelerator/Beamline | Moderate | Low
PIP-II PHA-13 | Ionizing Radiation exposure, outside accelerator enclosure | High | Moderate
PIP-II PHA-14 | Non-Ionizing Radiation | Moderate | Low
PIP-II PHA-15 | Material Handling | High | Moderate
PHAR Table 6‑1: Risk Assessment Summary

## Slide 22: ESH&Q Documentation
  Conclusion
  Currently nine of the risk categories have been mitigated to “Low or below” and six remain at a “Moderate” level; the latter include construction, electrical, ionizing radiation inside/outside, cryogenics, and material handling.
  PIP-II design objective to reduce hazards to no more than minor on-site and negligible off-site impacts to people and the environment during construction and operations
  Post-mitigation risk category conveys a realistic assessment of the residual risk posed by the PIP-II facility and became a critical input to the preliminary design effort
Preliminary Hazard Analysis

## Slide 23: ESH&Q Documentation
  The PIP-II Project Office is responsible for ensuring the quality of all items fabricated for PIP-II and must ensure that the project structure and organization are appropriate for effectively carrying out this mission.
  Fermilab and Division Quality Assurance Policies and Procedures are followed for work being conducted within Fermilab Divisions for PIP-II.
  Additionally, PIP-II and PIP-II Partners follow the Fermilab Engineering Standards Manual and all applicable domestic and/or international codes and standards.
  PIP-II management at all levels shall regularly evaluate achievement relative to performance requirements and shall appropriately validate or update performance requirements and expectations to ensure quality.
Quality Assurance Program (QAP)

## Slide 24: ESH&Q Documentation
  The PIP-II PM has the overall responsibility for quality improvement throughout the project and is supported by the PIP-II Machine Advisory Committee (P2MAC)
  At the Project level, the P2MAC:
  takes steps to detect and prevent quality problems
  identify the cause and correction of quality issues, and
  strive towards improvement
  At the Subsystem level, these responsibilities devolve onto the Level 2 Managers. The Level 2 Managers are responsible for:
  developing and documenting processes,
  making technical specifications for subsystem elements, and
  carrying out QA procedures to ensure that products and procured items conform to these specifications
  Level 2 Managers may delegate QA responsibilities to L3 Managers as appropriate
QAP

## Slide 25: ESH&Q Documentation
Risk strategy described in PIP-II-doc-1201
Laboratory has instituted FESHM Chapter 2110 - Ensuring Equivalent Safety Performance when Using International Codes and Standards
Experience integrating cryogenic feedcans from DAE into CMTS
Learning from LBNF experience
QAP and PIP-II International Partners

## Slide 26: Requirements
DOE Order 413.3B: Program and Project Management for the Acquisition of Capital Assets
10 CFR Part 1021 DOE NEPA Implementing Procedures
Deliverables
CD-1
  Complete a National Environmental Policy Act (NEPA) Strategy by securing a determination (e.g., Environmental Assessment) from DOE/FSO, as required by DOE O 451.1B.
CD-2
  Issue the final Environmental Impact Statement or Environmental Assessment and Finding of No Significant Impact, as required by DOE O 451.1B.
NEPA Strategy

## Slide 27: Progress to date
NEPA Environmental Evaluation was completed and submitted to DOE FSO on 8/18/2017
A final NEPA determination supporting the completion of an Environmental Assessment was issued by DOE-FSO on 8/25/2017 (DOE Document = DOE/FSO-2072)
EA notification letters were submitted to State agencies in Illinois on 9/13/2017
Teri Dykhuis (PIP-II NEPA Subproject Manager) is coordinating the effort to ensure completion of the Environmental Assessment
The PIP-II NEPA strategy is to conduct an Environmental Assessment that will cover all PIP-II activities; this approach is similar to the one used for LBNF, and NOvA
Procurement has awarded the bid for the EA to Arcadis
Charge #5
NEPA Strategy

## Slide 28: Work yet to be completed (for CD-2)
Kick off meeting will be conducted in January of 2018
Subcontractor will develop a schedule to complete the EA
  EA determines whether there would be no significant impact and if an EIS is or is not required
  If no EIS, then a Finding of No Significant Impact (FONSI) will be developed by the DOE FSO and made available to the general public and Project Stakeholders
The NEPA process will be completed by CD-2 or before any construction work (estimated 6-8 months for EA completion)
Charge #5
NEPA Strategy

## Slide 29: Summary
Is the NEPA Strategy being properly addressed given the project’s current state of development?
  NEPA determination has been made - Environmental Assessment
  Experienced ES&H professionals assigned PIP-II NEPA subproject
  FNAL and PIP-II management are actively engaged
  The NEPA process will be completed by CD-2 or before any construction work (estimated 6-8 months for EA completion, from time of initiation)
NEPA Strategy
Charge #5

## Slide 30: ESH&Q Strategy
Are ESH&Q and ISM aspects being properly addressed given the project’s current state of development?
  All CD-1 documentation has been developed
  NEPA determination in place – EA
  Experienced ESH&Q professional assigned to the Project
  Hazard analyses and work planning are integral to the safety process
  PIP-II management is actively engaged
  ESH&Q is integrated to support design and construction
  Lessons Learned continue to be integrated into ongoing project planning
  All work is similar to work performed at the Lab previously
  CD-2 Documentation in process
Summary
Charge #5