## Slide 1
Charge-Coupled Devices Steve Holland / Lawrence Berkeley National Laboratory

## Slide 2: Examples of astronomical CCD cameras
HyperSuprimeCam – 116 2k x 4k, (15 µm)2-pixel CCDs
CCDs from Hamamatsu Corporation
Subaru 8-m Telescope
870 Mpixels
FermiLab Dark Energy Survey Camera (DECam)
62 2k x 4k, (15 µm)2-pixel CCDs
CCDs from DALSA Semiconductor / LBNL
NOAO Cerro Tololo Blanco 4-m Telescope
Both use fully depleted CCDs, and have been operating since 2012
520 Mpixels

## Slide 3: Astronomical cameras with fully depleted CCDs
FermiLab Dark Energy Survey Camera (DECam)
62 2k x 4k, (15 µm)2-pixel CCDs (520 Mpixels)
CCDs from DALSA Semiconductor / LBNL
Full moon for scale

## Slide 4: Astronomical cameras with fully depleted CCDs
FermiLab Dark Energy Survey Camera (DECam)
62 2k x 4k, (15 µm)2-pixel CCDs (520 Mpixels)
CCDs from DALSA Semiconductor / LBNL
Full moon for scale
Roughly 50k galaxies per image
~ Goal is 300M galaxies studied during the Dark Energy Survey

## Slide 5: Astronomical cameras with fully depleted CCDs
HyperSuprimeCam – 116 2k x 4k, (15 µm)2-pixel CCDs (870 Mpixels)
CCDs from Hamamatsu Corporation / Subaru 8-m Telescope
http://subarutelescope.org/Topics/2016/05/12/
Full moon for scale

## Slide 6: Astronomical cameras with fully depleted CCDs
HyperSuprimeCam – 8 degrees x 3 degrees field of view
Video courtesy of Satoshi Miyazaki / Subaru Telescope

## Slide 7: DESI CCDs (in production)
DESI CCDs are 16 Mpixel imagers with
  Dark currents at -140C of about ~1 e-/pixel-hr (limited by 300K blackbody radiation)
  Noise levels approaching 1 e- rms at slow readout speeds
  PSF ~ 4 – 5 m rms
  150 mm wafers
    DALSA Semiconductor
    Finishing at LBNL
DESI: Dark Energy Spectroscopic Instrument

## Slide 8: LSST CCDs (in production)
Uniform illumination
Test target image
CCD in test fixture
T-E2v CCD250
T-DALSA/ITL STA3800C
100 m thick
Fully depleted
4k x 4k
10 m pixels
16 amplifiers
189 CCDs
3.2 Gpixels
Courtesy of Paul O’Connor of Brookhaven National Laboratory

## Slide 9: Invention (Innovation meets need)
Brief history of the CCD follows as well as innovations from the early era (1970’s) that have led to where we are today
  CCD invention
  Polysilicon gate electrodes
  Correlated double sampling

## Slide 10: Invention (Innovation meets need)
Invented by Boyle and Smith (Bell Laboratories) on September 8th, 1969 (Nobel Prize in Physics 2009)
Tasked to find a semiconductor analogy to the magnetic “bubble memory”
The basic concepts were conceived in a discussion session between Boyle and Smith “lasting not more than an hour” 1,2
[1] W.S. Boyle and G.E. Smith, “The inception of charge-coupled devices,” IEEE Trans. Elec. Dev., 23, 661, 1976.
[2] G.E. Smith, “The invention of the CCD”, Nucl. Instrum. Meth. A, 471, 1, 2001.

## Slide 11: Motivating Innovation
“To understand the atmosphere at the time, one must look at the structure of the Electronics Division at Bell Labs which was under Vice President Jack Morton. This was split into two divisions, one for semiconductor devices and one for all others. Bill Boyle was Executive Director of the semiconductor part and I was a department head under him. Jack Morton was anxious to speed up the development of magnetic bubbles as a major memory technology and there was talk of transferring resources from Bill’s division to the other where the bubble work was being done. For this not to happen, Morton demanded that Bill’s division come up with a semiconductor device to compete with bubbles. To address this demand, on 17 October 1969, Bill and I got together in his office. In a discussion lasting not much more than an hour, the basic structure of the CCD was sketched out on the blackboard, the principles of operation defined, and some preliminary ideas concerning applications were developed.”
http://aip.scitation.org/doi/full/10.1063/1.3578638

## Slide 12: Recollections of Willard Boyle
“Picturephone” (1970’s Facetime) conversation: Jack Morton / Bell Labs VP, W. Boyle
"Boyle?" "Hello Jack." "So what happened yesterday?" came the familiar refrain. Boyle shifted a little more in his chair.
"I can't see you, Bill," said Morton. "Right here, Jack."
"So what'd you guys do yesterday?" "You know, more of the same. We're still working on those new transistors," said Boyle. "Look Bill, the other guys are doing great stuff with magnetic bubbles. It's terrific. What are you semiconductor guys doing? The hell with transistors. Try and come up with something different. I'll call tomorrow." And he hung up.

## Slide 13: Boyle/Smith notebook entry
Relies on collection, storage and transport of photogenerated electrons or holes in potential wells formed by depletion regions under closely-spaced MOS1 capacitors
3-phase CCD diagram (lab notebook drawing Sept. 1969)
F1
F2
F3
F2 low
F1 low
F2 low
F2 high
F1 low
1Metal oxide semiconductor

## Slide 14
2-D simulation of charge transfer

## Slide 15
Triple polysilicon CCD pixel
Poly 1
Poly 3
Poly 2
Overlapping polysilicon gates used in modern scientific CCDs
Also invented at Bell Labs
Sequin et al, 1974
Prof. Emeritus UC-Berkeley EECS

## Slide 16: CCD early history
Early adopters of CCDs were Sony (commercial manufacturing) and the Jet Propulsion Laboratory (scientific applications for NASA)
  JPL effort with Texas Instruments for Hubble
Sony CCD production through 1999

## Slide 17
Link to paper
Early CCD development at JPL
Link to book

## Slide 18: Scientific CCD typical operation
Charge is transferred from the imaging area a row at a time into serial registers where the charge is shifted to source follower amplifiers that convert the charge to voltage (noise determined at this step)
Diode sense node
“Floating diffusion”

## Slide 19: Correlated double sampling
Another key invention from the 1970’s:
  Correlated Double Sampling:
  Eliminate kTC noise from the reset switch
10 V/e- conversion factor implies 15 fF
kTC noise would be about 49 electrons!
Scientific CCDs achieve a few e- noise
  Method:
1) Measure reset level
2) Transfer charge to the sense node
3) Measure signal
4) Subtract reset from signal
1M.H. White, D.H. McCann, I.A.G. Mack, F.C. Blaha, U.S. Patent 3,781,574, Dec. 1973
Link to patent and paper

## Slide 20: Correlated double sampling
Presently
Ohio State
ECE Prof.

## Slide 21: EDIT 2018 CCD talk
Remainder of the talk
  Thinned and fully depleted CCDs
  CCD performance parameters
  Future prospects

## Slide 22: CCDs for Astronomy
Two main types of astronomical CCDs
  Thinned and back-illuminated
    10 – 20 microns thick
  Thick and fully depleted
    250 – 650 microns thick
    Fully depleted with bias voltage
  Spectrographs often use thin CCDs for the blue wavelengths and FD CCDs for the red wavelengths
  Imaging cameras use fully depleted CCDs when red response is important, DECam, HyperSuprime CAM, LSST

## Slide 23: CCDs for Astronomy
Thinned CCDs
  Selective etch stops on the lightly doped epitaxial layer
  Backside treatment for high blue quantum efficiency
  Depletion depth limited by resistivity
    10 – 20 m typically, “Deep depletion” ~ 50 m
  Drawbacks include poor QE and fringing at red wavelengths, and possible spatial resolution degradation due to field-free (undepleted) region at the back surface

## Slide 24: CCDs for Astronomy
Thinned CCDs: Electrostatic potential at surface
  1-D simulation of the Poisson Eq (depletion approx)
Potential maximum some distance into the silicon bulk and away from trapping sites at the surface / due to the buried channel that is doped opposite to that of the substrate

## Slide 25: CCDs for Astronomy
Fully depleted CCDs
  Merging of CCD / pin diode from High-Energy Physics
    See Sally Seidel’s talk next week describing HEP tracking detectors based on fully depleted, pin diodes
  Excellent red response due to thickness
  Spatial resolution a tradeoff between thickness and substrate bias voltage
  Drawbacks include long tracks from cosmic rays and background radiation, and exacerbated effects due to lateral electric fields that affect precision measurements

## Slide 26
Vsub = 80V
Vsub = 30V
Potential minimum (collecting phase)
MEDICI simulations
Fully depleted CCDs / 2D simulations

## Slide 27
MEDICI simulations
Potential minimum (collecting phase)
Relatively insensitive to Vsub
Wide range of Vsub possible
Capacitor voltage divider effect
Vsub = 80V
Vsub = 30V
Fully depleted CCDs / 2D simulations

## Slide 28: CCD performance
Key CCD performance parameters
    Quantum efficiency
    Dark current
    Noise

## Slide 29: Optical properties of Si / Ge
Absorption in semiconductors
  Si and Ge are indirect gap semiconductors
  Valence band maximum and conduction band minimum do not correspond to the same “crystal” momentum
    Quantum mechanics calculations for an electron in a periodic potential
  For photon energies less than the direct bandgap, phonons (lattice vibrations) are required to conserve momentum
    Inefficient and temperature-dependent

## Slide 30: Optical properties of Si / Ge
Absorption in semiconductors cont’
T.S. Moss, “Optical properties of semi-conductors,” Butterworths Scientific Publications, 1959 and J.I. Pankove, “Optical processes in Semiconductors,” Prentice-Hall, Inc., 1971.
Germanium
Silicon
Strong absorption for Eph > Eg,direct ( = 0.5 and 1.55 m for Si, Ge)
Becoming transparent for Eph  Eg,indirect ( ~ 1.1 and 1.85 m for Si, Ge)
Realistic cutoff for Ge more like 1.5 um
Indirect
absorption
process

## Slide 31: Quantum efficiency
Near IR – Silicon becoming transparent, Eph  Si bandgap (~ 1.1 eV)
Blue end – Strong absorption in dead layers (n+ of p-i-n structure)

## Slide 32: Quantum efficiency
When the absorption length is > the CCD thickness,
multiply reflected light results in “fringing”

## Slide 33: Fringing in thinned CCDs
Fringing – Multiply reflected light in 10 – 20 µm thick CCDs
Uniform illumination (R. Stover / M. Wei Lick Observatory)
l = 8000A 9000A 10,000A
~  40%
(Laboratory)
For 250 m thick DECam CCDs, the fringing is negligible

## Slide 34: CCD performance
Key CCD performance parameters
    Quantum efficiency
    Dark current
    Noise

## Slide 35: Dark Current
Dark current from the substrate is determined by extremely low levels of unwanted impurities that have energy states near the center of the bandgap
10-5 of a monolayer is too much contamination!
Special fabrication steps to maintain low dark current

## Slide 36: Dark Current
Dark current measurements on a fully depleted LBNL CCD / line is the Shockley-Read-Hall model

## Slide 37: Dark Current
Leveling off at low temperatures is likely due to 300K blackbody radiation
  FermiLab innovation1: Direct dark matter detection with CCDs / ~ 0.001 e-/pixel-day at 120K with the CCDs in a cold enclosure
1Juan Estrada and others

## Slide 38: Dark Current
DAMIC roughly here with their cooled Cu box enclosure
0.001 e- / pixel-day at 120K (4 x 10-5 e- / pixel-hr)

## Slide 39: 30 minute dark at -140C / 80V VSUB
Tracks are cosmic ray muons and Compton electrons from U / Th in the background environment
Ability to achieve ultra-low dark current and low noise being exploited in direct dark matter detection (DAMIC and SENSEI)
169186.22.4/M1-28/dark1800s_Vsub80V_03.fits-f

## Slide 40
Cosmic rays
MOSAIC 3 Camera / 500 m thick CCDs

## Slide 41: CCD performance
Key CCD performance parameters
    Quantum efficiency
    Dark current
    Noise

## Slide 42: CCD amplifier noise
VR
MR
M1
VRG
VDD
GND
VOUT
RL
VSUB
Cgd,M1
CM
Cgd,MR
FD
p-channel
CP
CFD
Floating diffusion
Diode sense node
Output transistor M1

## Slide 43: CCD amplifier noise
Noise in electrons Qn depends on
1) SF transistor M1 noise
2) Total capacitance at the floating diffusion
White noise in M1 is given by
Reduce CT and/or improve the transistor (gm) to reduce noise

## Slide 44
CCD amplifier noise
Measured conversion gain versus transistor dimensions

## Slide 45
Measured read noise versus transistor dimensions (70 kpixels/sec, -140C)
CCD amplifier noise
Transistor used in LBNL CCDs for DESI has W/L = 20/6

## Slide 46: Transistor amplifier size study
R&D transistor with 22 nm gate insulator (SiO2) thickness
Conversion gain in ADU/e-
55Fe x-rays
Read noise in e- rms
70 kpixels/sec, -140C
JFET buffers

## Slide 47: CCD Noise
DESI CCD noise (Production lot #1)
  Noise vs Integration Time

## Slide 48: Skipper CCDs / sub-electron noise
Conventional CCDs nearing 1 e- read noise
Skipper CCDs take advantage of multiple sampling of the signal charge by use of a non-destructive readout amplifier (floating-gate)
  The noise is reduced by the square root on the number of samples
0.5 e- noise reported in 1990
  Chandler et al, SPIE 1242, 238, 1990 (Link)
  Janesick et al, SPIE 1242, 223, 1990 (Link)
  Field was dormant for about 20 years
  FermiLab / LBNL collaboration for dark matter

## Slide 49: Skipper CCDs / sub-electron noise
From Chandler et al, SPIE 1242, 238, 1990
Floating Gate sense node

## Slide 50: Skipper CCDs / sub-electron noise
Implementation on LBNL fully depleted CCD
Floating Gate sense node
Source follower transistor

## Slide 51: Skipper CCDs
Results from the SENSEI group based at FermiLab
0.068 e- rms after 4000 samples
Used for direct dark matter detection

## Slide 52: Skipper CCDs
Link to paper

## Slide 53: Future directions
Increase wavelength reach to ~ 1.4 m Germanium CCDs
  Cosmic Visions 2016 and 2018 reports
  Work underway at Lincoln Laboratory
  LDRD effort started at LBNL
J band

## Slide 54: Ge CCD effort at LBNL
  Mask design / partially processed Ge wafer shown
Fabrication efforts at LBNL and UC-Berkeley
Not nearly as straightforward as silicon
Ge wafer after 4 masks / 2 implants

## Slide 55: Future directions
  CMOS image sensors
    Have been back-illuminated since iPhone4
    Commercial CCDs are on the endangered list with the exception of compact digital cameras (20 Mpixel version shown)
Picture taken Jan 2018 with a back illuminated CMOS image sensor (iPhone6)

## Slide 56: 4T CMOS image sensor
CMOS image sensors have an source follower amplifier in each pixel
A transfer gate is included to take advantage of kTC noise reduction via double-correlated sampling
A. Theuwissen, IEEE Solid-State Circuits Magazine, 22, Spring 2010

## Slide 57: Front vs back illumination – CMOS
CMOS image sensors with small pixels need back illumination simply to get the light into the pixel
IBM front illuminated CMOS image sensor
2.2 µm pixel
2006 IDEM (Gambino et al)
Sony back illuminated CMOS image sensor
1.65 µm pixel
2010 ISSCC (Wakabayashi et al)

## Slide 58: 4T CMOS image sensor
Sony back-illuminated CMOS image sensor used in the Samsung Galaxy S7 (microlens at top of image)
Link to article

## Slide 59: CMOS image sensors
There is R&D underway in single-photon detection in CMOS image sensors
  Extremely low capacitance achievable in the advanced CMOS technologies, sub-electron noise possible
  Link to special issue of “Sensors” journal

## Slide 60: CMOS image sensors
2015 publication shows “golden” pixel with 0.22 e- noise, 423 V/e- conversion gain
  Ma et al, J. Elec. Dev. Soc., 3, 472, 2015 (link)

## Slide 61: CMOS image sensors
2017 publication from the same group
  Ma et al, Optica., 4, 1474, 2017 (link)
  NSF SBIR Phase I awarded (link)

## Slide 62: CMOS image sensors
R&D on fully depleted CMOS image sensors
  Stefanov et al, Sensors, 18, 118, 2018 (link)

## Slide 63: Summary
The invention of the CCD in 1970 by Boyle and Smith has had enormous impact on society and in scientific applications, particularly astronomy and astrophysics
Clever researchers continue to find new applications, e.g. direct dark matter detection and direct detection of x-rays for light sources
We look forward to innovations from the next generation of instrumentation experts

## Slide 64: Acknowledgements
R. Stover / M. Wei / W. Brown / C. Rockosi
A. Dey / R. Reed
DECam staff
H. Padmore / P. Denes
CCD group leaders – C. Bebek / N. Roe / M. Levi / S. Perlmutter
B. Flaugher / T. Diehl / J. Estrada / D. Kubik / J. Tiffenberg
R. Groulx / R. Frost / F. Dion

## Slide 65: Acknowledgements
Early grant from the NSF
  Award #9876605 (1999 – 2003)
Lawrence Berkeley National Laboratory
  MSL equipment upgrades / LDRD
Other support
  Keck Telescope / USAF / NNSA / NASA
Long term funding from the U.S. Department of Energy for sustained R&D