## Slide 1: Fermilab F1.3-2 (CM02) Beam Valves
Jerry Leibfritz and Tug Arkan

## Slide 2: Issues with Cold Gate Valves
  Both CM02 cold gate valves do not operate properly
    each exhibit different characteristics
    highly suspect they leak through and/or don’t seal properly
  As a result
    Experienced unexpected pressure differentials in various configurations during leak check and installation of CM02 at WS5 and at CMTS, resulting in filtered boiled-off nitrogen gas and cleanroom air being introduced into the cavity string in an uncontrolled manner.

## Slide 3: Upstream Cold Gate Valve
  Upstream Gate Valve (#472XX-XEOX-ALA1/0066)
    excessively rough to operate
    verified valve was fully closed
    able to see vacuum changes through closed valve in configuration shown above, suspected to be leaking through. Not trivial to calculate a reliable leak rate.
Upstream
(Feedcap)
Downstream
(Endcap)
Open
Closed
MFC
MFC
Configuration During WS5 Leak Check

## Slide 4: Downstream Cold Gate Valve
  Downstream Gate Valve (#472XX-XEOX-ALA1/0015)
    excessively easy to operate/turn
    leaked through when expected to be closed in configuration shown above. Not trivial to calculate a reliable leak rate.
    valve is very “touchy” and cannot be relied on to seal properly
Upstream
(Feedcap)
Downstream
(Endcap)
Closed
Open
MFC
PS
Closed
Spool
Configuration During CMTS Installation

## Slide 5: Additional Information
  In all leak checks of full cavity string system, no outside air leaks were detected
  Upstream and downstream right-angle valves (RAV) were leak checked successfully (not leaking through)
  Cavity string experienced pressure changes at uncontrolled rates though CMTS test did not show any excessive FE for this CM:
    F1.3-02: One cavity FE onset 12.5 MV/m; 7 acceptable

## Slide 6: F1.3-02 (CM02) Current Configuration Diagram
Cold GV (closed)
Cold GV
(closed)
Short spool with a mini right angle valve (RAV) (closed)
Cavity String
Downstream
(Endcap)
Upstream
(Feedcap)
Flange adapter with a right angle valve (RAV) (closed)
Cryostat Vessel

## Slide 7: Path forward
Ignore
Dale Gill, vacuum engineer at SLAC requested better assessment of the leak rate for these CGVs:
  Work on CGV and try to assess a better leak rate, this will require opening, closing CGV, pushing through nitrogen or helium through the closed CGVs and disturbing the current vacuum integrity of CM02 beamline
  Risky for the beamline integrity of the tested and qualified CM
Special handling/installation scheme at SLAC: next slide

## Slide 8: Proposed scheme for CM installation at SLAC
F1.3-2 aka CM02 has leaking through gate valves (E-7 mbar x liter / second range) at both UP an DS ends of the CM. (JLab CM02 might have the same issue)
Currently we have Faraday cup manifold (F10040886) assembled to US gate valve (closed) and F10023441 assembled to DS gate valve (closed).
`
F10040886
Fermilab proposes to ship F1.3-2 beamline as-is (under vacuum) with its current end configuration. (will require some additional pumping configurations during final QC after BLA installation
CM(n-1)
CM(n)
CM(n+1)
F1.3-2
Move F1.3-2 to the tunnel & backfill to atmosphere
Ensure both gate valves are closed
Install BLA between F1.3-2 and CM(n-1) and CM(n+1)
Pump & Leak check from each side of F1.3-2 at the same time
One proposed procedure