## Slide 1: HOM Qext tuning update
Anna Solopova for QAQC workshop
25-Jan-18

## Slide 2: Outline
  Introduction
    CM02 and CM03 refresher
  Investigation
  Lessons learned
  CM04 and CM05 results
  Documentation
  Path forward
  Summary

## Slide 3: CM02 Qext
Cavity | QxtFPC | Qprobe | QHOMA | QHOMB
1 | 4.14E+07 | 3.46E+11 | 1.03E+11 | 1.76E+12
2 | 3.94E+07 | 2.86E+11 | 4.81E+11 | 1.03E+11
3 | 4.25E+07 | 3.50E+11 | 1.34E+11 | 2.96E+11
4 | 4.17E+07 | 3.80E+11 | 4.67E+11 | 8.25E+10
5 | 3.99e+07 | 3.70E+11 | 7.16E+10 | 2.35E+11
6 | 4.07E+07 | 3.99E+11 | 6.23E+11 | 2.06E+11
7 | 3.91E+07 | 3.36E+11 | 6.86E+11 | 2.34E+11
8 | 3.96E+07 | 3.03E+11 | 2.19E+13 | 5.05E+11
  Cryo heat loads assumes < 0.5 W per HOM (LCLSII-4.1-PR-0146
  Qext HOM 1 – 5 below spec; Qext HOM 2 – 6 below spec

## Slide 4: CM03 investigation
  Original results on CM03 were also not great
    Five Qext HOM 1 and five Qext HOM 2 below spec
  Collected data using FNAL software
  Cross-checked measurements and calculations
    Same notch frequency results in 102 difference in Qext
    Close Qext have different notch frequency.
    Average frequency shift warm under vacuum 0.8-1MHZ vs ~0.4MHz at Fermi.
  Decided to tune to different frequencies
    HOM 1 to 1296.6MHz
    HOM 2 to 1296.3MHz
QHOM1 CMTF | QHOM2 CMTF
4.1E+12 | 2.9E+11
4.7E+10 | 9.4E+10
4.1E+11 | 4.6E+11
9.0E+10 | 8.5E+10
4.2E+10 | 1.6E+10
3.4E+12 | 1.6E+11
7.8E+10 | 3.5E+11
3.4E+10 | 1.7E+11

## Slide 5: CM03 testing round 2 results
 | Tuned HOM 1 notch | Tuned HOM 2 notch | HOM 1 Cold notch | HOM 2 Cold notch | Notch 1 shift, MHz | Notch 2 shift, MHz | Power HOM 1 | Power HOM 2 | Qext 1 | Qext 2
1 | 1296.8 | 1296.3 | 1299.5 | 1300.5 | 2.7 | 4.2 | 0.2 | 0.9 | 4.90E+12 | 3.50E+11
2 | 1296.5 | 1296.4 | 1304.8 | 1300.8 | 8.3 | 4.4 | 2.1 | 0.8 | 7.50E+10 | 4.70E+11
3 | 1296.5 | 1296.2 | 1300.9 | 1300.2 | 4.4 | 4.0 | 0.6 | 0.3 | 1.70E+12 | 5.30E+12
4 | 1296.4 | 1296.2 | 1303.3 | 1301.3 | 6.9 | 5.1 | 1.2 | 1.3 | 1.90E+11 | 1.50E+11
5 | 1296.4 | 1296.1 | 1304.8 | 1300.9 | 8.4 | 4.8 | 1.3 | 0.9 | 1.50E+11 | 4.70E+11
6 | 1296.8 | 1296.4 | 1300.0 | 1300.4 | 3.2 | 4.0 | 0.2 | 0.5 | 8.00E+12 | 1.50E+12
7 | 1296.4 | 1296.3 | 1300.9 | 1300.6 | 4.5 | 4.3 | 1.5 | 0.5 | 1.30E+11 | 1.84E+11
8 | 1296.7 | 1296.4 | 1300.9 | 1300.9 | 4.2 | 4.5 | 1.2 | 0.8 | 1.70E+11 | 5.10E+11
Better than last time
Notch target appears to be good
HOM tuner side is more stable
Preliminary Results
Measurements taken at ~8 MV/m
No pattern in the notch shift
No obvious reason for a large shift

## Slide 6: Lessons learned and applied to CM04
Studied and applied XFEL HOM tuning technique – iterative tuning.
  Removes mechanical stress from the HOM can end plate and hardens niobium
HOM tune is extremely sensitive to cable motion and external movement like torqueing nuts and bolts
  Must be the absolutely last thing done on the string before installation of a lower magnetic shield
  Leave enough slack on each cable for thermal contraction

## Slide 7: Mu metal magnetic shield interference
Found interference between magnetic shields of the helium vessel and HOM cans
  Multiple dimensions of the dressed cavity and shields are possibly causing unforeseen interferences – currently under investigation for root causes other than installation
  Quick solution in the mean time: trim HOM mag shields.

## Slide 8: CM04 Qext HOM results
Cavity | Tuned HOM 1 notch | Tuned HOM 2 notch | HOM 1 notch after test | HOM 2 notch after test | HOM1 (mW) | HOM2 (mW) | Q_HOM1 | Q_HOM2
1 | 1296.5 | 1296.2 | 1296.4 | 1296.2 | 7.4 | 19 | 3.6E+13 | 1.5E+13
2 | 1296.5 | 1296.2 | 1296.6 | 1296.3 | 41 | 88 | 7.0E+12 | 3.2E+13
3 | 1296.8 | 1296.4 | 1296.8 | 1296.4 | 0.04 | 16 | 4.7E+15 | 1.1E+13
4 | 1296.6 | 1297.3 | 1296.6 | 1297.4 | 1.1 | 646 | 2.5E+14 | 4.2E+11
5 | 1296.6 | 1296.2 | 1296.6 | 1296.6 | 5.6 | 25 | 4.7E+13 | 1.1E+13
6 | 1296.6 | 1296.4 | 1296.6 | 1296.4 | 1.8 | 175 | 1.5E+14 | 1.6E+12
7 | 1296.6 | 1296.4 | 1296.6 | 1296.3 | 8.3 | 35 | 3.2E+13 | 7.7E+12
8 | 1297.1 | 1296.3 | 1297.1 | 1296.3 | 88 | 66 | 3.2E+12 | 4.1E+12
  Almost no frequency shift before and after test.
    Iterative tuning is a success!
  All Qext HOM are above spec, Cavity 4 HOM 2 has an unfixable tight cable
  Cavity 4 HOM 2 was bumped after tuning, power out at ~13.3MeV is 0.97W
Notes: 13.3MeV, limited by FE

## Slide 9: CM05 Qext HOM results
Cavity | Tuned HOM 1 notch | Tuned HOM 2 notch | HOM 1 notch cold | HOM 1 notch cold | HOM1 (mW) | HOM2 (mW) | Q_HOM1 | Q_HOM2
1 | 1296.6 | 1296.3 | 1299.9 | 1300.1 | 0.09 | 0.09 | 4.2E+13 | 4.6E+12
2 | 1296.7 | 1296.3 | 1300.1 | 1300.2 | 0.07 | 0.13 | 5.7E+11 | 1.2E+13
3 | 1296.6 | 1296.3 | 1299.8 | 1300.3 | 0.09 | 0.32 | 2.9E+13 | 2.5E+12
4 | 1296.5 | 1296.3 | 1299.9 | 1300.1 | 0.23 | 0.23 | 3.4E+12 | 1.5E+13
5 | 1296.5 | 1296.3 | 1299.7 | 1300.0 | 0.26 | 0.26 | 5.6E+12 | 1.9E+15
6 | 1296.6 | 1296.3 | 1299.9 | 1300.4 | 0.04 | 0.39 | 5.4E+13 | 2.1E+12
7 | 1296.6 | 1296.3 | 1299.9 | 1300.2 | 0.02 | 0.16 | 3.2E+14 | 8.8E+12
8 | 1296.7 | 1296.4 | 1300.1 | 1300.2 | 0.12 | 0.19 | 2.4E+13 | 6.1E+12
  All Qext HOM exceed spec.
  Notch frequency shift is consistent across all cavities

## Slide 10: Documentation
Procedure and traveler are a work in progress. Draft versions available.

## Slide 11: Path forward
  Rework CM02 and CM03
  Test CM07, revise procedure if needed
    Improving procedure to reduce time required to tune one cavity
  Finalize documentation
  Find a better solution than cutting off magnetic shielding.

## Slide 12: Summary
  Took time to experiment with CM03
    Iterative tuning removes mechanical stress from HOM end plate and hardened the niobium can
    Mag shield interference due to floating cavity dimensions and installation issues of the first couple modules
    Average notch position shift from warm to cold module is larger than at Fermi and different for HOM 1 and 2.
  CM04 meets HOM specs
  CM05 exceeds HOM specs – our best result yet.
  Procedure and traveler are being finalized, drafts available