## Slide 1: High-field, high-repetition rate Dielectric Wakefield Acceleration Experiments
Brendan O’Shea, Gerard Andonian, Sam Barber, Christine Clarke, Phuc Hoang
Mark Hogan, Brian Naranjo, Oliver Williams, James Rosenzweig

## Slide 2: Dielectric Wakefield Acceleration
B. O’Shea, FAST/IOTA Workshop, May 10th 2017
Cerenkov Wakefield Accelerator
GV/m gradients measured at FACET
Source of THz
  High Energy (100 + mJ)
  Narrow bandwidth (<5%)
Cook et al., Phys. Rev. Lett. 103 095033 (2009)

## Slide 3: Experimental Setup @ FACET
B. O’Shea, FAST/IOTA Workshop, May 10th 2017
O’Shea et al., Nat. Commun. 7 (2016)
Parameter | Value
Beam Energy | 20.35 GeV
Charge | 1.1-2.4 nC
Beam Size @ IP | 30x30 μm
β-function | 0.3x3.0 m
Bunch Length | 40 μm

## Slide 4: High Gradient Result
B. O’Shea, FAST/IOTA Workshop, May 10th 2017
Single bunch
Energy change of 200 MeV, in 15 cm.
Measured average decelerating gradient of 1.35 GV/m
Deduced maximum accelerating gradient of 2.8 GV/m
Two bunches
Witness bunch gradient of 320 MV/m
~80% efficiency

## Slide 5: THz generation in DWA
Wakefield is phase locked to the velocity of the beam
The group velocity is a fraction of the speed of light, here 0.31c
At the moment the particle leaves the DWA there is a wakefield of length (1-𝛽g)LDWA
B. O’Shea, FAST/IOTA Workshop, May 10th 2017
Blue is the electron beam
Red is the wakefield
Dashes line the wakefield region determined by the group velocity

## Slide 6: THz generation in DWA
B. O’Shea, FAST/IOTA Workshop, May 10th 2017
No Losses
Losses

## Slide 7: The High gradient CCR Information was interesting…
200 MeV shift -> 640 mJ of energy
Beam run at 10 Hz
Expected a wave train that was
  30 cm
  Was: ~1 cm
B. O’Shea, FAST/IOTA Workshop, May 10th 2017

## Slide 8: High-field induced conductivity in SiO2
B. O’Shea, FAST/IOTA Workshop, May 10th 2017
Low Charge -> 500 MV/m
High Charge -> 1100 MV/m

## Slide 9: Induced Conductivity Quantification and Description
B. O’Shea, FAST/IOTA Workshop, May 10th 2017
Durach et al., PRL 105, 086803 (2010)
Schiffrin et al., Nature 70, 493 (2013)
Strong fields induce band-gap collapse which frees electrons
Strong terahertz fields drive keV electron energies
Collisional ionization ensues, avalanche
Effect reverses on 100s picosecond time scale, no long term damage
Conductivity results in energy absorption - dielectric heating
  Energy conservation suggests ~100 oC increase
Notes: Others have calculated the band gap collapse in SIO2 at ~1 GV/m

## Slide 10: Dielectric Heating
SiO2 melting point: ~ 1710°C
FACET
2.8 GV/m, 10 Hz -> 6.4 W
ΔT = M/(Cp*𝜌*Volume) = 114 °C
FAST
500 MV/m, 1 MHz
ΔT = 352,000 °C
For SiO2 should not exceed ~4 kHz without cooling
B. O’Shea, FAST/IOTA Workshop, May 10th 2017
SiO2 Melting Point - Room Temp

## Slide 11: What can be studied at FAST
Should examine ~4 kHz limit of SiO2
Fabrication of tubes and slabs a known process
Material Science Opportunities
  diamond - smaller band gap and 10% the heat capacity, very good thermal conductivity
  aluminum oxide - large band gap, 10 times larger heat capacity
Exotic structures that have less field in the dielectric
B. O’Shea, FAST/IOTA Workshop, May 10th 2017
Woodpile Structure
Notes: We know the dielectric returns to normal on the scale of milliseconds, but 1 MHz has a spacing of 1 microsecond!
Aluminum oxide appears to have a POWER loss alpha of 10 1/m, so already better than SiO2.

## Slide 12: OLD SLIDES
B. O’Shea, FAST/IOTA Workshop, May 10th 2017