## Slide 1
Yuri Alexahin*, Alex Macridin
Fermilab Workshop on Megawatt Rings
7-8 May 2018
Booster Beam Simulations

## Slide 2: Issues & Goals
stage | E_inj (MeV) | Np/batch (e12) | Qx/Qy
PIP-I | 400 | 4.5 | 0.25/0.31
PIP-I+ | 400 | 5.6 | 0.31/0.38
PIP-II | 800 | 6.5 | (0.36/0.44)*
*) would be with 400MeV injection
Losses at nominal (PIP-I) intensity are ~8%, will increase at high intensity operation (especially with 20Hz reprate)
Simulations goals:
 understand experimental observations
 offer ways of improvement
Tools used:
 Synergia (A. Macridin, E. Stern)
 MADX-SC (Y.A., A. Valishev with a lot of help from F. Schmidt)

## Slide 3: HEP Optics Measurements
Measurements performed by K-modulation definitely confirm HEP Optics model (MADX)

## Slide 4: Optics Perturbation
A number of solutions considered:
 modify the extraction dogleg using pulsed magnets (expensive)
 half-integer resonance correction using quadrupole harmonic circuits
 “flat” optics (Tan)
The source of the optics perturbation is well-known: the extraction dogleg created by DC magnets – the strongest effect @ injection.

## Slide 5: Optics Functions w/o SC
dogleg
dogleg
dogleg
“Pseudo-Flat Optics 2”
“Pseudo-Flat Optics 1”
“HEP Optics”
Fourier Sectra of  -functions
|F()|
n
|F()|
n
|F()|
n
Red: hor
Blue: ver

## Slide 6
Beam parameters (A. Macridin):
N(r.m.s.)=2.34m (N(95%)=14 mmmrad)
z= 0.831532m, p/p= 0.00185,
Longitudinal profile is not Gaussian, corrections were made that reduced space charge tuneshifts to 0.28, 0.38 for Np=7.e10/bunch
Synergia simulations w/o dogleg bump
 still losses due to longitudinal shift in SXL03 position by 4.75m
 excitation of Qx+2Qy=20
 can be compensated by tuning other sextupoles
Tracking Simulations
SXL #
I [A]
real currents (not used in sims)
used for correction of Qx+2Qy in sims

## Slide 7
Synergia Simulations
Qx=0.734,
Qy=0.824
Chr=(-17,-9)
n=7e10 pp bunch
horizontal chromaticity has a large influence on loss
CPL03 and dogs as in Booster
Position of the CPLO3 corrector package is the main culprit for beam loss

## Slide 8: MADX-SC Simulations for HEP Lattice
no Qx+2Qy correction
with Qx+2Qy correction
Losses over 2000 turns as function of bare lattice tunes at nominal Np.
Little improvement at Qx=6.7, Qy=6.8: 4.3%  3.8%
Qy
Loss %%
Qx
Qx
Qy

## Slide 9: MADX-SC Simulations for Flat Lattice 2
Np=5.6e10/bunch
Np= 8.1e10/bunch
Losses over 2000 turns as function of bare lattice tunes at nominal and PIP-II intensities. Qx+2Qy corrected.
At Qx=6.7, Qy=6.8 losses are negligible: 0%  0.07%
Qy
Loss %%
Qx
Qx
Qy

## Slide 10
Pseudo-Flat Optics 2 looks like a victory, but there is no better working point than with HEP lattice at high intensity!
(low intensity)

## Slide 11: Effect of Image Charges*
*) the interest renewed by S. Machida at 2nd SC collaboration meeting (CERN, March 2018)

## Slide 12: Skew Sextupole Studies
Booster measurements show little effect (if any) of SSS located close to F-magnets (K. Seiya)
Losses [%%]
ymax[mm]
Bending magnets have small (half) apertures:
F-magnets h=2.1 cm, L=2.9 m x 48, ks2(image)=0.001m-3 for y=1mm, Np=7.e10  can drive 2Qx+Qy
D-magnets h=2.9 cm  can drive 3Qy
The image charges were simulated as skew sextupoles components in F- and D-magnets ~ y ~ y1/2cos(ns/R) with n=20
MADX-SC simulations show that vertical offset should be ~0.3y to produce a noticeable effect in 2000 turns – too large?

## Slide 13: Summary
 From the standpoint of transverse dynamics with space charge there should be no problem with PIP-II intensity at the present injection energy when using “flat” optics.
 However, we could not reduce losses with these apparently better optics
We tried:
 injection orbit and optics matching
 aperture scans
 decoupling (though Qx+Qy has not been looked at since 2011)
 correction of the 3rd order using upright and skew sextupoles
 reduced chromaticity
 to see head-tail instability
 to detect dipole noise using TBT data
(quad noise seems unlikely)
- all to no or very limited success.
Had we missed anything important?
TBT spectra
V
1 – Q
H

## Slide 14
 Can RF phase errors that C.-Y. Tan and Chandra Bhat are looking at now be the reason for increased losses with improved optics?
Even if so, the explanation must be found – studies necessary.
 Simulations studies ongoing or planned:
- longitudinal dynamics with wakes and SC
- Effects of RF and quadrupole noise
- 6D dynamics during RF capture with 3DoF SC
- coherent (envelope) oscillations with MADX-SC
- …
Outlook