## Slide 1: Investigating Nonlinear Integrable Optics with Space Charge in IOTA Using IMPACT-Z
Chad Mitchell
Lawrence Berkeley National Laboratory
Fermilab Workshop on Megawatt Rings & IOTA/FAST Collaboration Meeting
Fermilab, Batavia, IL
May 7-10, 2018

## Slide 2
Outline
Introduction and single-particle tracking algorithm
Generation of zero-current matched distribution types
Self-consistent symplectic integration with space charge
Beam stability and invariant preservation (ΔQ=-0.03)
- approach to Vlasov near-equilibrium (through turn 700)
- dynamics within a near-equilibrium beam
- long-term stability behavior (through turn 3K)
Conclusions

## Slide 3: A very brief review of single-particle nonlinear integrable optics in IOTA
Dynamics inside the nonlinear magnetic insert:
[1] V. Danilov and S. Nagaitsev, PRAB 13, 084002 (2010)
Dynamics in the arc external to the nonlinear magnetic insert:
βx = βy , D = 0 across the nonlinear drift space
nπ phase advance from nonlinear drift space
exit to nonlinear drift space entrance
drift space for
nonlinear insert
Courant-Snyder transformation, scaling
D&N give in [1] a realizable potential U
such that HN admits a second invariant IN :
Assumed linear with a map RN given by:
Thus, the phase advance must be nπ.
(4x4 identity)
HN, IN are invariant under the one-turn map.
.
first invariant

## Slide 4: Tracking in the nonlinear insert is implemented in IMPACT-Z using a second-order symplectic integrator.
C. E. Mitchell, THPAK035, IPAC 2018 and LBNL Report LBNL-1007217 (2017)
The ideal 2D magnetic field within the nonlinear insert at location s is given by
, where the potentials are given in terms of dimensionless quantities:
using the complex function:
s-Dependent symplectic tracking is performed using:
.
The map for a single numerical step of size h is:
Field lines of the nonlinear insert in the
transverse plane (blue)
τ – dimensionless insert strength
c – transverse scale parameter [m1/2]
Bρ – magnetic rigidity [T-m]
β – betatron amplitude [m]
global error
global error
global error
global error
First invariant
Second invariant
Convergence with stepsize in tracking through the nonlinear insert

## Slide 5
Generation of zero current matched distribution types

## Slide 6: General procedure for the generation of an initial beam distribution matched to the nonlinear lattice
Python script developed by the RadiaSoft team is used for matched KV beam generation - populates uniformly a fixed level set of H.
[1] S. Webb et al, p. 3099, IPAC 2013.
physical phase space variables (x, px, y, py)
Courant-Snyder
transformation
normalized phase space
variables (xN , pxN , yN , pyN)
- Hamiltonian is s-dependent
- distribution varies periodically in s
- parameter ε0 plays the role of emittance
“nonlinear KV distribution” [1]
- Hamiltonian is s-independent
- distribution function is stationary
“nonlinear waterbag distribution”
Nonlinear KV
ε0 = 8 mm-mrad
Nonlinear waterbag
ε0 = 8 mm-mrad
boundary = equipotential curve
of the nonlinear potential

## Slide 7: Generation of matched distribution types with general Hamiltonian dependence
Given a probability density f on the phase space M (of dimension 2N) and a smooth Hamiltonian H, the probability density PH describing the values of H is given by the co-area formula as:
If f is taken to be uniform on the level sets of H, then for some function G, and so:
A numerical procedure for generating the beam is to first sample values of H from PH and then to populate uniformly each level set of H, so the resulting density on the phase space is given by:
where the surface integral on the right is over the 2N-1 dimensional level set of H with value h.
(This integral is defined and finite for almost all values of h.)
This Jacobian factor depends on h.

## Slide 8: Numerical evaluation of the Jacobian factor for the Danilov & Nagaitsev Hamiltonian
The Jacobian κ is evaluated using a numerical Monte Carlo method, as follows:
sample 10M points uniformly within the 2D domain Ah for the value h = ½ (dimensionless)
compute the dimensionless potential value Φ(x,y) at each point (x,y)
compute the histogram of Φ values to produce κΦ PΦ, valid for h ≤ 1/2
compute the cumulative distribution function of Φ to give κ
τ=0.00
τ=0.40
τ=0.45
τ=0.49
Jacobian factor
Dependence on τ
is weak but nonzero.
Almost exactly linear
in h for all τ.
2D area
line integral
Hamiltonian
Jacobian factor

## Slide 9: Definition of a two-parameter family of matched distribution types - smooth (except at the beam edge)
Nonlinear waterbag distribution:
Reduce to traditional waterbag and Gaussian distributions, respectively, when insert is off.
The nonlinear Gaussian reduces to the nonlinear waterbag as Λ goes to zero with the quantity <H> held fixed, and provides the ability to control (matched) halo extent.
Truncated nonlinear Gaussian (thermal) distribution:
temperature parameter
cutoff parameter
as .
as
as
as
Distribution Horizontal Profiles
Λ=0
Λ=1
Λ=3
Λ=5
<H> = 4 mm-mrad
α = 1.4082
β = 1.9065 m
τ = 0.4
c = 0.01 m1/2

## Slide 10: Examples of nonlinear Gaussian (thermal) distributions with cutoffs at Λ = 1, 3, 5 (shown at entrance to NLI)
Distribution parameters are selected to give: with identical Twiss values.
waterbag
distribution
waterbag
waterbag
waterbag

## Slide 11
Self-consistent symplectic integration with space charge

## Slide 12: Theory of a symplectic spectral space charge solver for coasting 2D beams (1)
Collective N-particle Hamiltonian:
Symplectic map for a single step:
single-particle Hamiltonian
w/o space charge (“external”)
2D space charge Green function in a rectangular conducting pipe
x
y
(0,0)
(a , 0)
(0, b.)
J. Qiang, Phys. Rev. ST Accel. Beams 20, 014203 (2017).
generalized perveance
continuum limit
2D Poisson equation

## Slide 13: Theory of a symplectic spectral space charge solver for coasting 2D beams (2)
Spectral approximation of G using Nl , Nm Fourier modes in x and y, respectively:
The symplectic map associated with is given for particle i as:
for mode (l,m):
Computed directly from particle data in the laboratory frame using (★).
Note: Momenta are normalized by the design momentum p0.
(★)
Computational complexity scales as . See also [1] and the talk by N. Cook.
[1] S. Webb, Plasma Phys. Control. Fusion 58, 034007 (2016).

## Slide 14: Benchmark 1: Expansion in free space of a cold uniform cylinder beam (1).
Measures of numerical resolution:
× 2.04
× 2.03
Beam size evolution
Emittance evolution
doubling
distance
Linear drift (kinematic nonlinearities off)
KE = 2.5 MeV p (equal to IOTA benchmark value)
R0 = 3.905 mm (equal to IOTA benchmark value)
I = 4.113 mA (10 × IOTA benchmark value)
a = b = 5 cm (chosen to be >> R0)

## Slide 15: Benchmark 1: Expansion in free space of a cold uniform cylinder beam (2): Hamiltonian preservation
The error in H scales as expected:
Evolution of the N-particle Hamiltonian
Relative change in H × 106
125 SC kicks
250 SC kicks
× 4.00
500 SC kicks
Initial value of H :
Numerical resolution:

## Slide 16: Benchmark 2: A matched waterbag beam in the linear IOTA lattice.
IOTA lattice retuned for space charge
tune depression of ΔQ = -0.03
Nonlinear insert turned OFF (linear lattice)
Final beam phase space
Waterbag beam, 1.024 M particles
I = 0.4113 mA, <H> = 4 mm-mrad
2D symplectic
spectral solver
2D PIC Poisson
solver
mean particle value
mean particle value
Emittance evolution:
Convergence of phase advance across the arc
increasing number of modes
horizontal
vertical
Emittance evolution:
Convergence of phase advance across the arc
increasing number of modes
horizontal
vertical
Relative emittance growth over 1K turns
2D PIC solver
2D Symplectic solver

## Slide 17
Beam stability and invariant preservation

## Slide 18: Tracking in the IOTA Lattice with Space Charge - Assumptions and Simulation Parameters
Objective: To isolate and understand the perturbative effects of space charge on the ideal
integrable single-particle dynamics at moderate space charge tune depression.
Elements external to the nonlinear insert are sliced longitudinally and treated as symplectic
maps alternating with space charge momentum kicks (split-operator approach): linear order.
Space charge is included self-consistently throughout the lattice using the symplectic spectral
solver with a rectangular boundary of large aperture to emulate free-space boundary conditions.
We consider a long, unbunched beam with zero energy spread to remain near the ideal
integrable working point.
Quadrupole settings are retuned to provide nπ phase advance across the arc after including
the linearized space charge fields at the desired value of beam current (A. Romanov, [1]).
Twiss functions with linearized space charge included must be appropriately matched to the
nonlinear insert. See also [2].
[1] A. Romanov et al, THPOA23, NAPAC 2016. [2] C. Hall et al, WEA4CO02, NAPAC 2016.
Insert parameters: τ = 0.4, c = 0.01 m1/2, μ0 = 0.30345, L = 1.8 m
Beam parameters: KE = 2.5 MeV, I = 0.4113 mA, <H> = 4.0 mm-mrad, ΔQx = ΔQx = -0.03
Tune advance footprint for 0.4113 mA
(waterbag beam, <H> = 4 mm-mrad)
SC induced
tune spread
Settings designed for
a space charge tune
depression of -0.03.

## Slide 19: Tracking in the IOTA Lattice with Space Charge – First 700 Turns (1)
Evolution of the standard deviation of the two invariants of single-particle motion for 700 turns.
First invariant
Second invariant
In all cases, <H> = 4 mm-mrad. Growth during the initial period of nonlinear mixing and phase space filamentation (turns 1-100) appears to depend only weakly on the cutoff parameter Λ.
The time scale for this initial mixing decreases with increasing Λ, as larger-amplitude particles in the tail contribute to stronger nonlinear damping.
nonlinear
waterbag (Λ=0)
nonlinear
Gaussian (Λ=3)
nonlinear
Gaussian (Λ=5)
nonlinear
waterbag (Λ=0)
nonlinear
Gaussian (Λ=3)
nonlinear
Gaussian (Λ=5)

## Slide 20: Tracking in the IOTA Lattice with Space Charge – First 700 Turns (2)
Evolution of the horizontal density profile showing stability of low-density tail
Gaussian (Λ=3)
Waterbag (Λ=0)
Gaussian (Λ=5)
initial beam
after 700 turns
initial beam
after 700 turns
initial beam
after 700 turns
All three spatial profiles appear quite stable.
Perhaps a minor change in the curvature of the profile near the outer beam edge in the waterbag case?
1.024 M particles, 64 x 64 spectral modes
480 steps through the nonlinear insert

## Slide 21: Tracking in the IOTA Lattice with Space Charge – First 700 Turns (3)
Evolution of the first invariant (Hamiltonian) profile showing the effects of space charge
Redistribution of the single-particle invariants occurs primarily near the outer beam edge through profile smoothing near the discontinuity at H=Hmax.
Similar behavior is apparent in the evolution of the
profile of the second invariant.
Gaussian (Λ=3)
Waterbag (Λ=0)
Gaussian (Λ=5)
initial beam
after 700 turns
initial beam
after 700 turns
initial beam
after 700 turns

## Slide 22: Dynamics within a near-equilibrium nonlinear waterbag beam – Invariant profiles are well-preserved across the arc
H, I are here expressed
in dimensionless units
Arc entry
Arc exit
Arc entry
Arc exit
Turn 350
Turn 700
First invariant profile
Second invariant profile
Beam distribution is
nearly stationary

## Slide 23: Dynamics within a near-equilibrium nonlinear waterbag beam – Advance of invariant values across the arc
Individual particle changes in H and I are as large as 20%
high
density
high
density
Turn 350
Turn 700
Turn 350
Turn 700
Footprint is
stable over
350 turns

## Slide 24: Smooth focusing waterbag model of equilibrium in the linear IOTA lattice (action advance across the arc)
Turn 350
Turn 700
Distribution in the
change of action
across the arc
1Assuming a stationary waterbag beam with emittance, phase advance, and tune depression used in the IOTA lattice.
stationary
Arc entry
Arc exit
Distribution of
action values
Turn 700
Smooth focusing model1
Linear IOTA lattice
Well-described
by a smooth
focusing model.

## Slide 25: Tracking in the IOTA Lattice with Space Charge – First 3,000 Turns
Long-term tracking over 3,000 turns showing sensitivity of diffusion rates to distribution details.
First invariant
Second invariant
nonlinear
waterbag (Λ=0)
nonlinear
Gaussian (Λ=3)
nonlinear
waterbag (Λ=0)
nonlinear
Gaussian (Λ=3)
In both cases, <H> = 4 mm-mrad. The beams are well-matched in horizontal and vertical rms beam sizes, but the current density differs by >10% at the beam center differences in tune advance for particles in the core. Greater nonlinearity in the space charge fields for the Gaussian
beam does not appear to result in more rapid diffusion in this case.

## Slide 26: Convergence of the Standard Deviation of Single-Particle Invariants with Numerical Resolution of Space Charge
1.4
1.2
Varying Nmode
Np = 1.024 M
Nsteps fixed
Dynamics of initial mixing and phase space
filamentation are well-resolved using ~100K
particles and 16x16 spectral modes.
Rates of diffusion (above) are computed using
linear interpolation of data taken over 200 turns.
Due to particle noise, ~1M particles are
required to begin to approach convergence of
the diffusion rates. This could potentially be
improved using higher-order macroparticle shapes.

## Slide 27: Traditional rms emittance growth and beam size evolution for the nonlinear waterbag beam
Emittance is well-preserved after initial
redistribution due to space charge.
Growth in the outer beam edge at the 10%
level over 3K turns (stable beyond turn 350).
Matched nonlinear waterbag beam
I = 0.4113 mA, <H> = 4.0 mm-mrad τ = 0.4, c = 0.01, μ0 = 0.30345, L = 1.8 m
Change in rms beam size: 3% (0.1 mm)
Change in maximum x-deviation: 11% (1.0 mm)
X and Y are strongly coupled by the nonlinear insert. We show the change in .
Beam size evolution on turn 3K
no losses
σx (turn 3K)
xmax (turn 1)
xmax (turn 3K)
Traditional emittance growth
64x64 modes, 1.024 M particles
rectangular boundary a=b=5 cm

## Slide 28: Conclusions
A family of initial beam distribution types controlled by two parameters <H> (generalized emittance) and Λ (cutoff) allows us to investigate sensitivity to distribution details while remaining matched to the (ideal) nonlinear lattice.
Tracking is performed using a symplectic integrator within the nonlinear magnetic insert, coupled with a symplectic spectral solver for self-consistent space charge tracking to avoid non-Hamiltonian sources of numerical noise. Particle noise has a significant impact on the observed stochatic diffusion. Here 1.024M particles are used.
We focus on isolating the perturbative effects of space charge for moderate tune depression (ΔQ=-0.03).
Initial nonlinear mixing leads to a near-matched equilibrium by turn 350. The largest visible effect is smoothing of the hard outer beam edge. The distribution of invariants is well-preserved both 1) across the nonlinear insert and 2) across the arc. However, the single-particle invariants along each orbit fluctuate significantly (~20%). Nevertheless, the invariants provide a sensitive measure of beam quality.
There remains evidence of slow stochastic diffusion, while both rms beam sizes remain well-controlled. An 11% increase in maximum horizontal particle amplitude is visible, and a larger number of spectral modes may be needed to verify that the space charge fields at the beam edge are well-resolved.
The dynamics appear robust in the presence of nonlinear space charge fields caused by the presence of a matched, low-density tail, which also results in more rapid nonlinear damping.

## Slide 29
Backup material

## Slide 30: Overview of advanced computing/modeling using IMPACT-Z
final longitudinal
phase space
D g
> 100, 000 cores
The IMPACT-Z code & physics model
  s-based symplectic particle tracking using maps
  Poisson solvers for 6 distinct boundary conditions
  standard beamline elements, RF and RW wakefields
  field, misalignment, and rotation errors
  multi-turn tracking with simulation restart
  efficient parallelization, access to NERSC
The IMPACT code suite is used by > 40
institutes worldwide
  successfully applied to both electron & proton
  machines:
    CERN PS2 ring
    LCLS-II linac
  unprecedented resolution: ~2B macroparticles
z (mm)
Collaboration with teams at RadiaSoft and FNAL, who are modeling IOTA using SYNERGIA.

## Slide 31: The IOTA ring : a test bed for strategies designed to mitigate space charge-induced beam halo.
Possible strategies: electron lenses/columns, nonlinear integrable lattices
Nonlinearity tune spread “washes out” coherent space charge instabilities
Integrability ensures orbits are regular and remain bounded (no chaos)
Integrable Optics Test Accelerator (IOTA)
- Novel accelerator physics: strongly nonlinear design
- Experimental test bed for SC mitigation schemes
- Run first with electrons, then low-energy protons
nonlinear magnetic insert
using conventional linear design
using nonlinear integrable design
1S. Webb et al, p. 2961, IPAC 2012
nonlinear decoherence1
halo
Fermilab

## Slide 32: Summary of spatial projections for revised matched distributions in the D&N potential
Nonlinear KV
Nonlinear Waterbag
Nonlinear Gaussian
Potential (dimensionless form)
Waterbag (Λ=0)
Gaussian (Λ=3)
Shown for
τ = 0.4,
<H> = 0.2
(dimensionless)

## Slide 33: Nonlinear Waterbag Beam in the IOTA Lattice – Spatial profiles are well-preserved across the arc
Horizontal profile
Arc entry
Arc exit
Y
Y
Turn 350
Turn 700
Arc entry
Arc exit
X, Y are dimensionless;
singularities located
at (X,Y)=(±1,0)
Vertical profile

## Slide 34: Smooth focusing waterbag model of equilibrium in the linear IOTA lattice
Hamiltonian:
Due to symmetry under rotation, H is integrable with a second invariant given by .
self-consistent
space charge
potential
Distribution function:
Spatial density:
Self-consistent potential:
Generalized space charge perveance:

## Slide 35: Smooth focusing waterbag model of equilibrium in the linear IOTA lattice
Hamiltonian expressed using zero-current action-angle variables:
Input parameters:
rms emittance: εx = 2 mm-mrad
undepressed tune advance A to B: Qx = 5.03
space charge tune depression: ΔQx = -0.03
length of arc A to B: Larc = 38.1682 m
Model parameters:
k0 = 0.828 m-1, k1 = 66.355 m-1
a = 3.817 mm, Hmax = 4.995 mm-mrad
Checks: σx = 3.118 mm, I = 4.85 mA
normalized
coordinates
Larc
insert gap
1.8 m
A
B
Matched to an rms equivalent KV beam.1
Examine the evolution of the zero-current invariants (actions).
1S. M. Lund et al, Phys. Rev. ST – Accel. Beams 12, 114801 (2009)
arc