## Slide 1: A new approach to calculating dynamic friction for magnetized electron coolers – relevance to future IOTA experiments and to EIC designs
Fermilab Workshop on Megawatt Rings & IOTA/FAST Collaboration Meeting
9 May 2018 – Batavia, IL
David Bruhwiler,
Stephen Webb, Dan T. Abell & Yury Eidelman
This work is supported by the US DOE, Office of Science, Office of Nuclear Physics, under Award # DE-SC0015212.

## Slide 2: Motivation – Nuclear Physics
Electron-ion colliders (EIC)
  high priority for the worldwide nuclear physics community
Relativistic, strongly-magnetized electron cooling
  may be essential for EIC, but never demonstrated
eRHIC concept from BNL
JLEIC concept from Jefferson Lab

## Slide 3: Idea for Electron Cooling is 50 Years Old
Budker developed the concept in 1967
  G.I. Budker, At. Energ. 22 (1967), p. 346.
Many low-energy electron cooling systems:
  continuous electron beam is generated
  electrons are nonrelativistic & very cold compared to bunches
  electrons are magnetized with a strong solenoid field
    suppresses transverse temperature & increases friction
Fermilab has shown cooling of relativistic p-bar’s
  S. Nagaitsev et al., PRL 96, 044801 (2006).
  ~5 MeV e-’s (g ~ 9) from a DC source
  The electron beam was not magnetized
Relativistic magnetized cooling not yet demonstrated
  electron cooling at g ~ 100 has not been demonstrated
    a non-magnetized concept was developed for RHIC
    Fedotov et al., Proc. PAC, THPAS092 (2007).

## Slide 4: Risk Reduction is Required for Relativistic Coolers
eRHIC, JLEIC both need cooling at high energy
  100 GeV/n  g ≈ 107  55 MeV bunched electrons, ~1 nC
Electron cooling at g~100 requires different thinking
  friction force scales like 1/g2 (Lorentz contraction, time dilation)
    challenging to achieve the required dynamical friction force
    not all of the processes that reduce the friction force have been quantified in this regime  significant technical risk
  normalized interaction time is reduced to order unity
    t = twpe >> 1 for nonrelativistic coolers
    t = twpe ~ 1 (in the beam frame), for g~100
      violates the assumptions of introductory beam & plasma textbooks
      breaks the intuition developed for non-relativistic coolers
      as a result, the problem requires careful analysis

## Slide 5: Goals
Simulate magnetized friction force
  include all relevant real world effects
    e.g. incoming beam distribution
  include a wide range of parameters
  cannot succeed via brute force
    improved understanding is required
Include key aspects of magnetized e- beam transport
  imperfect magnetization
  space charge
  field errors
from Zhang et al., MEIC design, arXiv (2012)
from Geller & Weisheit, Phys. Plasmas (1977)

## Slide 6: Asymptotic model for cold, strongly magnetized electrons
Ya. S. Derbenev and A.N. Skrinsky, “The Effect of an Accompanying Magnetic Field on Electron Cooling,” Part. Accel. 8 (1978), 235.
Ya. S. Derbenev and A.N. Skrinskii, “Magnetization effects in electron cooling,”
Fiz. Plazmy 4 (1978), p. 492; Sov. J. Plasma Phys. 4 (1978), 273.
I. Meshkov, “Electron Cooling; Status and Perspectives,” Phys. Part. Nucl. 25 (1994), 631.

## Slide 7: Including thermal effects
V.V. Parkhomchuk, “New insights in the theory of electron cooling,” Nucl. Instr. Meth. in Phys. Res. A 441 (2000).
D.V. Pestrikov, (2002), preprint.
Integrating D&S calculation over thermal electron population:
A.V. Fedotov, D.L. Bruhwiler and A.O. Sidorin, “Analysis of the magnetized friction force,” Proc. High Brightness (Tsukuba, 2006).

## Slide 8: VORPAL modeling of binary collisions clarified differences in formulae for magnetized friction
D&S asymptotics are accurate for ideal solenoid, cold electrons – not warm
Parkhomchuk formula often works for typical parameters, but not always
3D quad. of D&S with e- dist. works better (modified rmin, ideal solenoid)
In general, direct simulation is required
A.V. Fedotov, D.L. Bruhwiler,
A.O. Sidorin et al., “Numerical study of the magnetized friction force,” Phys. Rev. ST/AB 9, 074401 (2006).
blue line: Derbenev & Skrinsky
green line: Parkhomchuk
pink circles: VORPAL, cold e-
blue circles: VORPAL, warm e-

## Slide 9: Detailed simulations of magnetized friction:

## Slide 10: Detailed simulations of magnetized friction:
G.I. Bell, D.L. Bruhwiler,
A. Fedotov et al., “Simulating the dynamical friction force on ions due to a brieﬂy co-propagating electron beam,” J. Comp. Phys. 227, 8714 (2008).
A.V. Fedotov, D.L. Bruhwiler,
A.O. Sidorin et al., “Analysis of the magnetized friction force,” Proc. HB2006, WEAY04 (2006).
Parkhomchuk formula (green)
VORPAL/VSim (dots)
VORPAL/VSim results

## Slide 11: JLab EIC Design:
Magnetized Gun
Booster
50 MeV Linac Cryomodule
De-chirper
Chirper
Ion Beam
1 Tesla Cooling Solenoid
Beam dump
Images courtesy of Jefferson Lab.

## Slide 12: Can we quantify the required solenoidal field quality?
No, we cannot
  Parkhomchuk formula provides a parametric knob
  Derbenev and Skrinsky do not offer quantitative guidance
Can we quantify the effects of space charge forces?
  No, we cannot
Can we quantify the effects of non-Gaussian e- beam phase space distributions?
  No, we cannot

## Slide 13: A new dynamical friction calculation is underway…
We follow the approach described by Y. Derbenev
However, we begin from a new starting point
  analytic momentum transfer between ion and magnetized e-
  proceed step by step with calculation
Calculation is defined by the following considerations:
Y. Derbenev, “Theory of Electron Cooling,” arXiv (2017);
https://arxiv.org/abs/1703.09735

## Slide 14: Directly integrate Dpion to obtain friction force?
Straightforward integration includes space charge, etc.
  this approach worked for VORPAL/VSim simulations (w/ effort)
Problematic, so we follow Derbenev et al.

## Slide 15: The required steps are straightforward in principle:
Calculate the perturbed e- velocities
  due to a single ion
  initially, we consider purely longitudinal motion
Obtain time-derivative of perturbed E-field
  via Poisson and continuity equations
Integrate in time to get dE
  initially, this is for only a single value of e- velocity
  it is necessary to integrate over thermal e- velocities
Integrate dE along ion trajectory to obtain <F>
  hence, this is a 2nd-order effect, ~(Ze2)2 xx
Present efforts:
  find best way to integrate <F> over e- distribution functions
  consider transverse ion motion
  numerical approaches, testing, etc.

## Slide 16: Hamiltonian for 2-body magnetized collision:
Resulting equations of motion, in the standard drift-kick symplectic form:
D.L. Bruhwiler and S.D. Webb, “New algorithm for dynamical friction of ions in a magnetized electron beam,” in AIP Conf. Proc. 1812, 050006 (2017); http://aip.scitation.org/doi/abs/10.1063/1.4975867

## Slide 17: Analytic calculation of Dpion (1)

## Slide 18: Analytic calculation of Dpion (2)

## Slide 19: Time-explicit vs analytic shows agreement:
Two small parameters are required:
  Larmor radius must be small compared to impact param.
    averaging
  Kinetic energy must be large compared to max potential energy
    perturbative

## Slide 20: Choice of coordinate system is important:
-

## Slide 21: Integrate twice to obtain friction force:
Let
There is an integrable singularity for cold electrons.
The challenge now is to integrate over thermal velocities

## Slide 22: Long-term goals: Include other effects in Magnus Expansion
Quantitative treatment of space charge & field errors?
  space charge should work
  field errors are more challenging
Requires generalization of Magnus expansion
  we are optimistic this can be done

## Slide 23: Future Electron cooling experiments in IOTA
Could be used to test friction force equations…?
  RadiaSoft is interested to collaborate

## Slide 24
JSPEC on GitHub, https://github.com/zhanghe9704/electroncooling
Primary developer is He Zhang of JLab
A new GUI for JSPEC is under development, as part of the open source cloud computing initiative, Sirepo http://sirepo.com
JSPEC – new software for IBS and e- cooling

## Slide 25: Thank You! Questions?