## Slide 1
Salah Chaurize
Fermilab Workshop on Megawatt Rings & IOTA/FAST Collaboration Meeting
7 May 2018
PIP Booster Upgrades

## Slide 2: PIP Booster upgrades highlights :
The Fermilab Booster has seen over 40yrs of operation and various upgrades along the way. The following are just some but not all systems addressed by PIP.
High Level RF system upgrades
  Anode supply replacement
  BRF cavity refurbishment
  Solid State drive system (removal of cascode tubes)
  Cavity 21 and 22 installed
Digital Longitudinal Damper System
  Brings better mode damping diagnostics and control, modern components.
TLM Loss monitoring and safety system integration
  Robust complete ring coverage, less maintenance, lower part count and cost.

## Slide 3: PIP Booster upgrades highlights :
The Fermilab Booster has seen over 40yrs. of operation and various upgrades along the way. The following are just some but not all systems addressed by PIP.
Magnetic Beam cogging
  Dipole Magnet based beam position control, lower energy notch time
New Magnets Kicker systems cooling improvements
  Enhanced cooling and temperature management
  New short kicker system for notching
Aperture enhancements
  Aperture scans and magnet moves open aperture
Horizontal beam notching
  New kicker system, Dedicated Notch Absorber

## Slide 4: BRF Anode Supply and Transformer Upgrade
New anode supplies and transformer replaces 40+ years old system
New wiring also pulled to RF stations from this new anode supply.

## Slide 5: New BRF Anode Supply Diode bridges and cap banks
BRF Anode Supply and Transformer Upgrade

## Slide 6
Booster – Cavity 21 & 22 installed at Long 20 Region
Solid state driver in gallery connects to PA amp in tunnel. Improved PA lifetimes and reliability.
Refurbished Cavity and tuner assemblies.

## Slide 7: BRF Stations 21 and 22 RF Room
Gallery space repurposed for the addition of 2 RF stations.
RF Modulators, Bias Supplies and Solid State Driver racks

## Slide 8: BRF Cavity and Tuner Refurbishment
Obvious and hidden problems were found and fixed during the
refurbishment process. This allowed reliable operation at 15Hz
K. Gollwitzer

## Slide 9: Longitudinal Digital Damper System
10 MHz
N. Eddy

## Slide 10: Longitudinal Digital Damper Diagnostics
Error signals for various modes
See changes in mode error amplitude

## Slide 11: Longitudinal Digital Damper Controls
Turn mode damping ON/Off
Control based per beam cycle
Control Phase and amplitude via tunable curves

## Slide 12: Digital Longitudinal Damper System
Beam measurements in the MI-8 line which show amplitude and phase of extracted Booster bunches.
With the new digital dampers working – phase errors look excellent and should help reduce loses in downstream machines.
Phase error
Bunch Phase
Bunches
Bunches
16
-16

## Slide 13: Motivation for TLM:
Large numbers of additional interlocked detectors (chipmunks) would be required for some installations, e.g.,
  Muon campus (42->200 - mu2e experiment)
  Booster (48->? – PIP/PIP-II)
AD received encouragement from the Fermilab ESH&Q Section in May 2011 to pursue development of a long detector system
A. Leveling
Booster TLM System

## Slide 14
A. Leveling
Good correlation between TLM and chipmunk

## Slide 15: TLM system diagram
A. Leveling
Detector works in ion chamber mode
  800 volt detector bias
Argon/CO2 detector gas
  Nominally 25 cc/min
Electrometer output is calibrated in units of nC/TTL pulse
Heartbeat provided by 10 Tohm resistor (83 pA = 5 nC/min)

## Slide 16: Booster TLM Tunnel Layout

## Slide 17: Development of New Cogging System (Magnetic Cogging)
Gap
for the extraction kicker
h=588
h=84
Notch(extraction kicker gap) – Booster extraction kicker –MI/RR injection kicker
Notch has to be created at LOW energy
Main Injector / Recycler
81 bunches + 3 empty buckets
Notch
81 bunches
+ 3 empty bkts
capture with
37MHz RF
 84 bunches
1 Booster revolution
Injection
200MHz
Longitudinal profile monitor
@ Booster injection
Time
K. Seiya (Fermilab Booster)

## Slide 18: Magnetic Cogging using 48 new dipole corrector magnets
Fixed with RPOS feedback
Keeps beam on central orbit and preserves aperture.
Create notch anytime after injection( sync/w LINAC notch)
 reduce beam power loss by 40%.
Path length (radial position) of the beam
Magnetic Cogging
RF Cogging
K. Seiya (Fermilab Booster)

## Slide 19: Notch Beam energy reduced from 700MeV to 400MeV
Reduced beam energy loss at the Notch creation by 40 % and the total cycle loss by 15%.
700MeV
400MeV
Previous system
Notch at 700 MeV
New cogging system
Notch at 400 MeV
K. Seiya (Fermilab Booster)

## Slide 20: Kicker systems improvements
8-15 ns difference between ANU pulser and
Operational Booster pulser(Slower)
C. Jensen

## Slide 21: New Booster Notching Kicker System
Click to add caption text [16pt Bold]
C. Jensen

## Slide 22: New short notching magnets
Standard 1.1m extraction style long kicker
Half meter short notching kickers
Fit on same beam tube footprint and base plate as long kicker

## Slide 23
Enhanced Cooling for Extraction kicker
RCC Chassis for cooler running at 15Hz
To allow cooling overhead.
15Hz
20Hz

## Slide 24
Before Move4
After Move4
+/-0.8mm
Horizontal
Vertical
Orbit difference between before and after Move4
+/-0.6mm
K. Seiya (Fermilab Booster)
Aperture scan and magnet move

## Slide 25
Long
Short
Collimators
Collimators
Vertical aperture (90%) before and after alignment

## Slide 26: Horizontal Plane Beam Notching
Faster Short notching Magnets

## Slide 27: Horizontal Plane Beam Notching
[mm]
K. Seiya (Fermilab Booster)
Simulated and measured beam orbit of notched bunches
V. Sidorov (absorber design)

## Slide 28
Two Notches in the pulse train
First notch is laser only
Second is laser + Booster Notcher
Booster Notch loss profile
Laser Off (Red – higher loss)
Initial Linac Laser Notching
One Revolution 2.2 usec

## Slide 29: Horizontal Plane Beam Notching
Notch Absorber
Simulation December, 2011 I.Tropin
V. Sidorov (absorber design)

## Slide 30: Horizontal Plane Beam Notching

## Slide 31: Summary of Booster upgrades
Improvements are incremental and build on one another.
Multi-faceted approach provided success based on a system wide understanding vulnerabilities.
Stagger resources over time to allow measurable improvements. Bring new systems on-line incrementally allowing less downtime with phased improvements.
Other upgrades and efforts not mentioned also contributed to reaching PIP goal of 2.4E17 p/hr.
Many people and groups where indispensable to the success of PIP.