## Slide 1
David Johnson, Todd Johnson, David Slimmer, Kevin Duel, Pat Karns, Brian Schupbach, Kiyomi Seiya, Salah Chaurize, Chandra Bhat, Bill Pellico
Fermilab Workshop on Megawatt Rings & IOTA/FAST Collaboration Meeting
7 May 2018
Fermilab Linac Laser Notcher: Motivation, Method, and First Operational Experience

## Slide 2: Acknowledgements
Bob Zwaska
Fernanda Garcia
Bill Pellico
Matt Gardner
Chandra Bhat
Pat Karns
Brian Schupbach
Dan Bollinger
Drew Feld
Ben Ogert
Jason Kubinski
Justin Briney
Jeff Larson
Fred Mach
Katrina Hunden
Mike Kucera
Bobby Santucci
Tom Boes
Jinhao Ruan
Jamie Santucci
Andrea Saewert
Vic Scarpine
Randy Keup
Alex Lumpkin
Matt Quinn & Dave Baird (LSO)
ES&H Interlock Group
Alignment crew
KV Reddy & Sreenivas Patel of PriTel
Don Sipes & Jason Tafoya of Optical Engines
Jay Doster & Dennis Lockwood Grumman
Plus many others

## Slide 3: Motivation
Proton Improvement Plan Intensity Goals
  Ultimate goal: 2.3E17 protons delivered/hr @ 15 HZ
  >85% acceleration availability
Booster runs at Administrative loss limit
Notching in the Booster ring deposits the removed bunches into dedicated Absorbers. This accounts for ~30% of Booster beam power loss ( few % of beam intensity).
We would like to remove this loss from the ring and safely dispose of the notched ions.
Ultimately one needs about 80 ns notch in the beam at extraction time for the extraction kicker rise time and the 8 GeV Recycler injection kicker
In the 200 MHz beam structure this would correspond to ~16 200 MHz bunches every 2.2 us and for 16 turns this would be a total of about 256 bunches or about 1-2% of injected beam.
  When we started in 2011, it was 10-12 bunches and 10 turns
  Now, we’re at 16 bunches and 16 to 18 turns and there’s talk of more…
Techniques developed here may be applicable in other projects such as laser stripping, laser chopping, laser collimation

## Slide 4: Laser Notching of Linac H- at Fermilab
In 2001, Ray Tomlin reported on a successful experiment to create notches in the CW linac beam in the H- 750 keV beam line and have this notch survive at Booster injection.
He created a 25 ns notch utilizing a 200 mJ 5 ns laser pulse.
To create multiple notches in the linac pulse he
proposed a
  “4 pass bow-tie cavity some 665 meters
  long (with a storage time of 2.22 ms)”. Large Pockels
  cells would shuttle the laser to and from the delay line.
A disk gain section would restore optical losses.
Average laser pulse energy of 103 mJ
Peak power of ~20 MW to strip 99.9% of the ions.
This was not implemented.
First Laser Notching Experiment

## Slide 5: A Little Background: The Proton Source
RFQ
MEBT
Linac
201.25 MHz
750 keV
400 MeV
Ion
Source
FRF (injection) 38 MHz
tREV ~ 2.21 ms
Booster
8 GeV
Notch created in Booster @ 400 MeV
Move this process out of the Booster tunnel
Laser
Notcher
 Create Notch in linac at 750 keV
~35.5 us (~ 16 Booster turns)
LINAC PULSE
Loss from Booster Notcher
-> 30% total power loss

## Slide 6: Technique: Photoneutralization
H-
1 micron laser- near peak of cross section
1 J
Want to make process efficient
Match laser pulses to bunch parameters
Non-resonant optical cavity (we call a zig-zag cavity)
43 mJ/bunch
~0.5J/notch
2 mJ/pulse
32 mJ/notch
Need to develop 2 components: interaction cavity & laser system
-> minimize required laser pulse energy/average power
Notes: When the neutralization probability does not depend on the electron intensity
The fraction of neutralized ions is given by… where….
Select 1 micron
3) Laser flux -> reduce area and size
cross section -> constant
interaction time -> maximize
If we create a single laser pulse for each notch (SINGLE PASS …show plot 4)
Rather than a sledge hammer, Create a scalpel. tailor the laser to the bunch…5)
6) To further reduce pulse intensity increase time by increasing the number of interactions -- zig-zag cavity
Ultimately, 2mJ /bunch-> 32 mJ/notch

## Slide 7: New 750 keV RFQ Injection Line (RIL)
Must fit in this space

## Slide 8: Optical Cavity Test -- Demonstration Experiment (January 2015)
Use zig-zag Optical Cavity with Q-switch laser
Quantel 100 mJ Q-switch laser

## Slide 9: Change number of bounces by adjusting input angle into cavity
Use a video camera looking at the back of the frosted fixed mirror to look at the leakage through the mirror

## Slide 10: Operational Laser System Block diagram
Pulsed fiber Amp
1st DPSS
2nd DPSS
Dump
Integrating spheres
photodiode

## Slide 11: Operational Laser System Installed in Linac
RFQ
Buncher
Quad doublet
Interaction Cavity
Transport
Dump

## Slide 12: Controls
Laser seed
Intensity Modulator
MWave Booster fiber Amp
PriTel Pre-amp
PriTel Power amp
Optical Engines fiber amp
TDK Lambda RBA
TDK Lambda REA
Chiller
RBA e-Drive
REA e-Drive
Ophir Energy Meter
Piezo-electric mirror mounts
Video cameras
USB Hub
Local Computer
Front End
NI DAQ
80 analog channels
24 digital I/O channels
Photodiodes
Optical BPM’s
Temperature sensors
Digital control
Digital status
ACNET
USER Interface
Parameter page
Web Monitor
Alarms
Logging
Scope/Camera
TV Channels
UPS

## Slide 13: Controls: LabView Front-end
Flexible que driven state machine
GUI interface, ACNET communication, hardware monitoring, and state machine – ALL INDEPENDENT tasks
Real time configurable alarms
Robust setting, monitoring(configuration and communication) display and logging
  Configurable mail reports
Settable range constraints for all control inputs
Very flexible waveform creation
Main Operations interface through ACNET parameter page and JAVA web monitor page

## Slide 14: Waveform Generation 1
Waveform creation very flexible.

## Slide 15: Waveform Generation 2

## Slide 16: Laser System Monitor

## Slide 17: Operational ACNET Interface
Use inconjunction with monitor page and

## Slide 18: WCM & Output Photodiode from Scope in Pre-Acc

## Slide 19: Output Photodiode response

## Slide 20: Linac Wall Current Monitor

## Slide 21: Preliminary bunch and notch neutralization

## Slide 22: Booster Wall current monitor
80ns notch
200 MHz bunches
80ns notch
38 MHz bunches

## Slide 23: Notch survival in Booster
End of injection
acceleration
200 MHz bunch
38 MHz bunch

## Slide 24: What is the impact on the program (1)
PIP design goal
Laser Notcher installed
We can provide MORE beam !
Increase Acceleration Efficiency !
Laser Notcher installed

## Slide 25: What is the impact on the program (2)
Laser off
Laser on
Absorber for
Booster notching
Collimators
Extraction
Injection
4.5E12 p/pulse
2.2E17 p/hr up to 2.4E17/hr
Administrative Limit
Lower losses !

## Slide 26: What is the impact on the program (3)
More Beam to experiments and lower extraction losses !

## Slide 27: Current Activities and Issues
Operations
  Working on improving the laser and ion beam diagnostics
  Reducing the impact of electrical noise in communication system
  Improving the Operational interface with the MCR and learning how to monitor operate the system
  Flattening the laser pulse energy
Puzzles
  Understanding the laser energy loss from the output of last amplifier to the laser dump (some of the 99.9% reflective mirrors appear to have 6-10% loss)
  Understanding the damage to the optical cavity mirrors

## Slide 28: Optical Cavity Mirror Damage

## Slide 29: Optical Cavity Mirror Damage
Add mask

## Slide 30: Damage after mask

## Slide 31: Development going forward
The Laser Notcher laser system is a burst-mode, bunch-by-bunch, H- neutralization system that can be tailored for many application.
The final amplifier stage of the laser system was developed specific ion bunch structure which has limitations on average power/duty factor.
Many of the suggested applications require a system capable of higher duty factor and average power
  Transverse collimation in one or two planes (in combination with notching)
  Creation of four beam sections in Booster for the g-2 experiment
  Longitudinal collimation in a linac where the head and/or tail of a bunch is removed
  Extinction measurement for the PIP-II mu2e experiment
  Cleaning the 900 ns no-beam section in the PIP-II mu2e experiment
  As a potential component for J-PARC laser stripping experiment
Each may require a potential different final amplification stage, but can use the infrastructure and technology for the laser notcher.

## Slide 32: Adjusted our transverse laser profile and collimated the H- in vertical

## Slide 33: Near term
Current waveform generator has single table for all resets.
  Create an array of waveform generators to be triggered by different beam cycles

## Slide 34: Examples of PCF Amplifiers
Version built for MIT runs at ~1 mJ/pulse (3-4 ns)
300 kW peak power 200W average power sustained

## Slide 35: Longitudinal collimation
pw
ps
prfmicro
pw = 100 ps each
pE = 15 uJ each
ps = 2 ns
prf = 201.25 MHz
DF = 0.016
w = 50 us
prf = 15 Hz
DF = 7.5E-4
Laser produces 201.25E6*50e-6 = 10,000 pulses /cycle
For 30 uJ/pulse*10,000 pulses = 0.3 J /pulse
Peak Power = E/pulse/pulse width
=30 uJ/0.1 ns = 300 kW
Average power = Peak power*DF
= 300 kW* 3E-5 = 9W
Linac
Split amplified pulse OPTICAL delay line  recombine
temporally with adjustable spacing (ps)
Create head/tail out of single amplified laser pulse
Spot size 1mm x 7.5mm
50 passes, 0.59 mm separation, 1.19mm at mirror
cavity length 2.9 cm, laser path 0.73 m,
neutralization 96% with 15 uJ pulse
w
prfMACRO

## Slide 36: Longitudinal collimation
pw
ps
prfmicro
w
prfMACRO
pw = 100 ps
ps = 1 ns
prf = 162.5 MHz
DF = 0.016
w = 500 us
prf = 15 Hz
DF = 7.5E-3
Peak Power = E/pulse/pulse width
=10 uJ/0.1 ns = 100 kW
Average power = Peak power*DF
= 100 kW* 1E-4 = 10W
PIP-II Momentum collimation
Split amplified pulse delay line  recombine
temporally with adjustable spacing (ps)
Create head/tail out of single amplified laser pulse
Spot size 1mm x 1.6mm
100 passes, 1.1 mm separation, cavity length 10.9 cm
Laser path 1.6m, neutralization 99.7% with 5 uJ pulse

## Slide 37: Summary
We have developed a prototype burst mode bunch-by bunch neutralization laser system.
This prototype system is now operational (since end of January)
  Has allowed for a ~30% increase beam delivered to BMB
  Reduced extraction losses and losses in the Booster notcher absorber
  Increased acceleration efficiency
  Booster running at record throughput
We are learning how to operate the system and working on optimization
We continue development to move toward a laser system capable of higher average power capable of additional applications
We want to thank all those whom have supported and contributed to the development and installation of the Laser Notcher… it really does take a village !

## Slide 38
Thank you for your attention
Questions ?