## Slide 1
Alexander Valishev
IOTA/FAST Collaboration Meeting
9 May 2018
Status of Integrable Optics Test Accelerator

## Slide 2: Acknowledgments
R.Andrews, D.Barak, V.Bocean, D.Broemmelsiek, A.Burov, K.Carlson, D.Crawford, A.Didenko, N.Eddy, D.Edstrom, J.Eldred, R.Espinoza, D.Franck, J.Jarvis, V.Kashikhin, R.Kellett, M.Kucera, V.Lebedev, J.Leibfritz, C.Jensen, W.Johnson, P.Li, M.McGee, S.Nagaitsev, L.Nobrega, M.Obrycki, H.Piekarz, E.Prebys, I.Rakhno, A.Romanov, J.Ruan, J.Santucci, V.Shiltsev, G.Stancari, A.Valishev, J.VanBogaert, A.Warner, S.Wesseln(FNAL)
M.Andorff, S.Chattopadhyay, P.Piot, S.Szustkowski (NIU)
D.Shatilov (BINP)
S.Antipov, N.Kuklev (U of Chicago)
D.Abell, D.Bruhwiler, N.Cook, C.Hall, S.Webb (RadiaSoft)
C.Mitchell (LBNL)
R.Agustsson, A.Murokh, F.O’Shea (RadiaBeam)
H.Baumgartner, R.Kishek, K.Ruisard (UMD)

## Slide 3
IOTA Design

## Slide 4: IOTA Design Criteria – AAA
Adaptable
  Can operate with either electrons or protons
  Large aperture
  Easily reconfigurable – quick-change experimental equipment
  Significant flexibility of the lattice
Accurate
  Precise control of the optics quality and stability
  Comprehensive set of precision instrumentation
  Set up for very high intensity operation (with protons)
Affordable
  Cost-effective solution, re-use existing parts whenever possible
  Mostly based on conventional technology (magnets, RF)
  Balance between low energy (low cost) and research potential

## Slide 5: IOTA Parameters
Nominal kinetic energy | e-: 150 MeV, p+: 2.5 MeV
Nominal intensity | e-: 1×109, p+: 1×1011
Circumference | 40 m
Bending dipole field | 0.7 T
Beam pipe aperture | 50 mm dia.
Maximum b-function (x,y) | 12, 5 m
Momentum compaction | -0.02 ÷ 0.1
Betatron tune (integer) | 3 ÷ 5
Betatron tune chromaticity | -15 ÷ 0
Transverse emittance r.m.s. | e-: 0.04 mm, p+: 2mm
SR damping time | 0.6s (5×106 turns)
RF V,f,q | e-: 1 kV, 30 MHz, 4
Synchrotron tune | e-: 2×10-4 ÷ 5×10-4
Bunch length, momentum spread | e-: 12 cm, 1.4×10-4
Beam lifetime | e-: 1 hour, p+: 1 min

## Slide 6: IOTA Layout
E-Lens
RF
Octupoles
NL Magnet
Lambertson
Kickers
injected beam

## Slide 7: IOTA Layout in the Tunnel
e- beam line
2.5 MeV RFQ
p beam line
22 m

## Slide 8: IOTA Layout - Elements
2
8
39
8
1
18
8
2
1
1
21
8

## Slide 9: IOTA Lattice – 2NL Option

## Slide 10
IOTA Components

## Slide 11: Main Dipole Magnets – 30-deg and 60-deg
Conventional C-shape, 0.7T, 520A, water-cooled magnet
  Simple to design and fabricate
Comprehensive 3D field optimization
  Large pole gap (59+mm) to pole width (200 mm) ratio
  10-3 field integral uniformity within the 48mm beam pipe aperture
  Designed by subcontractor (BINP, Novosibirsk), verified at FNAL
10 magnets (8+2 spares) built at IHEP Beijing
  Required minor corrections to pole geometry
  Tested/measured at Fermilab

## Slide 12: Main Quadrupoles – 39 magnets in initial lattice
30 old ASQA type
Built in 1990s for AmPS
Refurbished and tested at Fermilab
9 new FNM type
Designed, built and tested by RadiaBeam

## Slide 13: Combined H/V and Skew-Quadrupole Correctors
For high flexibility of the lattice needed 18 correctors
  H steering
  V steering
  Skew-quadrupole
Due to lack of real estate combined 3 functions in one device
  Simple frame magnet with carefully optimized coil shape
  4 individually powered coils
    Corresponding number of power supplies inherited from ECool
  Fermilab 2D concept
  3D design, fabrication and testing by RadiaBeam

## Slide 14: Combined H/V and Skew-Quadrupole Correctors

## Slide 15: Injection Devices – Lambertson
Lambertson septum magnet
  30-degree horizontal bend and 1.2-degree vertical angle
  DC, powered in series with main bending magnets
  Designed and fabricated at Fermilab
Circulating beam
Injected beam

## Slide 16: Injection Devices – Stripline Kicker
Vertical kicker for injection – 1m long, 50kV plate-to-plate
Horizontal kicker for experiments – 55cm long, 50kV
40 mm gap
50𝛀 impedance
Designed and fabricated at Fermilab

## Slide 17: Vacuum System Designed for 10-10 Torr
Vacuum pipe is 2” diameter stainless steel tube (35 m)
Aluminum chambers in dipole magnets (5 m)
  Silver-plated to avoid ion accumulation
Baking system up to 100÷150C
45 L/s NEG combination pumps every 2 m

## Slide 18: Magnet Power Supplies
Main dipoles – powered in series with Lambertson
  PS reused from Tevatron
  Unipolar, 10-4 stability, 600A, 240kW
Quadrupoles – each magnet individually powered
  New acquisition
  Unipolar, 10-4 stability, 3 types
    400A/10V, 4kW
    120A/12.5V, 1.5kW
    70A/12V, 850W
Correctors/special magnets
  Reused from Tevatron ECool
  Bipolar, 2A, 15V

## Slide 19: Kicker Power Supplies
Reused Tevatron pulse generators
Modified for short pulse (<100 ns) operation
Two systems each with one controls rack, resonant charger, and positive and negative pulsers
Tested successfully to just over 50 kV (25 kV load voltage) into resistive load
Regulate well at 18-50 kV (0.3% rms pulse stability)
Jitter < 0.5 ns

## Slide 20: RF System
Low particle energy and low frequency → very simple requirements
  Electrons: 1 kV, 30.02 MHz (4 × 7.506 MHz)
  Protons: 0.4 kV, 2.184 MHz (4 × 0.546 MHz)
Both gaps implemented in a single device
Cavity shell and ferrite rings reused from pbar source
Off-the-shelf solid-state amplifier
Frequency/Resonance control with capacitor/stepper motor

## Slide 21: RF System

## Slide 22: Instrumentation – BPM System
21 Capacitive button-type H/V pickups (4+ /betatron period)
  50 mm diameter
  already used in FAST linac
Fermilab-designed BPM electronics
  Turn-by-turn capability all BPMs (100 um resolution, 32k turns)
  Closed orbit mode (1 um resolution)

## Slide 23: Instrumentation – Synchrotron Light Monitors
SR from IOTA bending magnet
Beam: E=150 MeV, I=1.2 mA (109 e-)
l=550±20 nm
photons / turn = 2.6×105
photons / s = 1.97×1012
Monitor
BlackFly 23S6M monochromatic camera: 2.3 MP, 5.86 μm pixel size, 41FPS, 71 dB dynamic range
7 um resolution

## Slide 24: Instrumentation – Synchrotron Light Monitors

## Slide 25: Synchronization System

## Slide 26: Other Systems
Beam current measurement
  Wall current monitor
  DCCT
  SR/PMT
Machine Protection System
Stripline kickers
  Switch
  Low-amplitude kicker pulse generators
  Damper (anti-damper)
Sextupole magnets
Water cooling

## Slide 27
IOTA Construction

## Slide 28: IOTA Last Year – June 2017

## Slide 29: IOTA Today – May 4, 2018

## Slide 30: Lessons from FAST 300MeV Construction/Startup
Major engineering project
  Mechanical construction
  Vacuum component cleaning/certification UHV, particle free
  Installation/commissioning of power supplies and instrumentation
  Shielding Assessment: modeling and simulations, review
Took longer than originally projected (2017 June⟹Sept.)
  Longest delay – Shielding Assessment review
    Lesson learned, IOTA SA done early!!!
  Failures of the aging cryogenic system before/during startup
    Installed new booster pump
    Excellent support by Technical Division Cryo, but system needs investments in the long term
  Failure of the gun laser
    New amplifier, different vendor

## Slide 31: FAST 300 MeV Line Construction – Schedule

## Slide 32: IOTA Construction – Shedule (1)

## Slide 33: IOTA Construction – Shedule (2)

## Slide 34: IOTA Construction – Shedule (3)

## Slide 35: IOTA Construction – Shedule (4)

## Slide 36
IOTA Commissioning

## Slide 37: IOTA Commissioning Plan (1)
Injection device tuning (1 week).
  Lambertson septum tuning to observe beam on first BPM.
  Kicker timing to send beam directly though injection straight (using synchrotron radiation diagnostics in the first dipole magnet).
First turn (1 week).
  Match main bus current to beam energy (using synchrotron radiation diagnostics).
  Synchronize BPM electronics with beam signal.
Beam Circulation (1 week).
  Starting with ‘soft’ betatron lattice away from major resonances.
    Start with uncompensated chromaticity.
    Gradually increase number of turns.
    Main goal to establish closed orbit and stable betatron tunes. Expect fast convergence due to well-characterized magnets.
  Turn on RF and scan cavity phase to synchronize injected beam with bucket.

## Slide 38: IOTA Commissioning Plan (2)
Machine Tuning (2 weeks).
  Tune-up of synchroton light diagnostics system (CCD cameras).
  Stable lattice with LOCO.
  Aperture scans with local orbit bumps to establish ‘golden’ orbit.
  Scrubbing run at maximum current to achieve maximum beam life time.
Transition to Experimental Operation (1 week).
  Commissioning of synchronized turn-by-turn BPM operation, data collection.
  Calibration of small-amplitude kicks on circulating beam.
Total: 6 weeks
  Anticipate the schedule may stretch by up to 2 weeks due to tunnel access and downtime

## Slide 39
A few words about injectors

## Slide 40: FAST Electron Linac = IOTA e- Injector
Low Energy (preinjector) part - 20 m
High Energy part - 100 m
Bunch charge | up to 2 nC
Gun gradient | 45 MV/m
CC1 gradient | 26 MV/m
CC2 gradient | 15 MV/m
CM2 gradient | up to 31.5 MV/m
Beam energy | 150 (up to 300) MeV
Bunch length | 6-8 ps (rms)
Pulse length | 1 ms
Bunch freq. | 3 MHz
Rep. rate | 1 Hz (5 Hz)

## Slide 41: 2 Months of FAST Linac Operations in 2017
Primary goal – IOTA injector commissioning
  Acceleration in CM-2 to 150MeV
  Instrumentation
  Machine Protection System
  Machine stability and reproducibility
  Beam line tuning for injection to IOTA
Achievement of 300 MeV beam in SRF linac
  Conditioning and phasing of cavities
  Low-Level RF tuning
Parasitically – collaboration-driven experimental program
Overal uptime 85.6%
normalized to planned hours
of operation (2 shifts/day)
Downtime contributions

## Slide 42: FAST Linac Tuning for IOTA Injection
Use quadrupole scan to measure initial conditions
Setup lattice for actual initial conditions
Find actual focusing fields of the machine by measuring trajectory responses to dipole correctors
Correct lattice
Repeat correction several times
Demonstrated stable beam with phase space suitable for injection to IOTA – injector commissioned!
Fit model to measurements
Implement correction

## Slide 43: IOTA Proton Injector – Status of Ion Source/LEBT
Ion source (formerly HINS) recommissioned in situ at MDB.
  HV Cabinet Rebuilt in 2017
Source Parameters:
  Max Energy: 50 kV (design)
  Max Current: 10 mA (nominal*)
  LEBT Optimized for 20 kV
Fabricated/Swapped Filament
  With Bell-Jar station at ESB
Faraday Cup Response
Filament Activation

## Slide 44: IOTA Proton Injector – Further Steps*
Initial 50 kV commissioning resulted in an event, requiring cleaning
  Funding is expected to return shortly to pursue this
Immediate steps: 50 kV Commissioning
  Clean the source and update drawings
  Refine filament production procedure
  Optimize source output for 50 kV
Short Term: LEBT Build-out
  Spectrometer Magnet → Species separation/optimization
  Allison Scanner → Emittance measurements
  Wire Scanner → Species identification and beam profiles
Longer Term: 325 MHz HLRF system development at FAST
  The RFQ will accelerate H+ beam to 2.5 MeV from LEBT
  A buncher cavity requires characterization/integration w/ IOTA RF
Filament Activation in ESB Bell-Jar
* Currently on hold

## Slide 45
IOTA Research

## Slide 46: IOTA Research
Nonlinear Integrable Optics – Experimental demonstration of NIO lattice in a practical accelerator
Space Charge Compensation – Suppression of SC-related effects in high intensity circular accelerators
  Nonlinear Integrable Optics
  Electron lenses
  Electron columns
  Circular betatron modes
Optical Stochastic Cooling – Proof-of-principle
Electron Cooling – Advanced techniques

## Slide 47: IOTA Staging
Phase I with electron beam will concentrate on the academic aspect of single-particle motion stability using e- beams
  Demonstrate large amplitude-dependent detuning
  Machine tuning must be at the state of the art level to satisfy integrable optics requirements
  e- beams best for the purpose
Phase II – After commissioning with e-, we will move the existing 2.5 MeV proton/H- RFQ to FAST to inject protons into the IOTA ring
  Opens the way for intense-beam studies

## Slide 48: Experimental Procedure
Two kickers, horizontal and vertical, place particles at arbitrary points in phase space
Measure beam position on every
turn to create a Poincare map
As electrons lose energy due to synchrotron radiation, they will cover all available phase space
Can control the strength on the nonlinearity
Final goal – measure dependence of betatron frequency on amplitude
Ideal system
Stable for 4x103
Stable for 105 turns
Phase space of
Henon-Heiles like
System in IOTA
(simulation)
S.A. Antipov et al 2017 JINST 12 P04008

## Slide 49: Devices for First Nonlinear Optics Experiments
1.8m Nonlinear Insert built by RadiaBeam Technologies
IOTA octupole
Henon-Heiles like system with octupole magnets
  All 18 magnets built as summer project
    Minor consolidation required, in progress
2D-Integrable Danilov-Nagaitsev system
  Magnet built by RadiaBeam as SBIR project
    Delivered to Fermilab, vacuum leak repaired, alignment in progress
Both experiments require turn-by-turn BPM system
Pulsed kickers are those used for injection

## Slide 50: IOTA Major Goals and Nearest Plans
FY17
  ✓Electron Injector installation complete
FY18
  ✓300 MeV electron beam commissioned through injector
  ✓ FAST linac tuning and research (2 months)
  IOTA Ring installation and commissioning with electrons
  Research (4 months into FY19, Sept.-Dec.)
    Nonlinear Integrable Optics in IOTA
    Experiments at FAST linac
  ? Continued work on of Proton Injector
FY19
  Proton Injector installation and commissioning
  IOTA Ring commissioning with protons
  Research with protons and electrons (OSC, NIO ~ 4 months)

## Slide 51: Summary
FAST e- linac commissioned with up to 300MeV beam
  First major SRF accelerator at Fermilab
  Opens way to more accelerator science experiments, technology development (e.g. high-current SRF operation)
IOTA construction in good shape
  Focused team, help of support departments
  Critical path items identified, get constant attention
    Lambertson magnet
    Injection kickers
Plan to complete IOTA in July
  Commissioning in August
  Research with e- beam Sept.–Dec.
Time to ramp up research → this meeting!