## Slide 1: Operational challenges at the LHC and injector synchrotrons
Kajetan Fuchsberger
Many Thanks to: G. Azzopardi, E. Fol, M. Fraser, V. Kain, K. Li, B. Mikulec, J. Wenninger

## Slide 2: Disclaimer…
I am a total ML newby
Thanks to all the colleagues who answered my (potentially stupid) questions!!!

## Slide 3: Content
LHC & Injector Challenges
Examples of ongoing efforts

## Slide 4: Content
LHC & Injector Challenges
Examples of ongoing efforts

## Slide 5: For the sake of completeness…
Depth of 70-140 m

## Slide 6: LHC layout and parameters
8 arcs (sectors), ~3 km each
8 long straight sections (700 m long)
4 Experiments
Protons and pb82+
Energy:
  2 x 6.5TeV/beam currently,
  2 x 7TeV/beam design
Beam:
  Currently: ~1900 bunches / beam
  Design: 2808 bunches / beam
  1.15x1011 particles / bunch
RF
Circumference: 26,7 km.
Depth: 70-140 m.
Acceleration of protons and pb82+ to unprece-dented energy of 2·7 TeV. (v/c= 99.9999991%)
Luminosity of up to 1034cm-2s-1. => About 1 Billion collisions per second in every experiment.
2808 bunches with over 1011 protons/bunch.
Notes: Beam circulating in bunches!
Ions
7TeV design energy
Derzeit 3.5 bis shutdown 2012

## Slide 7: High Power
360 MJ  No “playing around” possible; Highly reproducible operation desired…
Courtesy: J. Wenninger

## Slide 8: LHC Cycle
Courtesy: M. Hostettler
Turnaround: ~ 3 hours
Dumps are Costly!
 Downtime Minimization

## Slide 9: LHC – some more ML ideas
Diagnostics of tripped circuits:
  Aim: Identify cause of circuit failures e.g. quenches, circuit protection trigger/faults
Preventive Maintenance detection
  E.g. Hardware degration (Magnet, Converter, Protection system…)
Instability detection
  Very detailed diagnostics, but triggering is too loose (only ~1% of ~100 triggers per fill are real instabilities)  Improvement potential (classical and/or ML)

## Slide 10: Magnetic Model - Fine Tuning
In principle very good model
But 10-20 % of fills significant deviations
Courtesy: J. Wenninger

## Slide 11: Pre-accelerators
 | Top Energy
Linac | 0.05 GeV
PSB | 1.4 GeV
CPS | 26 GeV
SPS | 450 GeV
LHC | 7000 GeV
The LHC needs most of the CERN accelerators...
1959!

## Slide 12: Injector Challenges
Old machines:
  Operating magnets in saturation
  missing magnet measurement data
  —> difficult to have a precise magnetic (+optics) model
Machine drifts (e.g. temperature): Difficult to keep beams at top quality
Insufficient diagnostics for deterministic correction; correction often based on optimising transmission.
Operation without margin and around narrow optima.
IPM ON/OFF
Courtesy: S. Hirlander
E.g. LEIR Transmission
 Little Changes have big effects

## Slide 13: Multi-Cycle Operation
Every 1.2 s a different cycle
have to handle several hundred different cycles/year in PSB
Difficult to ensure stability of trajectories in transfer lines (+rings) due to different magnet settings:
  different optics
  different destinations,
  magnet hysteresis
  different extraction energies,
  stray field compensation in transfer lines that run along another ring…

## Slide 14: Content
LHC & Injector Challenges
Examples of ongoing efforts
Spike detection for Collimation alignment
SPS septum alignment
LHC Optics measurements

## Slide 15: Content
LHC & Injector Challenges
Examples of ongoing efforts
Spike detection for Collimation alignment
SPS septum alignment
LHC Optics measurements

## Slide 16: Beam Collimation
More than 100 collimators and absorbers; to be aligned every year
beam
1.2 m
 Alignment is a time-consuming task
Commissioning time: Improved a lot over the years, Improvements now saturating
Courtesy: G. Azzopardi
Notes: 17 km langer ring, durchfädeln

## Slide 17: Example: Collimator alignment – Spike detection
A predefined threshold is selected such that when the losses exceed the threshold the collimator stops moving and the data must be analyzed for spikes
Courtesy: G. Azzopardi

## Slide 18: Collimation Alignment – Spike extraction
5 features extracted:
Collimator Position
Spike Height
3 parameters from exponential decay
Dataset used has about ~1500 samples (e.g. 80% training, 20% test)
Courtesy: G. Azzopardi

## Slide 19: Result Examples (MD)
G. Azzopardi, “Spike Pattern Recognition for Automatic Collimation Alignment” No. CERN-ACC-NOTE-2018-0010.
The ML model was tested during an MD and achieved 50/52 correct classifications
Examples:
Correctly classified No Spike Correctly Classified Spike
Courtesy: G. Azzopardi

## Slide 20: ML for Collimation alignment - Summary
The MD results indicate that it is indeed possible to automate the alignment using machine learning for pattern recognition
Fully automating the alignment of collimators will save time and allow for the alignment to be done more often during the year
ML models will also allow for automating the angular alignment methods(*), this is crucial as at present it takes too long to align all collimator jaws at different angle
(*) G. Azzopardi "Automatic Angular Alignment of LHC Collimators." In ICALEPCS, p. 928-933. 2017.

## Slide 21: Content
LHC & Injector Challenges
Examples of ongoing efforts
Spike detection for Collimation alignment
SPS septum alignment
LHC Optics measurements

## Slide 22: Example: ZS (Septum) alignment
Slow extraction from SPS
Notes: [add picture of spill]

## Slide 23
circulating beam
z
x
support
extracted
beam
electrode
(Al, Ti, SS)
beam direction
septum foil
(Mo or W-Re)
scattering
of beam on wires
depleted density
Courtesy: M. Fraser
Wire: 100 um
Length: ~ 3.5m
Notes: 100 um wire, 3m tank

## Slide 24: ZS alignment - Layout
X
Z
ZS1 ZS2 ZS3 ZS4 ZS5
2x girder positions: UP and DO, we usually fix UP
10x anode positions: UP and DO
Courtesy: M. Fraser
All 5 Tanks in beam at once
Today: manual alignment (1 tank at a time), observing total losses and local losses  achieving acceptable losses (Still factor 3-4 lower than expected)
Multi-turn effects: misalignments of dowsntream septa can affect BLM's upstream due to multi-turn effects.
Time consuming (>= 8h) and not very intuitive … too much data
Notes: FLUKA model: expected BLM loss response can be computed for given configuration of alignments: CPU expensive.
perhaps state all 5 tanks are "in beam at once"
perhaps mention today's procedure: it is aligned manually using a beam-based technique aiming to minimise losses measured on BLMs. scanning one dof at a time looking at total losses of all blms and BLMs local to the scan location. start upstream and iterate downstream one tank at a time. repeating iterations. time consuming but it generally works to achieve acceptable losses. often not very intuitive for a human... too much data!

## Slide 25: ZS alignment Challenges – ML approach
Model features:
  12 Inputs (Girder Positions)
  Outputs:
    >20 BLM signals
    Extracted beam intensity
Imperfections:
  Noise on BLMs
  Position Inaccuracy / drifts
ML in very early stage
Toy model  aimed for understanding alignment procedure and investigating new ones: even automatic ones or those using ML algorithms
Already lot of understanding gained by preparation for ML (e.g. toy model creation)
M. Fraser: Poster
P. van Trappen: Talk on Thursday

## Slide 26: Content
LHC & Injector Challenges
Examples of ongoing efforts
Spike detection for Collimation alignment
SPS septum alignment
LHC Optics measurements

## Slide 27: Evaluation: ML for optics correction
Measurement principle
~500 Beam position monitors per beam and plane
Exciting the beam
Oscillations on all BPMs
(Analytically) Calculate beta-beating from phase differences between BPMs.
(+ quite some data cleaning ;-)

## Slide 28: Example: Evaluation of ML for Optics correction
Goal: Proof of Concept to resemble optics model through ML model
Training Dataset: 50000 generated configurations (80% training, 20% test)
Features: Phase errors at BPMs (~500 per beam and plane)
Evaluation of different Estimators.
Elena Fol, “Evaluation of Machine Learning Methods
for LHC Optics Measurements and Corrections Software”, Master Thesis, 2017

## Slide 29: ML for Optics Correction – Estimator examples
Linear Regressor:
“Random Forrest”  almost perfect
Courtesy: Elena Fol

## Slide 30: Summary – discussion
Challenges in LHC & Injectors  Time is the enemy ;-)
First ML tries have shown promising results.
How to identify problems, where ML would be an advantage?
  … And what are the advantages (faster/better/more fault tolerant..?)
  Where better not?