## Slide 1
Derek Plant , dkplant@fnal.gov
Fermi National Accelerator Laboratory
Ghost Train Generator, “Instant Flagman”

## Slide 2: Railroad beds are elevated for a reason
A freight train can weigh 20,000 tons, and travel 70 MPH. Same mass as 4 CDF detectors!
Stable, flexible and adequately drained substrate is absolutely essential, therefore the rails are elevated wherever possible

## Slide 3: Perfect example of a “high centered” vehicle

## Slide 5: Box trailers also have poor ground clearance
This also adds an area for human error

## Slide 6: There are at least 4 people in the response chain. There is no data set. 10 to 15 minutes is common
Click to add caption text [16pt Bold]

## Slide 7: How It Works
Railroad traffic control systems use the rails and train wheels ELECTRICALLY, to keep track of a train’s location, and to keep trains from colliding (Low voltage)
Basically, a train on the track “shorts” the DC track circuit, forcing red lights at a distance from the train
The Ghost Train Generator also forces the existing signal system to change to red condition, alerting oncoming trains to a blocked track
Almost like having a person instantly waving a red flag several miles down the track
Eliminates the 15 minute blind spot

## Slide 8: The Device
5 lb, 14” long:
similar to average kitchen/home fire extinguisher
rail
cross
section
Ghost train
Generator
device

## Slide 9: Wayside Block Signal (East Gate)

## Slide 10: Deploying the Device
Uses High Power magnets
  NdFeB, Grade N42, encapsulated in copper
  13.2 kGauss
  Large surface area
What are the benefits?
  Reliable, secure connection to the track
  Ideal for high traffic, high speed rail crossings where these types of collisions typically occur
  Quick deployment

## Slide 11: Market Size/Impact
Potential Customers
  Heavy commercial vehicles
  Emergency or first response vehicles
  School buses, charter buses, stretch limousines
According to Federal Motor Carriage Safety Administration:
10 million trucks

## Slide 12: Where are we now?
Device works very well; tested at Railway Museum in Union, Illinois
Easy to manufacture and nearly ready for market
  More testing to understand any technical limitations, e.g. at the Federal Railway Administration (FRA) test facility in Pueblo, CO
  Understanding the regulatory environment
We are seeking Licensing Partners
  Patent pending

## Slide 13: Testing at the Illinois Railway Museum (with permission)

## Slide 14: Do you have an idea?
JUST DO IT. Call the OPTT. What can you lose?
It does not have to be complicated or impressive
There are incentives, and opportunity
Does your colleague have an idea? Help them out
Bridge the gap