## Slide 1
Sergei NAGAITSEV (Fermilab)
Nearly all slides are from Vladimir Shiltsev
March 9, 2018
Challenges for Future
Energy Frontier Colliders

## Slide 2: ( Yes or No ) = ( Physics × Feasibility )
PHYSICS case of post-LHC high energy physics machine depends on the LHC discoveries:
  it might call for a collider (if signals are clear)
  otherwise, search for signs of new physics in the neutrino/rare decays (Intensity Frontier) or astrophysics
FEASIBILITY of an accelerator is actually complex:
  Feasibility of ENERGY
    Is it possible to reach the E of interest / what’s needed ?
  Feasibility of PERFORMANCE
    Will we get enough physics out there / luminosity ?
  Feasibility of COST
    Is it affordable to build and operate ?
Will There Be Energy Frontier Colliders After the LHC?

## Slide 3
Colliders: 29 Built… 7 in Operation
VEPP-2000
VEPP-4M
LHC
DAFNE
BEPC-II
KEK-B
RHIC
One under construction: NICA (JINR, Dubna), two new ones proposed

## Slide 4: Colliders: Glorious Past
E~exp(t/5yrs)
UNK
 ?

## Slide 5: Four “Feasible” Technologies
Normal Conducting Magnets
Normal Conducting RF
SC RF
SC magnets
… in addition to “traditional” technologies of tunneling, electric power and site infrastructures, etc …
(CLIC)

## Slide 6: Possible Future Lepton Colliders
ILC 30 km long, 250 + 250 GeV e+e- - SCRF
CLIC
e+e- 50km
1.5 + 1.5 TeV
NC RF
Two beam
acceleration
Muon Collider
~15km μ-μ+ 3+3TeV
NC RF+SC Magn+Muon produc’n; cooling; accel’n
CepC/FCC-ee 250GeV cm
C=52/100 km SCRF NC Mag

## Slide 7
LHC reference
Vladimir’s cost model: https://arxiv.org/abs/1511.01934

## Slide 8: Some thoughts about advanced concepts: plasma and dielectric
To compete with ILC or CLIC designs, an Adv Accel collider concept needs to achieve a luminosity of ~2x1034 at ~1 TeV c.m.
The upper energy for an electron-positron collider is limited by beamstrahlung (not by accelerating technology).
We should keep in mind that particle physicists are asking for an electron-positron collider, NOT electron-electron. Thus, it is important for a plasma-based concept to work equally well for both electrons and positrons.
  Maybe gamma-gamma?
Early non-HEP applications ~2035-2040, time-scale (according the the

## Slide 9: Dielectric Structures: Potentially higher gradient; lower cost due to simpler geometry Capitalizes on CLIC studies
Simplicity
Two Beam Acceleration

## Slide 10: Advanced LC concepts vs CLIC (3 TeV cm) (a simplified personal view)
 | CLIC | DWA-LC | PWFA-LC Blow-out | LPA-LC Linear & hollow
Energy | Gradient & staging de- monstrated, e+ OK | Gradient OK, staging demo, e+ OK | Gradient OK, No staging demo, e+ questionable | Gradient OK, No hollow channel & linear regime demo yet.
Luminosity | High risk | High risk, similar to CLIC | Very high risk | Very high risk
Cost, site power | TPC(US) ~$26B 560 MW | TPC(US) ~XXB$ similar to CLIC ~400 MW | Potential of lower power and lower TPC | Potential of lower power and lower TPC, Promise of many applications

## Slide 11: Possible Future Hadron Colliders
HE-LHC same tunnel, 25-30 TeV cm pp 16T SC magnets
SSC 87km
40cme=20+20TeV
6.6T SC Magnets
Muon Collider
~15km μ-μ+ 3+3TeV
NC RF+SC Magn+Muon produc’n; cooling; accel’n
FCC/SppC
80-100/54 km
100/70 TeV cme
16-20T SC Magn
VLHC
233 km
175 TeV cme
9.8T SC Magnets

## Slide 12
Option 1: re-use
LHC, inj, infrastr.

## Slide 13: 100 TeV pp : Qualitative Cost Dependencies
* for illustration purposes only
Option 2 : Develop Technology to Lower the Cost

## Slide 14: On SC Magnet Technology
Driven by SC cable technology
NbTi – upto 10 T
Nb3Sn – upto 16 T
HTS – 20+T
Cost of SC conductor
NbTi – $$
Nb3Sn – $$ x 5
HTS – $$ x 25

## Slide 15: High Temperature Superconductors (HTS)
REBa2Cu3O7-x (REBCO, RE = rare earth)
coated conductors Geneva, 2016
Achieved 25 T = 21T LTS +4T HTS insert
27 T = 18T LTS +9T HTS insert
NHMFL (Talahassie)
YBCO coil test (2015)

## Slide 16: R&D On Cost-Effective SRF Structures
ILC prototype elipical cell “p-cavity” (1.3 GHz): field alternates with each cell
31.5-35 MV/m
New materials (Nb3Sn) –
higher gradients
New techniques (Nb on Cu) – lower cost
Surface treatment (N2 doping) – higher Q0 and lower operation cost
(ILC)

## Slide 17: Historical prices of Niobium (per ton)

## Slide 18: Option 3: “Move to China !”

## Slide 19: SSRF Spring-8 Diamond NSLSII
1436 m
8 GeV
11 BY
1997
China Japan UK USA
432 m
3.5 GeV
1.2B RMB 2007
562 m
3 GeV
383 M £
2007
792 m
3 GeV
912 M$
2015
Account infl’n, convert to USD and scale to sqrt(1 km):
350 M$ 772 M$ 1040 M$ 1024 M$

## Slide 20: “Move to China !” - Caveats

## Slide 21: A “Dream” Collider
Far Future “Energy Frontier” assumes
  300-1000 TeV (20-100 × LHC)
  “decent luminosity” (TBD)
What we know:
For the same reason there
is no circular e+e- collider above
Higgs-F there will be no circular pp
colliders beyond 100 TeV  LINEAR
2. Electrons radiate 100% beam-strahlung (<3 TeV) and in focusing channel
(<10 TeV)  µ+µ- or pp

## Slide 22: Summary
Post-LHC colliders are possible but :
  Dependent on the LHC results (motivation)
  if based on current technologies (SRF, SCMag, etc) only HE-LHC is cost feasible (<LHC), some are close (CepC/FCCee, ILC, Muon Coll, VLHC-I), others need significant R&D (FCC)…or move to China (?)
  Or must be based on an entirely new technology