## Slide 1: Tritium Debrief: BNB Canopy and Berm Stabilization
Cons Gattuso
March 12, 2018

## Slide 2: BNB Tritium Mitigation
Annual cost of disposal and risk to surface water and groundwater
    ~$350-400K+ for disposal cost
Canopy will allow for observation of leaks while intercepting at least ~70% of water
  Represents most of the tritiated water
  Lateral infiltration volume to exterior wells is estimated as a maximum of ~30% of pumped water from system (in winter frozen surface conditions)

## Slide 3: Vertical Infiltration Solution: Roof/Clay Option
Multi prong approach to address vertical infiltration
  Building Drainage modifications – West Side Done
  Berm Grading/Stabilization (Secondary/tertiary mitigation)
    Starting in ~2-3 weeks
      No beam to BNB during the concrete work that request us to dig into the berm. (projected to be 2 day shifts)
        Retaining walls around
          50 meter absorber diagnostic box
          Berm cooling unit
          Stairwell work
      Adding clay to the berm should not impact operations
      COMM and safety cables relocation
  Canopy (Primary vertical infiltration mitigation)
    Summer shutdown time frame

## Slide 5: MI-12 Finished
Removable roof section
for 25M absorbers
Sky lights
Remove for well
access

## Slide 6: Canopy Criteria Sent to Various Vendors
Length: 200’
Width: 80’
Height: 18’
Type: Straight walls to a height of ~7’
End Walls: Open
Access Doors: (1) 16’ wide x 12’ high
Personnel Doors: (2) 3’ wide x 7’ high
Special: There is a hatch in the middle of the length that requires access. We are flexible as to how this occurs. It could be a removable section or installed in such a way that those segments can be removed in the future.
Notes: Berm Grading/Stabilization
  Bring the berm height back to original height and grade along the length of the berm
    Settling and erosion
  Secondary line of defense for vertical mitigation of water
  Installation issues
    Stair replacement at South end near MI12 service build
    Build up of wall behind berm cooling system
    Well collars to maintain access to wells
    Removal of French drain at north end of the berm
    Redirect the sump of the Peanut tank at north end of berm
    Grading west side of the berm toward Indian creek

## Slide 7: MI-12

## Slide 8: Utility Interference issues
Removal of French
Drain system
Verification of COMM
line running to SBNB
Location of direct bury
120V power line to MI13A
Notes: Relocation of Buried 120V power line to MI13A

## Slide 9
Presenter | Presentation Title or Meeting Title
11/2/2016

## Slide 10
Presenter | Presentation Title or Meeting Title
11/2/2016
MI-12 to MBD Duct |  |  | 
Cable | Signal(s) | Status | Notes
36-C Multimode fiber | TCLK, MIBS, MDAT, NuMI-BP | active/damaged | 5 fibers in use; OTDR shows loss at ~700 ft
24-C Singlemode fiber | ACNET, various signals | active | all fiber in use; network, etc.
1/2" Cablewave 50 Ohm Coax | BRF | (SBN) | rf at MBD
1/2" Cablewave 50 Ohm Coax | BES | (SBN) | No BES at MBD
1/2" Cablewave 50 Ohm Coax | RWM | no longer in use | TDR'd OK
1/2" Cablewave 50 Ohm Coax | spare | unused | TDR'd OK
20 Cond 18 AWG Blue Jacket | Safety- Interlocks | active | NuMI Interlocks
20 Cond 18 AWG Blue Jacket | Safety- Interlocks | active | NuMI Interlocks
4 Twisted Pair 18 AWG Blue Jacket | Safety- Interlocks | active | NuMI Interlocks
4 Twisted Pair 18 AWG Blue Jacket | Safety- Interlocks | active | NuMI Interlocks
4 Twisted Pair 18 AWG Orange Jacket | Fire Protection | active | FP network, MSB to MI-65
75 ohm 1/2" Hardline | CATV | unused | not terminated at MBD
75 ohm 1/2" Hardline | CATV | unused | not terminated at MBD
75 ohm 1/2" Hardline | CATV | unused | not terminated at MBD
75 ohm 1/2" Hardline | CATV | unused | not terminated at MBD
Moved in 2016
Abandon in place
Will be installed in 5-6 weeks
Determining the status

## Slide 11: New Communication Duct
Daniel ohnson | MI-12 Duct Meeting
New duct bank installed (partial)
  MI-12 to just short of Geise Road
Cable relocation process
  Once all the cable arrives we will pull it
  Connection will be made up during the summer shutdown period
  Will not impact operation
11/23/2016