## Slide 1
ESS status and progress（Ti ESS, feedthrough dose measurement, others)
Y. Arakaki (KEK)
HD
Nu
RCS
MR
Linac
MLF
J-PARC

## Slide 2
ESS configuration
Ti-ESS1
Ti chamber：φ593.6mmx1700mm
Material ： pure titanium II
surface treatment ： San-titan
Ti-yoke
Electrode
Feedthough
Positioning (Electrode）
Positioning (Yoke）

## Slide 3
Absorbed Dose Measurement @Feedthough
Measurement Range
Alanine dosimeter :10Gy~100kGy
OSL(Optically Stimulated Luminescence Dosimeter)
:0.1mGy~10Gy
Period of installation | RUN | ESS1（Gy） | ESS2（Gy)
2012/01/19~2012/02/24 | RUN40(SX) | 432 | 79.9
2012/02/24~2012/06/06 | RUN41,42(FX） | 20.238 | 25.535
2012/06/06~2012/07/10 | RUN43(SX) | 1061.5 | 124.5
2012/12/12~2012/12/28 | RUN45(SX) | ---------- | -----------
2012/12/28~2013/01/17 | RUN46(SX) | 1332 | 173
2013/01/17~2013/03/06 | RUN47(FX) | 47 | 43
2013/03/06~2013/05/08 | RUN49(SX,FX) | 1003 | 147
2014/03/17~2014/08/29 | RUN52~56(FX) | 1.222 | 0.509
2014/08/29~2015/04/02 | RUN57~61(FX) | 15 | 19
2015/04/02~2015/06/03 | RUN62(SX,FX) | 3824 | 478
2015/06/03~2015/07/01 | RUN63(SX,FX) | 5015 | 526
2015/09/29~2016/01/19 | RUN64~65(SX) | 14966 | 1946
2016/01/19~2016/05/25 | RUN66~68(FX) | 111 | 14
2016/05/25~2016/08/03 | RUN68~69(SX) | 8798 | 1093
2017/01/25~2017/04/12 | RUN72~74(FX) | 762 | 73
2017/05/31~2017/10/10 | RUN75(SX) | 12272 | --------------

## Slide 4
Alanine dosimeter (Upstream)
Alanine dosimeter (Downstream)
Beam
yoke
Electrode

## Slide 5
Dose of ESS @ Feedthough
Only one ESS operation
in May 2017
due to the serious
failure.
The absorbed dose of ESS1 is 8 times higher than that of ESS2

## Slide 6
Fluorinert Circulation
Device
Fluorinert FC40
ESS1
ESS2
Expansion Tank
Fluorinert circulation system in ESS (Closed system)
Since the resistant pressure of feedthough is 0.157MPa, The pressure limit
is set to be 0.1MPa in case of clogging.
Feedthough
Pipe
Line size: 3/8
Material:SUS316L
Total length:~50m

## Slide 7
Old type feedthough (SUS304)
Stress cone(Hollow)
Fluorinert(FC４０)
0.2L+1.15L+0.16L
=1.51L
200cc
160cc
IN
Out
Ceramic (KP-999)
Flange and stress cone
is separated
polyethylene
ICF

## Slide 8
New type Feedthough (Ti)
Stress cone(Solid)
Mounting flage
(Unibody)
EPDM rubber
(radiation resistant)
Fluorinert(FC４０)
1.15L
Polyethylene
Metal O-ring with silver coating
Metallized
&brazing
Welding
Ceramic (A-601L)

## Slide 9
Mounting Flange
M8-30 bolt
Ti64aroy
with TIN-coating
to avoid galling
Kapton film
for protection of ceramic
while assembling
Finger contact
material:Titanium
Ceramic bushing
Assembling the feedthogh

## Slide 10
A cross sectional view of the Feedthough

## Slide 11
Ti-ESS2
The surface is finished with San-titan after buffing

## Slide 12
Vacuum features in Ti-ESS2
Ion pump(600L/s)
TMP(480L/s)
Ion guage
Blue line :Ion pump
Green line: Ion guage
2018/03/09
Scroll pump ON
(pumping from atmosphere)
2018/03/05
2.8x10-6Pa
7.9x10-7Pa