## Slide 1: Bunch-by-bunch Neutralization and applications for H- beams
David Johnson, Todd Johnson
US-Japan Collaboration Meeting
14-March-2018

## Slide 2: Lasers for Accelerators
Lasers have been used for laser profile monitors; SNS, BNL, JPARC, …and
  H- + g -> Ho + e-
3 step process of 2 electron removal (H- Stripping for injection)
  SNS Model
  J-PARC Model
The first as notcher test here at FNAL linac (first demonstration circa 2000 Ray Tomlin using a 500 mJ q-switch laser on a CW beam in 750 KeV line to create a single notch)
Additional notcher proposals were described in 2005 by Xi Yang to notch the linac beam at the Booster injection RF frequency (FN-0765-AD) and at the revolution frequency utilizing a pumped recirculating cavity (FN-0767-AD). Neither of these proposals were implemented.
The first bunch-by-bunch neutralization system using a laser proposed 2009 for Project X wideband chopper.
“Laser Chopping Concepts” presented to APC SCRF group Nov. 2009
“Linac Laser Notcher in the Proton Improvement Plan” APT seminar Feb 2014
“Fermilab Linac Laser Notcher” IPAC 2015 (poster/paper)
“Linac Laser Notcher for the Fermilab Booster” LINAC 2016 (invited talk/paper)

## Slide 3: Laser Landscape
Laser Notcher
Courtesy of Yun Liu, SNS
Laser Stripping Workshop 2013

## Slide 4: Design ideas (1)
Major questions to determine Laser/Amplifier requirements;
  What are we trying to do with our laser interactions of H-ions
    Neutralize or strip ?
  Ion beam energy
  Ion bunch structure –PRF (MACRO, MINI, MICRO bunch structure)
  Ion beam size (transverse and longitudinal)
  How many bunches do we want to affect?
 Duty factor
J-PARC LINAC beam parameters:
Pranab K. Saha: 2017/11/08
LI peak current at present: 50 mA
LI pulse width/ repetition: 0.5ms/25 Hz
Duty = 1.25%
Chopper duty on beam: 56%
When ADS will be in operation:
LI repetition will be upgraded to 50 Hz
25 Hz w/ chopper on to the RCS (133 kW)
25 Hz w/ no chop to the ADS
 324 (972) MHz micro pulse to the ADS
Beam power to the ADS: 237 kW
To ADS TEF-P target: 10 W at max.
Rest of 237 kW to the ADS TEF-T target
DF 5.3E-4
DE 3.6E-2
DF 0.4
Total DF 7.7E-06

## Slide 5: Design ideas (2)
Laser requirements
  Wavelength (near IR, MID – IR , UV, deep UV ?)
  Pulse length
  Pulse energy
  Base rep frequency
What type of laser system
  Given the laser requirements
    Off the shelf (commercial) OR custom system design
    Laser system (cavity & gain medium) OR Seed/Amplifier (i.e. MOPA)
  Further choices
    Bulk gain media OR fiber gain media OR a combination (i.e. hybrid)
    CW pumped or pulsed pumped or some combination
  Interface – how to interface to your facility
Peak Power
Average Power

## Slide 6: Design ideas (3)
Lasers (pumped gain medium in a cavity – CW or pulsed (q-switch)
  Source of pulses to be amplified either in fiber or bulk amplifiers
  Creation of final pulse requirements
Amplifiers
  Requires a seed source
    Laser with a given prf (or maybe adjustable)
    CW diode laser with external pulse modulation
      This allows for a very flexible pulse format
      The pulse energy at this stage is VERY low ( 10’s pJ’s)
  Requires amplification to get to uJ or mJ pulse energies
    How many stages to get uJ or mJ
      Assume 1 mJ from 1 pJ  90 dB  6 stages
    Details get rather complicated at this point as to selection of seed and amplifiers

## Slide 7: Example of Amplifier chain
Chart: Laser Notcher Energy Gain w/ Phase modulator and Booster amp

## Slide 8: Example of Amplifier layout
Peak Power:
Laser Notcher design
2 mJ/2 ns = 1 mW
Currently ½ to ¾ MW
82 mJ/500ns = 164 kW
Slide from: Andy Clarkson
ORC, Southampton ,UK
SMR 1829-5 (2007)

## Slide 9: Laser System Block Diagram for Laser Notcher
MOPA system
Hybrid Amplifiers
Transverse profile shaping
Must lock to 200MHz Linac bunch
Must lock to Booster RF
Cogging system must lock to notch
Booster must lock to existing notches
Design Intensity 2 mJ/pulse for 256 pulses/linac cycle.
Currently running a mean pulse energy of 1 mJ for 272 pulses/linac cycle
PCF gain fiber

## Slide 10: Non-resonant interaction cavity to reduce required laser power

## Slide 11: Reduction of required pulse energy

## Slide 12: Change number of bounces by adjusting input angle into cavity

## Slide 13: Adjusted our transverse laser profile and collimated the H- in vertical

## Slide 14: Development going Forward

## Slide 15: Examples of PCF Amplifier
Version built for MIT runs at ~1 mJ/pulse (3-4 ns)
300 kW peak power 200W average power sustained

## Slide 16: Concept for Momentum collimation – shaving longitudinal phase
pw
ps
prfmicro
w
prfMACRO
pw = 50 ps each
pE = 15 uJ each
ps = 2 ns
prf = 201.25 MHz
DF = 0.016
w = 50 us
prf = 15 Hz
DF = 7.5E-4
Laser produces 201.25E6*50e-6 = 10,000 pulses /cycle
For 30 uJ/pulse*10,000 pulses = 0.3 J /pulse
Peak Power = E/pulse/pulse width
=30 uJ/0.1 ns = 300 kW
Average power = Peak power*DF
= 300 kW* 3E-5 = 9W
Linac
Split amplified pulse delay line  recombine
temporally with adjustable spacing (ps)
Create head/tail out of single amplified laser pulse
Spot size 1mm x 7.5mm
50 passes, 0.59 mm separation, 1.19mm at mirror
cavity length 2.9 cm, laser path 0.73 m,
neutralization 96% with 15 uJ pulse

## Slide 17: Concept for Momentum collimation – shaving longitudinal phase
pw
ps
prfmicro
w
prfMACRO
pw = 100 ps
ps = 1 ns
prf = 162.5 MHz
DF = 0.016
w = 500 us
prf = 15 Hz
DF = 7.5E-3
Laser produces 162.5E6*500e-6 = 81,250 pulses /cycle
For 10 uJ/pulse*81,250 pulses = 0.8125 J /pulse
Peak Power = E/pulse/pulse width
=10 uJ/0.1 ns = 100 kW
Average power = Peak power*DF
= 100 kW* 1E-4 = 10W
PIP-II Momentum collimation
Split amplified pulse delay line  recombine
temporally with adjustable spacing (ps)
Create head/tail out of single amplified laser pulse
Spot size 1mm x 1.6mm
100 passes, 1.1 mm separation, cavity length 10.9 cm
Laser path 1.6m, neutralization 99.7% with 5 uJ pulse

## Slide 18: Summary
We have demonstrated the ability to neutralize individual bunches with in a bunch train.
This flexibility can be applied to many applications, not only in H- manipulation, but in any application requiring multi-MHz pulses in a continuous or burst mode
Fermilab continues to develop technology in non-resonant interaction cavities.
Fermilab will continue to develop laser system with a high peak, high average power quasi-CW laser systems suitable for full linac pulse neutralization applications.
We see this approach as contributing to the further growth in the utilizing of laser interactions with H- for a variety of applications.

## Slide 19
END

## Slide 20: Required Pulse Structure
We must match the H- ion 200 MHz bunch structure exiting RFQ.
The width of the 200 MHz burst must be at least 60 ns to allow for rise time of the Booster extraction kicker (we will use 80 ns).
Number of notches = Number of injected turns in Booster – 1.
Each pulse must match H- bunch length out of the RFQ.
Want variable pulse length and roughly uniform spatial and temporal profiles.

## Slide 21: Photoneutralization
The fraction of electrons that are detached from the moving H- ions is:
The photon flux (generated by the laser)
in the lab frame [photons/cm2/sec]
The photon flux in the lab frame is transformed into the
rest frame of moving ion as:
The interaction (crossing) time is just the ion path length/ ion velocity
The neutralization factor for an ion crossing on axis
of the laser beam may be written in terms of lab frame parameters
21
Total neutralization for N interactions