## Slide 1
US-Japan Collaboration on high intensity neutrino beams ● Laser manipulation of H- beams Brief status at J-PARC &
Progress of 400 MeV H- striping to protons
by using only lasers -
Pranab K. Saha
On behalf of J-PARC laser stripping group
US-Japan Collaboration meeting @ Fermi National Accelerator Lab, USA
2018/Mar/28-29

## Slide 2
Laser manipulation of H- beams --- status at J-PARC
Three major activities:
-- Proof-of-principle (POP) demonstration for 400 MeV H- stripping to protons by using only lasers.
Goal to realize laser stripping H- charge exchange system.
-- Developments of H- neutralization system by using laser for J-PARC TEF.
R&D studies at 3 MeV H- now. To be tested for 400 MeV H- and put the system for operation.
-- Multi-laser-wire diagnostic system for measuring H- beam profiles at J-PARC.
R&D stage, Laser stripping chamber will be used.

## Slide 3
Outline:
1. Brief introduction of J-PARC and the RCS
2. Motivation of H- laser stripping
3. Principle of H- stripping by only lasers
4. Experimental strategy, progress to date
5. Summary and outlook

## Slide 4
Neutrino Beam Line to Kamioka (NU)
Materials & Life Science Facility (MLF)
3 GeV Rapid Cycling Synchrotron (RCS)
Hadron Experimental Hall (HD)
400 MeV H- Linac
50 GeV Main Ring Synchrotron (MR) [30 GeV at present]
J-PARC
KEK & JAEA)

## Slide 5: 1. Introduction of J-PARC 3-GeV RCS
Layout of J-PARC 3-GeV RCS
● Multi-turn H- stripping injection.
(stripping efficiency: 99.7% design)
● Injection Energy: 400 MeV
● Extraction Energy: 3 GeV
● Repetition: 25 Hz
● Beam power (design): 1MW
Successfully demonstrated
in the beam studies!
Mid-term plan for beam power
Upgrade to 1.5 MW!
Two big reasons:
① RCS beam sharing to the MLF and MR.
When MR runs at 1s cycle (~2018), RCS beam
sharing to MLF becomes: (25-4)/25 = 0.84
RCS equivalent beam power to the MLF
should be 1.0/0.84 = 1.2 MW!
② Also planning for a second neutron
production target station at MLF.
Stripper foil lifetime may be the most
concerning issue!
● Feasible scenario:
Peak current: 50  60 mA
Injection pulse: 0.5  0.6ms

## Slide 6: Motivation
An alternate H- stripping method other than using stripper foil.
 Laser stripping of H- holds the promise of eliminating
limitation and issues involved of using stripper foil.
Reasons:
■ May be hard to maintain stable and longer foil lifetime for
1 MW routine operation at J-PARC RCS.
■ Foil may not survive at 1.5 MW beam power.
■ Foil scattering beam loss and the resulting high residual
radiation at the injection area is already a serious concern for
hardware maintenance even at lower beam power.
★ Additional collimators had to installed at the downstream of stripper foil.
★ New design of the injection chicane magnets to install radiation
shielding surrounding the foil are in progress.

## Slide 7: Experience of stripper foil behaviors at the SNS and J-PARC
To | Pbeam (MW) | Beam sharing(%) | e_painting (p mm mrad) | Foil hit
MLF | 1 | 84 | 200 | 10
MR | 1 | 16 | 50 | 70
S. Cousineau (HB2014)
Normalized avg. foil hit: ~20 but
instantaneous foil heat for MR cycle is extremely high!
If the total charge limit on foil is 10000 C
 Foil lifetime at 1 MW: 2 weeks at best!!
J-PARC: 0.3 MW operation
Avg. foil hit: 10
Foil hit at 1 MW operation (estimation)
Unstripped H- increased
twice more.
Waste beam dump
capacity: 4 KW

## Slide 8: Energy deposition and foil temperature (Comparison between RCS and the SNS for 1 MW beam power)
Accelerator | T [GeV] | tinj [ms] | Foil thickness [mg/cm2] | Avg. foil hit | Energy Depo. (dE) [J] | Wpeak (DE/tinj) [Watts-peak]
J-PARC RCS | 0.4 | 0.5 | 340 | 10 | 0.2598 | 276
SNS-AR | 1 | 1 | 300 | 6 | 0.0712 | 71
Wpeak and foil temperature (T):
Wpeak ∞ T4
Wpeak (RCS) / Wpeak(SNS) = 4
T (RCS) ≈ 1.4 x T (SNS)?
(Rep rate not taken into account)
If stripper foil limits SNS beam
power to 1.5 MW,
it is then may be 1 MW at
J-PARC RCS!!

## Slide 9: Residual radiation at the RCS injection area
M. Yoshimoto
Residual radiation near the stripper foil is as high as 15 mSv/h
on contact, 4 hours after 0.4 MW routine operation!

## Slide 10: Review of our earlier study for laser assisted H- stripping at 400 MeV (same as SNS framework)
Magnetic field issues:
● In the practical application, the
magnets should have larger radius.
● For 400 MeV H-, hard to realize
over 2 T magnetic field.
● Circulating beam size after
injection is quite large!
r ~5 cm!
A. Aleksandrov, HB2014
For SNS 1 GeV H-
Magnetic field 1.2T
Inner radius: 0.15cm
Peak power: 1 MW
Stripping eff.: 90%
J-PARC RCS: 400 MeV injection for 1 MW.
Beam distribution at the end of injection.
( Simulation: TP: none, LP: full )

## Slide 11: Principle of H- stripping by only lasers at J-PARC
H-
H0
H0*
p
e-
e-
e-
e-
Excimer laser
l= 193 nm
Step 1:
H- + g → H0 + e-
Step 2:
Excitation of H0
H0 + g → H0* (n=3)
Step 3:
H0* + g → p + e-
Nd: YAG Laser
l=1064 nm
Nd: YAG Laser
l=1064 nm
63.3°
90°
90°
Isao Yamane, Hiroyuki Harada, Saha Pranab and Shinichi Kato
PASJ, Vol. 13, 2016, 1-11 (in Japanese)
Doppler effect of the 400
MeV H- beam:
b = 0.713, g = 1.426
l = l0 (1 + b cosa)g
Process | Eph (eV) | l (nm) | a (deg.) | l0 (nm) | Laser
H- H0 | 1.67 | 1064 | 90 | 743 | Nd:YAG
H0H0* | 12.1 | 193 | 63 | 102 | Excimer (ArF)
H0*p | 1.67 | 1064 | 90 | 743 | ND:YAG
DE=12.1 eV
DE = hc/l0
l0= 102 nm

## Slide 12
SNS demonstrated 90% stripping
for 1 GeV 10 ms H- pulse
H-
p
Laser pulse and peak power:
Nd:YAG laser of 1064 nm
 3rd harmonic conversion (355 nm)
Synchronized to 402.5 MHz H- pulses.
Pulse energy and width: 50mJ, 50ps
 Peak power: 1 MW
SNS, Oak Ridge
B >1T
Stripping efficiency: Achieved > 90%

## Slide 13: Photodetachment, Photoionization cross sections and the corresponding laser power
743 nm
s = 4×10-17 cm2
13
800nm
s= 1.8×10-17 cm2
Eph = 1.67 eV @ 743 nm
Saturation density Fs in PRF
Fs = (Eph/s) = 6.7×10-3 J/cm2
r(H-) = 1mm, t(H-)=30 psec
ti(collision) = 10 psec, tl(laser) = 40 psec
E(laser) = (Fs/g)×(pr2)×(tl/ti)
= 0.6 mJ  15 MW
L. M. BRANSCOMB, “Physics of the One-And-Two-Electron Atoms”,
Edited by F. Bopp and H. Kleinpoppen, North-Holland, (1969)
E(laser) = 1.3 mJ  33 MW
Photodetachment
H- H0
Photoionization
H0*  p
H- neutralization is well studied in many places:
FNAL: Laser notcher system
J-PARC TEF: R&D studies for 3 MeV H-.

## Slide 14: Lasers we have for the POP demonstration
Two Nd: YAG lasers available:
Purpose: 1st (H-  H0) and 3rd (H0* p) stripping
1. Nd: YAG 1064 nm, 5-9 ns (FWHM), E= 0.2 ~0.6 J
-- Detail study under progress with 0.2 J
2. J-PARC TEF facility has one more powerful YAG laser
Nd: YAG 1064 nm, 5-9 ns (FWHM), 1.6 J
Test experiments done for 3 MeV H- neutralization.
Excimer laser:
ArF 193 nm excimer laser (by Mlase)
Energy= 13 mJ, Pulse length = 5-10 ns (s)
Bandwidth: ~4THz
 Ppeak > 1 MW can be reached
Excitation efficiency: 90% might be achieved.
If we succeed pulse compression of the ArF laser,
we can reach Ppeak >> 1 MW
ArF 193 nm excimer laser
Manufacturer data
193 194
…. Air
N2 purged
0.3 ×0.6 mm2

## Slide 15: JFY 2017 progress highlights
1. Preparation of POP (Proof-of-principle) demonstration of 400 MeV
H- stripping to protons by using only lasers at J-PARC is under preparation.
--- Vacuum chamber in the beam line is installed.
--- R&D of the lasers are also in progress.
--- Simulation, H- beam manipulations more details from now.
2. For R&D of the lasers we have new collaboration with Kyoto Univ. and
the Univ. of Electro-communications, Tokyo (in progress). ---(H. Harada leading)
3. Dr. Timofey from SNS visited J-PARC
for 2 weeks in March as an invited fellow.
-- Worked with Saha to develop pyORBIT
code for 400 MeV H0 excitation.
-- Discussion on the J-PARC laser stripping
strategy, H- beam manipulation, etc.
Laser peak power for
H0 excitation
Specially optimized H- beam
1.3 MW for 90% excitation

## Slide 16: Recent status and the strategy in detail
We aim to demonstrate ~90% stripping efficiency
for a single micro pulse.
To do
■ We should study about the expected laser power and
effort to reduce the laser power.
■ Experimental strategy and the measurement techniques
We should use existing devices and monitors for
the POP demonstration.
● Extensive R&D studies of the lasers:
H. Harada, P.K. Saha + other members..
● H- beam manipulation, measurement principles…
P.K. Saha, A. Miura, H. Harada + other members…

## Slide 17
Experimental place, beamline
The POP experiment will be performed at the end section of
L-3BT (Linac to the 3-GeV Beam Transport)
H-
H-
H0
p

## Slide 18
Experimental Setup and strategy
● We can simultaneously measure all three charge fractions in three separated beam
lines in the downstream of IP.
● A stripper foil will be installed near 90-deg dump to strip H0 to p for measuring it.
For confirmation of H0 excitation, we can also measure emitted lights from H0 decay.
Setup for the POP experiment
(Nd: YAG laser can also be splitted in
the beginning for the 1st and 3rd steps)

## Slide 19: POP experimental devices setup
QM61
~1.5m
H- beam
Chamber for the
POP chamber
End section of Linac to 3-GeV
Beam Transport

## Slide 20: Vacuum chamber for POP experiment installed
H- beam
The chamber is designed for multi purpose laser manipulation of the H- beam.
● Laser stripping of 400 H- beam.
● Multi-layer laser wire monitor.
● Electron impact on H-/p for beam for stripping, monitoring, SC neutralization, etc..

## Slide 21
There are many windows on the chamber
for multi-purpose uses.
Vacuum chamber: close view
The excimer laser window is made large to try for direct ionization of ground state H0
l0 = 91.2 nm, l = 193nm,
From l = l0(1 + bcosa)g
a = 47o
Variation range: 67o<a<45o

## Slide 22
Laser power for 400 MeV H0 excitation (n=3) at J-PARC:
-- Based on SNS experience
V. Danilov, PRST-AB 6, 053501 (2003)
Where, d is the ratio of unexcited and excited atoms. d <<1 is expected.
Ppeak = 1 MW for 90% efficiency
At 400 MeV (b=0.713, g =1.4263), Naively, Ppeak ~1.7 MW is required 90% efficiency.
To reduce the laser power, extensive manipulations of the H- beam
were done at the SNS:
★ Shorter longitudinal beam size. sz = 30 ps  Not an issue for our POP expt.
★ Dispersion derivative of the H- beam
★ Minimization of the betatron angular spread
★ Smaller vertical beam size
Laser peak power, Ppeak for H0 excitation n=13
How much we can optimize
these parameters?

## Slide 23: Reduction of laser power
Let’s take the equation of laser beam angular spread (Yamane-san)
Required angular spread of the laser pulse:
Introduce dispersion derivative
Reduction of betatron
angular spread (page 14)
0
=

## Slide 24
In order to eliminate transition frequency spread, due to the momentum
spread dp/p0 in the H- beam, dispersion (D) tailoring method is utilized.
= = -1.3
Due to the Doppler effect
= l0 (1+bcosa)g
b, g are Lorentz parameters
a = a0 – x’, da = -x’
For reference particle (dp/p0=0),
a = a0
For off-momentum particle,
x = D(dp/p0), x’ = D’(dp/p0)
From dp/p0 = (1/b2) dg/g
da/dg = -D’/b2g
The dispersion relation becomes,
g1
g2
g3
gn
a
H0
H0*
Uniform laser beam
● Hydrogen atom with different energies have the
same laser light frequency in their rest frame.
● Laser light does not have to have a divergence.
 Gain on the laser peak power.
Dispersion derivative of the H- beam
g0

## Slide 25: Optimization of betatron angular spread
X
X’
Transverse beam emittance:
e = gx2 + 2axx’ + bx’2
g = (1+a2)/b
tan(2f) = 2a/(g-b)
a, b, g, e are twiss parameters
Angular spread is controlled by optimizing a to zero and also with large b.
a = 0
X
X’
{
f
a = 0, b enlarge
As for the vertical size of the H- beam, a smaller size is required to
gain on the beam density. At SNS, sv = 0.15 mm achieved.

## Slide 26: Trial optimization of the H- beam
~ Typical
1st trail of optimized for
POP experiment
Further more studies needed
IP
Transverse beam optimization at the IP
D’ = -0.13
Efforts are ongoing
IP

## Slide 27: Measurement Strategy for POP demonstration, expected signal
20ns
Excimer laser
pulse
Typical 324 MHz BPM electrode signal.
The H- beam signal will be reduced in the laser pulse overlapping region.
The protons go to the 100 deg. dump.
H- pulse
3ns
. . .
3.08ns
Micro pulse (324 MHz)
814ns
456ns
. . .
Intermediate pulse (1.2285 MHz)
(Structure @ injecting into the RCS)
0.5ms
40ms
. . .
Cycle (25 Hz)
RCS
Macro pulse
We concentrate only on a single micro pulse.
Use stripline BPM signal.

## Slide 28: How to cover 0.5 ms (~105 micro pulses) for practical application?
toroidal mirror
toroidal mirror
plane mirror
Splitter mirror
Lens
seed laser
100mJ, 100psec, 25Hz
waist
waist
(IP)
waist
(transmission：~1%)
amplifier
amplifier
laser output
monitor
H－beam
One candidate: Laser storage ring, originally
proposed by Isao Yamane.
We plan for detail R&D studies but many issues
to realize full specifications, especially for
the excimer laser.
Amplification, laser life time …
Alternative ideas should come.
H. Harada

## Slide 29: Measurement method of stripping efficiency of a single micro pulse
Checked by inserting L-3BT scrapper at present
(Charge-exchange type transverse beam halo scrapper. Stripped protons go
to the 100-deg. Beam dump)

## Slide 30: Measurement techniques: Experimental results
FFT
Stripping efficiency of single medium pulse
can easily be obtained by using FFT analysis.
However, we have to obtain stripping efficiency
of a single micro pulse of 324 MHz.
 Analysis of individual micro pulse

## Slide 31: Analysis of individual micro pulse
● New effort to measure micro pulse stripping
efficiency.
● Can be utilized also for micro pulse stability.
100-deg. dump (p)
L-3BT line (H-)
Fraction p : pink to red
Fraction H- black to blue

## Slide 32: Laser stripping of 400 MeV H- beam --- Scheduled step by step
● The detail studies of ND:YAG laser are in good progress. At present detail of
laser stability, pulse shape up to with 200 mJ are being studied.
★ The ArF excimer laser study just started.
★ We will work for pulse shortening of the lasers.
★ Placing lasers at the acceleration tunnel is big issue!
H- neutralization
study first.

## Slide 33
The preparation for POP demonstration of 400 MeV H- stripping
by using only lasers at J-PARC is in progress.
The experiment will be carried out in steps.
First trial of complete set of experiment planned within JFY 2018.
Laser and H- beam manipulations more studies needed.
Measurement technique for even a single micro pulse established.
POP final goal: 90% stripping efficiency for a single micro pulse.
Next step, not straightforward to cover ~105 micro pulses.
Candidates:
Laser storage ring synchronized with 324 MHz H- micro pulse.
Many issues for realistic implementation with full specifications.
Other ideas have to come.
Summary

## Slide 34: Collaboration outlook
■ Laser interaction of the H- beam for utilization in stripping,
chopping, beam diagnostic and other manipulations are an
important subject for the present and next-generation
high-intensity proton accelerators.
■ Non-destructive and highly required not only for the existing
high intensity machines but also to realize multi-MW beam power.
The collaboration aims at
Developing a framework for an effective laser manipulation
of the H- beam
 Achieve maximum efficiency with a minimum laser power.
Explore for multi-dimensional application.
. . . . . . . . . . . .