## Slide 1: Multi-laser-wire diagnostic system for measuring H- beam profiles at J-PARC
Akihiko Miura
J-PARC Linac, JAEA
29th, Mar., 2018
Meeting on Laser manipulation of H- beam under the US-Japan Collaboration for high intensity neutrino beams, Fermilab, Batavia, Illinois, USA

## Slide 2: Contents
Multi-laser-wire diagnostic system for measuring H- beam profiles at J-PARC
Beam specification of J-PARC linac
Introduction / Objective
Design of the multi-laser-wire
Demonstration of the multi-laser-wire formation
Design of the multi-laser-wire profile monitor
Conclusion

## Slide 3: 1. Beam specification of J-PARC linac
Beam-line layout of J-PARC linac
Linac accelerates the H- beam up to 400 MeV.
There are 8 matching sections where the transverse matching is conducted using the wire scanner monitors.
: matching section
H- beam is accelerated by 324 MHz RF which is the smallest time structure (3.01 ns).
Intermediate bunch with 560 ns is for the injection to the downstream RCS.
The longest pulse duration is 0.5 ms.
Time structure of pulsed beam

## Slide 4: 2. Introduction / Objective
Beam profile monitor plays am important role in the high-current and high-brilliance accelerators.
To avoid the thermal damage of the metallic wire scanner monitor and to reduce the radiation during an operation, the laser-wire method is the possible candidate for the profile measurement.
The photon energy with only 0.75 eV is required for the photo detachment to generate H0 from H-.
Laser-wire profile monitor

## Slide 5: 2. Introduction / Objective (Cont.)
A simple optical design with only a pair of concave mirrors brings the multi-laser paths.
No scanning device and no multiple-shots of the accelerated beams are required for the system.
Multi-laser-wire
To design the system for the J-PARC linac, the feasibility check and the demonstration of the multi-laser-wire formation are key missions of our study.
Objective of the study

## Slide 6: 3. Design of the multi-laser-wire
The 1/e2 radius at c0, c1, ……, cn as w0, w1, ……, wn using a wave length (l).
Injecting Beam
f2
f1
Focal Lens
b1
d1
a
c0
c1
c2
axis
Mirror 2
Mirror 1
x2
x0
x1
b2
d0
A pair of concave mirrors with different diameters to make multi-paths of laser beam, and the beam waists of the laser paths are aligned in principle.

## Slide 7: 4. Demonstration of the multi-laser-wire formation
Injecting Beam
f2
f1
Focal Lens
b1
d1
a
c0
c1
c2
axis
Mirror 2
Mirror 1
x2
x0
x1
b2
d0
Thin film plane
A thin film plane is inserted to observe the laser paths.
The aligned multi-laser spots on the target is clearly observed.
The laser beam spots is approaching to “a”.
We will use the top-half of the confocal cavity.
The relation wn = (f2/f1)n-1 w0 suggests the spot size decreases at f2 > f1.

## Slide 8: 4. Demonstration of the multi-laser-wire formation
laser intensity measurement using a micro-mirror
a
Mirror 2
Mirror 1
Photodiode
Micro mirror
A micro mirror is produced by f30um gold-wire with optical flat surface.
A photodiode is used for the quantitative measurement.
We could count 24-laser spots at the top-half of the center axis clearly.
Spots are overlapped around the center axis.

## Slide 9: 5. Design of the multi-laser-wire profile monitor
Wavelength of laser beam
A region for large cross-section
Visible light
Wavelength should be matched the cross section of the photo detachment of H- to H0.
Visible light (l = 380-800 nm) is included in the large cross sectional region.
When we chose the longer or shorter wavelength, we can take a match to the largest cross section with incident angle described by following eq.
Requirements of the laser profile monitor | 
Wavelength | 400 – 1200 nm
Horizontal resolution | < 0.2 mm
Dynamic range | > 102
Measurement time | 2.5 mins / profile

## Slide 10: 5. Design of the multi-laser-wire profile monitor
Horizontal resolution and dynamic range
Minimum beam size is 2.0 mm RMS. Less than 0.2-mm intervals are required.
The beam halo appears around 1/10 magnitude of the beam core. Over 102 dynamic range is required.
Transverse profile taken by WSM
a
Mirror 2
Mirror 1
Micro mirror
Time intervals
Accelerated beam duration is 3.01 ns intervals due to 324 MHz RF.
Time of the laser beam round trip is 4L/c (L = f1+f2).
Laser beam flight time should be in the RF repetition timing, i. e.,
.

## Slide 11: 6. Conclusion
Advancement of the multi-laser profile monitor
No scanning device is required.
It is non-destructive to the accelerated beam.
Fast data taking.
Summary
Demonstration of the multi-laser-wire formation was conducted.
We set the specification of the laser profile measurement.
We proposed the design policy of the multi-laser-wire profile monitor.
Future works / Discussions
Need to discus how to match a laser and H- beam.
Need to decide the electron detector.
Design, fabrication and test at 3-MeV beam line.
Application to the 400-MeV beam line.
A. Miura, et. al., thal03, IBIC2016, Barcelona, Spain, Sept., 2016