## Slide 1
Ming-Jen Yang
Friday 9:00 am Meeting,
April 13, 2018
Machine status

## Slide 2: NuMI

## Slide 3: Muon

## Slide 4: SY

## Slide 5: MI downtime

## Slide 6: RR Downtime

## Slide 7: Issues
R:KPS1A
  Replaced burnt out connector on Saturday.
  Changed out trigger board on Sunday.
I:KPS4A
  Backterm 2 was out, for about 30 minutes.
  Inspected kicker cabinet, on Monday afternoon.
Toroid re-calibration
    I:TOR806, found 4.7% high.
    R:TOR853, found 1.3% low.
E9 cycle 2.5 MHz RF
  Add fan cooling to feed-forward board.
Looking for opportunistic downtime
    4 house access to MI
    To hipot upper bend bus penetration at MI60

## Slide 8: Studies
Past studies
  1.2 sec fast ramp.
  RR dispersion function measurement.
  RR E9 beam loading compensation.
Study requests
  1.2 sec fast ramp.
  MI TBT lattice measurement
    8-GeV.
  RR TBT lattice measurement