## Slide 1
Dual Phase Photon Detection System
Installation Plan
Burak Bilki
Inés Gil-Botella
Dominique Duchesneau

## Slide 2
Baseline Parameters of DPPD
Cryo size: 12 m x 60 m x 12 m
720 Hamamatsu R5912-MOD20 PMTs at the density of 1 PMT/m2 (+ 80 spares)
HV granularity: 24 channels/module (SHV connectors)
Positive HV with external splitter so, 1 cable/PMT | RG303/U cold; HTC 50-3-2 warm
Flange size: ~250 mm diameter
SHV density: ~ 1/(3 cm x 3 cm)
1 flange/24 SHV and 4 fiber SMAs feeding 24 PMTs
The basic unit of PD is 24. Let us call this a “sector”.

## Slide 3
Each sector covers 4 m x 6 m  30 sectors, can be named N1…15, S1…15 (for North and South), PMTs on square grid within the sector
Cabling: Bottom trays to sides, then up to the feedthroughs. 1 HV module/sector. 30 feedthroughs 30 flanges along the 60 m edge.

## Slide 4
Higher PMT density scenario: 1 PMT/0.75 m2, total 960 PMTs
Each sector covers 3 m x 6 m  40 sectors, can be named N1…20, S1…20 (for North and South), PMTs on square grid within the sector or in custom arrangement based on detailed cathode geometry
Cabling: Bottom trays to sides, then up to the feedthroughs. 1 HV module/sector. 40 feedthroughs 40 flanges along the 60 m edge.

## Slide 5
Equipment Transportation
The dirty transport boxes are unpacked
Empty boxes are prepared for return to the surface
Waste is packaged to return to the surface
Equipment is moved to the cleanroom.
Equipment is moved to other underground areas.

## Slide 6
Underground Clean Room Operations
The supplies for the cleanroom are responsibility of UIT (Underground Installation Team)
The cleanroom is cleaned by UIT
Equipment is moved into the cleanroom by UIT
Equipment is unpacked by DPPD
Visual inspection and testing by DPPD
Carts to move equipment in the cleanroom are provided by UIT
Specific tooling to handle detector components are provided by DPPD
Storage space in the cleanroom is coordinated by the UIT.
Basic rigging equipment is provided by UIT

## Slide 7
24 PMTs = 1 sector
  EUR1 pallets (800 mm x 1200 mm) can carry 27 PMTs at a time (9 PMTs in 3 rows)
   3 pallets/trip (3 sectors + spare PMTs /trip)
  PMT installation (per sectors) will be coordinated with the schedule of the other subsystems. The ordering of the installation in sectors will follow:
  Field cage/side wall installation
  Feedthrough installation
  CRP installation
  Cathode installation + ground grid (to be lifted after assembly)
  Removal of the false floor / Access to the membrane floor
  PMT installation
  Lowering the ground grid
Underground Operations

## Slide 8
The current DPPD installation schedule is from October 2024 to July 2025 (10 months).
  3 sectors/month (18 PMTs/week) ~ 5 PMTs/shift @ 4 shifts/week (depending on cabling and number of people underground)
  Cable trays will be installed starting October 2024. The exact schedule will be coordinated with field cage and flange installation.
  PMT support base structures will be installed on the membrane in accordance with the PMT installation schedule.
  Cabling options:
    Cables and fibers will be routed from the feedthrough to the bottom (and then connected to a short cable soldered to the PMT base)
    If enough space between cryostat wall and field cage, cables and fibers can be routed from PMTs to the feedthrough (no need for intermediate connectors)
  The installation will be signed off in sectors.
  There will be one DPPD installation supervisor.
Underground Operations

## Slide 9
Cryostat Roof Operations
Installation procedures with necessary stay-clear envelopes for DPPD equipment are to be developed by DPPD
If tooling is needed for installation it is the responsibility of DPPD and must include all procedures and safety approval.
DPPD equipment to be installed will be transported to the work location by DPPD
The installation schedule of the splitters and relevant cabling will follow the schedule of PMT installation (October 2024 – July 2025). Once a sector installation is signed off, it will be tested
There will be one DPPD roof operation supervisor.