## Slide 1: Fermilab LLRF Systems Architecture and Overview
B. Chase/P. Varghese
Fermilab LLRF Systems
17 April 2017

## Slide 2: LLRF System Architecture
AcNET Interface – requestor
Front-end software - director
  User interface
  Scenario execution
Shared Libraries – workers
  Software – logger, event, cog,…
  Hardware – link, VXI-UCD, VXI
DSP Software – serfs
  Patterns
VXI Module Hardware
  40 MHz AD-SHARC™ DSP
  ADCs, DACs, NCOs, Link ports
CA Client
CA Server
Drivers
IOC
EPICS

## Slide 3: Front-End Software
The “application program” or *.exe file (VxWorks)
  Provides set of services or tools to end-user.
  Coordinator of tasks within front-end by combining services provided by different modules.
  Responds to IRQs, TRIGs or external requests for data.
  Error detection, logging and recovery.
Basic Control System Interface – devices (PV)
Advanced Control Interface – I6/R6
  Scenarios - UseManager, Multi-timer

## Slide 4: VXI Module Software
DSP Software Patterns
  Vector Interrupts
  Link Port Communication
  Scheduler
  Fast Time Plot Variables (PV)
Object Based Methodology
  Construction
  Configuration
  Information
DSP Software
Shared Library
Slot 0 level
Hardware DACs, ADCs, etc.
FPGA
Actuators / Detectors
beam

## Slide 5: Software Modules
AN (Channel Access Server)
  Acnet interface, callback mechanism
Event
  Observer pattern or Publish-Subscribe model
Logger
  Message queue used to log error messages
  Different message levels, information content
Cog
  manages cogging beam to specific RF buckets
  Details of cogging hidden, interface clear

## Slide 6: DSP Software
Multiple processing rates
  100 kHz, 16.6 kHz, 720 Hz
Common software patterns
  Scheduler – schedules work tasks
  Vector Interrupts – slot 0 to DSP interface
  FTP Variables – accelerator data variables
  Link port communication - high speed data transfer between multiple modules.

## Slide 7: MILLRF Front End Software
Construction and Configuration
I6 PA Interface
  Use case scenarios
  Multi-timer and UseManager
Middleware
  Gather resources to accomplish tasks, i.e. feedback state changes, machine transfers
  Use interface of lower level libraries
Parameter Page Devices
  Readings/Settings
  FTP Variables

## Slide 8: I6 Primary Application

## Slide 9: MILLRF LLRF VXI Crate

## Slide 10: Booster, Recycler and Main Injector

## Slide 11: Recycler/Main Injector LLRF Systems

## Slide 12: Recycler/Main Injector LLRF Systems

## Slide 13: Main Injector Feedback Loops

## Slide 14: LEL LLRF System

## Slide 15: LEL LLRF Station

## Slide 16: MFC FPGA/DSP Board

## Slide 17: FAST LLRF System

## Slide 18: FAST LLRF Station

## Slide 19: PIP-II IT LLRF System

## Slide 20: PIP-II IT LLRF Racks

## Slide 21: SOC MFC Overview

## Slide 22: ARRIA10 SOC MFC Overview