## Slide 1: Muon Campus Status
Jim Morgan
Weekly Status
May 11, 2018

## Slide 2: Beam to g-2 this week
Beam from Recycler
g-2 T0 Detector
Decay Positrons
Delivery Ring
Trolley Run/Slow dump/Trolley Runv
g-2 Kicker
KRF5/Trolley Run
KRF5
g-2 kicker
Trolley Run/MI Access
g-2 Kicker

## Slide 3: Protons on Target

## Slide 4: G-2 Experiment summary
Surpassed BNL!

## Slide 5: In the past week
Decent up time and muon delivery this week
Gathered data to pinpoint source of poor transmission on cycle(s) after SY120
Nuisance EKIK trips on a Thyratron prefire indication
  Added to permit loop to make sure it’s noticed
I:HVF11 has significant 180 Hz ripple
  Appears to be source of varying positions on 8 transfers
Noisy dump water flow interlock jumpered
  Redundant pressure and temperature interlocks still active
Switched M1 trims from ramped to DC operation
Limited upstairs work planned during today’s MI access

## Slide 6: Sharing P1 and P2 Lines with SY120
P1 and P2 Lines are shared between g-2 and SY120
  Can’t run both concurrently
  SY120 operates at 120 GeV, g-2 beam to target is 8 GeV
Two “switch” magnets powered for g-2, not powered for SY120
  V703 is at the junction of the RR to P1 stub and the P1 Line from MI
  F17B3 is at the junction of the P2 Line and M1 to g-2 and P3 to Switchyard
The R:V703 and I:F17B3 power supplies can’t ramp up fast enough to allow all possible cycles to be sent to g-2
  Three cycles are lost after SY120 cycle
  Beginning of SY120 spill can be affected by decaying tail of R:V703 and I:F17B3
MI SY120 cycles is 5.5 seconds, NuMI/g-2 cycles 1.4 seconds
  Expected to lose 4 cycles when SY120 runs (4/43 = 9.3%)
  Currently go from 43 to 36 events in TLG when SY120 runs (7/43 = 16.3%)

## Slide 7: Beam Path to Muon and Switchyard
Recycler
P1, P2, M1
M2
M3
Delivery Ring
M5
M4
AP0
target
hall
AP30
AP50
AP10
Mu2e
MC-1
(g-2)
P3
F17B3
V703

## Slide 8: SY120 Effect
I:F17B3, bends beam
From P2 into M1
16 bunch operation March 22
SY120 cycle
Spill to Switchyard

## Slide 9: Unexpected SY120 Effect
There is also a loss of yield on (mainly) the first g-2 cycle after SY120 cycle
  First g-2 cycle is down about 50%, next several have minor loss of flux
Beam measurements seem to exonerate everything
  BPM’s look the same, wires show the same positions and beam widths
  Wires in (secondary) M2/M3 Lines show lower intensity and shifted horizontal position, Ion Chambers show lower intensity
  Creating gap in TLG of the same size as SY120 event doesn’t change Target Station performance
Have a study plan that explores the event spacing with and without SY120 more thoroughly

## Slide 10: SY120 Effects
Beam in Delivery Ring
Main Injector ramp
SY120