## Slide 1: Muon Campus Status
Jim Morgan
Weekly Status
May 18, 2018

## Slide 2: Beam to g-2 this week
Beam from Recycler
g-2 T0 Detector
Decay Positrons
Delivery Ring
g-2 Kicker repair and recovery
MI Abort Vacuum
Trolley Run
Momentum Scrapers
retracted
g-2 kicker
g-2 quad problems
Congressional Tour
g-2 kicker problems
Trolley Run
Accelerator
Studies
I:LAM41 & MI access
MI Abort Vacuum
g-2 kicker problems

## Slide 3: In the past week
Down three days due to g-2 kicker repair
Accelerator studies on Monday
  RR to Target dispersion measurements
  Development of 3.1 GeV to 8 GeV mode changes
  Second day of studies planned, but MI abort vacuum access occurred
Work on EKIK due to thyratron prefire trips
  Thyratron pre-trigger circuit modified
  All kickers added to permit loop to inhibit beam when they trip
I:HVF11 has significant 180 Hz ripple
  Still trying to get experts significant time to troubleshoot
Some vacuum issues in Delivery Ring
  BV209 has worsening leak each time it’s cycled
Working on getting more g-2 parameters into ACNET

## Slide 4: Protons on Target

## Slide 5: G-2 Experiment summary
101.6% Last Friday

## Slide 6: Plan
Primary short-term goal is to concentrate on maximizing g-2 data taking with existing rate of muon delivery
  Accelerator studies will be parasitic or coordinated with experiment downtime
  Maximize up-time, accesses only for repairs
Parasitic studies
  Understanding and mitigating lower efficiency cycles after SY120 (improved)
  Improving yield from Target Station (without turning up lithium lens)
  General tuning to maintain or improve current muon delivery
More destructive studies
  Dispersion measurement in primary beamlines (Done)
  Software improvements for mode changing between 3.1 GeV and 8 GeV
  Delivery Ring 8 GeV proton tune measurement
  “Straight-through” muon storage studies to quantify Delivery Ring efficiency
  Beam intensity to end of M5 with 1, 2, 3 & 4 turns in the Delivery Ring
  3 turn proton removal

## Slide 7: SY120 Effect before and after M:HT107A ramp fixed
SY120
SY120