## Slide 1
Window temperature rise, 325 MHz coupler
S. Kazakov
05/31/2018

## Slide 2
9.4 kW, TW
90 K
35 W/(K*m2)
5W/(K*m2)
Boundary conditions around are adiabatic: dQ = 0
Loss tangent of ceramics is 5E-4. Total loss in ceramics is ~ 2W (for 10 kW, TW)
Boundary conditions and losses in ceramics.
Emis = 0.8
Emis. = 0.1

## Slide 3
 | P = 0 | P = | dT
Simulation | 276.3 | 283.7/ 4.7 kW, TW | 7.4
Measured | 276 | 283.3 / 2.2 kW, full Rf. | 7.3
Simulation and measurements
Temperature at window flange

## Slide 4
P = 0 kW

## Slide 5
P = 0 kW

## Slide 6
Average window temperature ~ 277.5K
Temperature along radius in the ceramics, P = 0 kW

## Slide 7
P = 4.7 kW

## Slide 8
P = 4.7 kW

## Slide 9
Temperature along radius in the ceramics, P = 4.7 kW, TW
Window temperature rise dT ~ 7.5 K
Average window temperature ~ 285.0K