## Slide 1
Alex Chen
Final Design/Procurement Readiness Review for the PIP-II MEBT kickers
2 August 2018
MEBT 200 Ohm Kicker Mechanical Design

## Slide 2: Outline
Specification & requirement
  Tolerances
  Cooling
  vacuum
Mechanical Design
  Mechanical
  Material choice
  Vacuum seals
  Brazing, Winding, laser welding,
  Assembling
  QA/AC
Analyses and Tests
  Thermal/Cooling/Vacuum
Summary

## Slide 3: Specification & Requirement
Function Requirement(mechanical):
Insert Length (flange-to-flange): ≤650 mm
Effective electromagnetic length: ~500 mm
Vertical gap:
  16mm±0.5 between opposite electrodes
  13mm± 0.5 in protection electrode
Protection electrodes
Temperature ≤ 100C on helix due to epoxy(-60~130C)
Vacuum:
Self-sustain better than 1E-7 torr
UHV compatible
Low particulate practice not required.

## Slide 4: Specification & Requirement (helixes)
Item | Parameter | Value | Units
 | Helix |  | 
1 | #13 flat magnet wire dimensions, nom. (w x t) | .105 x .042 | inches
2 | Number of helical turns | 47.5 | 
3 | Pitch (p). Tolerance of each turn location is with respect to the reference (one end of the ceramic spacer). | .412 ±.002 (10.46 ±.050) | inches (mm)
4 | Helix wire height above ground in the central section (h) | .240 ±.002 (6.10 ±.05) | Inches (mm)
5 | Copper tube central section OD (the helix “ground”) | 1.116 ±.003 (28.35 ±.1) | Inches (mm)
6 | Central section tube length having the OD value stated in item 4 | 18.746 ±.01 (47.615 ±.03) | Inches (cm)
7 | Copper tube stepped-end OD at both ends, see Physical Requirement 4, below, and Figure 3. | . 800 ±.002 (20.32 ±.050) | inches (mm)
8 | Helix length, measured between wire centers where wire is clamped at both ends (47.5 turns) | 19.570 (501.4) | inches (mm)
9 | Approximate Microstrip wire total length, 47.5 turns | 263 (6.68) | inches (m)
10 | Helix diameter, microstrip wire center-to-center | 1.638 | inches
11 | Electrode dimensions (copper or bronze) | .300 ±.002 x .7874 ±.002 x .020 (7.62 ±.05 x 20 ±.05 x .508) | inches (mm)
12 | Ceramic spacer thickness, (thickness is 1/8 in. nom.) | .136 ±.002 (3.45 ±.05) | Inches (mm)
13 | Ceramic spacer dielectric constant | 5.9 ±.2 | 
14 | Ceramic spacer thermal conductivity, minimum | 50 | W/m/K
15 | Space between facing helix electrode surfaces of the two parallel helices | .630 ±.02 (16 ±.5) | inches (mm)
16 | Minimum space between helix wire and enclosure surface—top, bottom and sides | 2.5 (63.5) | Inches (mm)

## Slide 5: Specification & Requirement
6W electrical power dissipates along the helix.
40W steady state beam absorption
20J of accidental beam loss
Heating Estimates
(Helixes, cont.)
 | 200 Ohm Interconnecting Microstrip Transmission Lines |  | 
17 | Signal wire size | #16 solid round wire (dia. = .051 in.) | 
18 | Signal wire height above ground, wire center to ground surface | .350 ±.005 (8.89 ±.12) | Inches (mm)
19 | Ground strip, copper shim stock; width x thickness | .75 ±.01 x .010 (19 ±.12 x .254) | Inches (mm)
20 | Space between microstrip signal wire and enclosure wall, minimum | 1.0 (25.4) | Inches (mm)

## Slide 6: Mechanical Design
Mechanical
Material choice
Vacuum seals
Brazing, Epoxying, Winding, Laser Welding,
Assembling
QA/AC

## Slide 7: Mechanical Design
ViewPort
Power FT(4)
Cooling FT
FT of Protection electrodes
Pump Port

## Slide 8: Mechanical Design
Beam
Protection Electrode (2)
ViewPort
Power FT(4)
Cooling FT
FT of Protection electrodes
Pump Port
Gauge port

## Slide 9: Materials choices
 | Thermal conductivity (w/m.k) | Thermal Expansion coefficiency (10-6 /°C) | Electrically conductivity (10-6 Ω.cm)
OFHC | 385 | 17.3 | 1.7
6061-T6 | 167 | 23.6 | 4.0
SS 304 | 16.2 | 17.0 | 72
Cu, (OFHC): ground tube, excellent electrical and thermal conductivity
Stainless 304: Base Plates, CF flanges
Alu 6061-T6: for vacuum box, EASY to machine

## Slide 10: Materials(ceramic)
 |  |  |  | Photoveel II (helix spacers) | Macor (stands)
General Properties | Density (g/cm3) |  |  | 2.56 | 2.52
 | Water Absorption (%) |  |  | 0 | 0
Mechanical Properties | Bending Strength (MPa) |  |  | 440 | 90
 | Young's Modulus (GPa) |  |  | 157 | 67
 | Vickers Hardness (GPa) |  |  | 2.3 | 4.5
Thermal Properties | Max.Operating Temperature (°C) (In nonoxidizing atmosphere) |  |  | 1000 | 1000
 | Coefficient of Thermal Expansion (1/°C×10-6) |  |  | 1.4 (RT~400°C) | 6.3-9.7
 | Coefficient of Thermal Conductivity (W/m×K) |  |  | 50 | 1.46
 | Thermal Shock Resistance ΔT (°C) |  |  | 600 | 25-100
Electrical Properties | Volume Resistivity |  | 25°C | 2.2×1015 | >1017
 |  |  | 300°C | - | 
 | Dielectric Constant |  | 10GHz | 5.9 | 6.03
 | Dielectric Loss (×10-4) |  |  | 10 | 
 | Q Factor (×104) |  |  | 0.1 | 
 | Dielectric Breakdown Voltage (KV/mm) |  |  | 35 | 40

## Slide 11: Assembly(F10105856)
Pumping Port
Beamline Port
View Port
Vacuum Gauge Port
Lifting (4)

## Slide 12: Assembly(F10105592)
View Port
Pumping Port
FT of Protection Electrodes
FT of LCW
NEW routing of cooling line

## Slide 13: Base Plate(F10105880)
line to align the base of stands

## Slide 14: Protection Electrodes(F10059185)
NEW:
Doubled thickness to increase cooling
Kapton@MT, and Epoxy
contact area |  |  |  |  | 
Radius | 0.402 | inch |  |  | 
length | 0.52 | inch |  |  | 
Area (90% of half circle) | 0.59 | in2 |  |  | 
Kapton data |  |  |  | Heat | 
thickness | 0.002 | inch |  | 40 | watt
working Temp (cont) | 200 | C |  |  | 
one time | 400 | C |  | dT | 
thermal conductivity | 0.12 | w/(mK) | Kapton | 44.4 | C
 | 0.46 |  | Kapton MT | 11.6 | C
 | 0.75 |  | Kapton MT+ | 7.1 | C

## Slide 15: Ground Tube with Brazed cooling tubing
Positioning Groves

## Slide 16: Ground tube with Ceramic Spacers, (Epoxy)
Ceramic Spacers:
Photoveel II (machinable AlN)
12 identical mid pieces
8 unique end pieces

## Slide 17: Positioning Ceramic Spacers with Epoxy
Ring Clamps
To align spacer-spacer joint
To stay radial
To remain pressure
End Disk
to set longitudinal position,
to keep spacers in radial direction
Ring Clamp
To apply longitudinal pressure
To keep spacers in radial

## Slide 18: Epoxing

## Slide 19: Epoxing
Curing overnight

## Slide 20: Epoxing
Complete epoxying and assembled with end stands

## Slide 21: Epoxing

## Slide 22: Winding Helix
Macor Ceramic End Stands & Clamps
Positioning Key (Ceramic)
Macor ceramic clamps & stands and vented screws

## Slide 23: Winding
Winding setup
Weight to stabilize tension on conduct
Toothed belt driving to synchronize feeding with pitch angle

## Slide 24: Winding setup
10:48 ratio

## Slide 25: Winding
Winding setup
Starts with mandrel pieces clamped

## Slide 26: Winding
Vacuum epoxy KL-320
Thermal Conductivity | N/A
Coeff. of Expansion | 55 x 10-6 cm/°C
Volume Resistivity | @25°C: 6 x 1013 ohm-cm @100°C: 1 x 1010 ohm-cm
Uncured Resin | Milky paste
Tensile Shear | @25°C: N/A
Shelf Life | @Room Temp.: 4-5 mo
Pot Life | @Room Temp.: 30 mins
Cure Cycle (After Mixing) | @25°C: 18hr @65°C: 4hr
Working Temperature | -60°C to 130°C
Apply proper amount epoxy in each notch
Watch conduct carefully when it engages w notch , avoid landing on edges.

## Slide 27: Winding
Remove any excess of epoxy

## Slide 28: Winding
Move mandrel pieces after 6~7 turns

## Slide 29: Winding
Clamp at the end

## Slide 30: Laser Welding Setup
Positioning electrodes on fixture

## Slide 31: Laser Welding Setup
Positioning Helix on fixture
Check again for any excess epoxy on the top of helix conduct where it contacts electrode, remove any excess with knife

## Slide 32: Laser Welding Setup
Adding the Strongback

## Slide 33: Laser Welding Setup
Ready for Laser welding
Check all electrodes to be within their pockets,
Check holes on flat portion of conduct
Check “no gap” in between electrode and helix

## Slide 34: Helix with Electrodes

## Slide 35: Laser Welded Electrode
2 point laser welding
0.02” dia.
Vacuum grade epoxy, remove any excess that will create gap in between electrode and helix conduct
Test piece

## Slide 36: Laser Welded Electrode
2 point laser welding
0.02” dia.
Vacuum grade epoxy
Inspection and
Align for laser
Adjust gas (Argon) nozzle into welding area

## Slide 37: Laser Welded Electrode
2 point laser welding
0.02” dia.
Vacuum grade epoxy
Typical setting

## Slide 38: Assemble Two Helixes on Base Plate

## Slide 39: Measurements of the helix temperature
Suggestion: use a thermal imager, available at EE support (Bob Brooker)
  Fluke Ti32
  temperature range -20°C to +600°C; spectral range 8 to 14 µm
Requires a ZnSe window (0.55 – 18 µm)
  For example, from CeramTec
Check of calibration
  heat up the helix in vacuum with a DC current, using the helix resistance as indication of temperature
  Measure with imager
  Repeat with RF heating

## Slide 40: Bench Test Setup
Driver
Load

## Slide 41: Bench Test Setup

## Slide 42: Bench Test Setup
Load

## Slide 43: Vacuum
Seals:
  metal seals at feedthroughs on SS base plate
  Brazing and welding on water cooling line
  O-Ring on Al Vacuum Box with total permeation 8e-7 torr.l/s
4 ½” Port for IP 100 l/s Pumps to achieve mid E-8 torr without beam
UHV handling with cautiousness of Low Particulate environment

## Slide 44: RGA results (1)
Chart: RGA Scans of Power Test










N2
Residual gases are Hydrogen, Water, and Air
Hydrocarbons are very low, more than 3 decades below.

## Slide 45: RGA results(2)
Chart: Outgassing of 200 Ohm Kicker Half Model Vacuum Test
M2 | 7.0543e-08 | 7.7224e-08 | 7.4707e-08 | 5.9706e-08 | 5.9983e-08 | 6.0421e-08 | 5.458e-08 | 2.4937e-08 | 2.5485e-08 | 2.6602e-08 | 2.6887e-08 | 2.5226e-08
M18 | 6.7599e-08 | 6.5055e-08 | 6.0342e-08 | 4.0717e-08 | 4.0931e-08 | 4.1249e-08 | 3.6639e-08 | 1.6496e-08 | 1.6762e-08 | 1.6619e-08 | 1.7678e-08 | 1.6625e-08
M28 | 2.3919e-08 | 2.5961e-08 | 2.487e-08 | 1.7885e-08 | 1.7993e-08 | 1.8127e-08 | 1.6358e-08 | 7.3654e-09 | 6.9002e-09 | 7.5047e-09 | 7.4475e-09 | 6.9553e-09

## Slide 46: Thermal Test: Temperature Rise (in air)
Water Cooled
Water Stop
Power Off
Water @85F
Room @67F
~50F rise
~4F rise
Vast majority of heat conducted into water

## Slide 47: Thermal test: Temperature Rise (in vacuum)
20A
25A
30A
OFF
Water@86F
Helix
G. Tube

## Slide 48: Vacuum improved over 2 wks
Ambient T
Gauge
Ion Pump

## Slide 49: Kicker Vacuum in Operation
Gauge and Ion pump readings during May 20, 2017-July 18, 2018

## Slide 50: Thermal Estimates
Q=46 watt (40 beam + 6 electrical)
Over 48 (electrodes + turns)
Heat each turn q=46/48=.9 watt
∆T = 11.6 °C for Photoveel II with 10% Cu-Ceramic Contact
Instant temperature rise due to 20J beam loss
∆T=3.1 ° C (uniform on 48 electrodes)
∆T=150 ° C (on single electrode)
Water temperature rise 1.8°C with 0.1 gpm flow rate

## Slide 51: Thermal Estimates
Thermal Caculation on Greg's Kicker |  |  |  |  |  |  |  |  | 
 |  | Dimmenssions |  |  | Material Property |  |  |  | 
 |  |  |  | mm | thermal conductivity |  | conductance per pitch |  | resistance
ceramic strip |  | width | length | height | w/(m.K) |  | w/K |  | K/w
 | inch | 0.125 |  | 0.185 |  |  |  |  | 
 | mm | 3.175 | 500 | 4.699 | 50 |  | 0.28581 |  | 3.50
copper wire | inch | 0.105 | 1.180 | 0.042 |  |  | conductance per quart turn |  | 
 | mm | 2.667 | 29.98 | 1.067 | 385 |  | 0.0365 |  | 27.4
coil |  | pitch (mm) | diameter(inch) |  | turns |  |  |  | 
 |  | 8.46 | 1.503 |  | 48 |  |  |  | 
Heat(watt) | total resistance per turn |  |  | contact |  | DT (K) |  |  | 
46 | R for 4 contacts | 2.6 |  | 100% |  | 2.5 |  |  | 
 |  | 4.3 |  | 50% |  | 4.1 |  |  | 
 |  | 7.7 |  | 20% |  | 7.4 |  |  | 
 |  | 12.1 |  | 10% |  | 11.6 |  |  | 
 | R for 2 contacts | 15.436 |  | 100% |  | 14.8 |  |  | 
 | C for 2 contacts | 0.06478 |  |  |  |  |  |  | 
flow rate of LCW (gpm) | 0.1 |  |  |  |  |  |  |  | 
dT of water in C | 0.0 |  |  |  |  |  |  |  | 
electrode volume (mm3) | 38.7 |  |  |  |  |  |  |  | 
density (g/cm3) | 8.96 |  |  |  |  |  |  |  | 
mass (g) | 0.35 |  |  |  |  |  |  |  | 
specific heat (j/gk) | 0.385 |  |  |  |  |  |  |  | 
instant heat (J) | 20 |  |  |  |  |  |  |  | 
instant dT uniform | 3.12 |  |  |  |  |  |  |  | 
instant dT on single | 149.8 |  |  |  |  |  |  |  | 
DT between electrode and ground tube
Photoveel II

## Slide 52: Thermal Estimates
Macor

## Slide 53: QA/QC
Visual inspections on receiving, during assembling
tests
  Vacuum,
  pressure
  thermal

## Slide 54: Summary
FRS has been met on prototype
Drawings and procedures established
Prototype fully tested