## Slide 1
Greg Saewert
Chopper Review Meeting
2 August 2018
PIP2 MEBT Kicker Review

## Slide 2: Outline
Requirements overview & system design approach
Challenges
Design details
Electrical performance results
Issues to be addressed

## Slide 3: Kicker Requirements
Kick individual bunches (bunch-by-bunch)
Rise/fall time 4.0 ns (5-95%) maximum between bunches
  This leaves 2.15 ns flattop to both kick and pass
Kicking scheme
  +/- 500 V to kick beam out, 0 V to pass
Kick an arbitrary pattern for Booster delivery (at 20 Hz)
  45 MHz average switching rate during 550 ms macro-pulse
  0.5 MHz overall average switching rate
Beam test modes
  81.25 MHz switching rate for 10’s of ms, at 20 Hz
  Any arbitrary pattern having switching rates <81 MHz and <0.5 MHz average

## Slide 4: Kicker System

## Slide 5: Overview – the Helix
Dual 200 Ohm helical, traveling wave structure
  200 Ω (as opposed to typical 50) lowers drive current and power making fast switching conceivable
    <<10 Watts RF skin effect losses in the vacuum
  Symmetric and broadband structure
    Potentially low internal reflections
Thermal design
  ~0.1 gpm water-cooled ground tube for 40 W beam loss
Includes protection electrodes
Challenges
  Match propagation to beam velocity
  Reflections
    Discontinuities between helix, 200 Ω strip lines and load
  Frequency dependent effect (referred to as “dispersion” )
    Cause: inter-winding coupling and winding capacitance to ground

## Slide 6: “Dispersion” Effect
Low-side Switch Pulse
High-side Switch Pulse
“Dispersion” effect
circled in RED
Low-side Switch Pulse
High-side Switch Pulse
“Dispersion” effect is circled in RED
Influence on the beam is an integration: ½ of the peak voltage shown

## Slide 7: Addressing the Helix Design Challenges
Propagation time is matched to beam beta by a tuning procedure
  Both prototype helices were tuned to -0.5% of ideal
Reflection issues
  Microstrip lines in and out are designed for 200 Ohms
    Feed-through to strip line to helix reflections are low
  Helix low impedance end-effects cause reflections
    Coupling between windings raises strip line impedance from ~140 to 200 Ω … but the turn at each end lacks the coupling
    Modeling used to find suitable compensation scheme
    Ground tube stepped 1-turn, both ends, raises impedance
    Reflection reduced about 30%
  Load reflection can be compensated with small series inductance
  Switch-driver close to feed-through (and no coax) reduces reflections
Dispersion effect reduction
  Helices are located away from ground surfaces by 1.75”
  Helix dimensions were chosen to be slightly faster than beam beta
  Adding inter-winding capacitive plates provides compensation
  Compensation decreases dispersion and increases propagation time
    Integrated value of dispersion voltage peaking reduced to <5%

## Slide 8: Overview – Helix Drivers
Kicker drivers are fast switches
  One single-switch driver per helix, opposite voltage polarity
Apply ±500 V to kick beam out, 0 V to pass
Switches are series-connected FETs to share switching losses
  Total switch switching loss from Cds, 3 FETs in series:
Switch construction
  Each switch fully isolated
  Each FET is individually gated simultaneously
Driver design challenges
  Switch on and off fast enough
  Custom FET gate driver required for this switching speed
  Determine FETs reliability to handle thermal cycling
  Handling switching losses for Booster requirement
    1 mJ switching loss per cycle – capacitive switching loss
    45 Watts are dissipated per FET at 45 MHz rep rate

## Slide 9: Addressing the Driver Design Challenges
Photonics laser and transmitter provides precision triggering
  The generator signal gates laser
  Splitters deliver triggering to all FETs simultaneously to photo detectors on each GaNFET driver board
Switching speed is obtained using GaN FETs (GaN Systems, Inc.)
  GS66502B: 7 Adc, 15 A pulsed; 650 V; 20 pF d-s, 65 pF g-s
  GaNFET driver circuit kept as small as conveniently possible minimizing parasitics
Custom FET gate driver circuit designed with operating margin
  Turn-on time is settable to <2 ns
  3-FET switches operate at 500 V above 90 MHz; and 81.25 MHz at 600 V
  A Calibration procedure used to match FET timing
    Both turn-on and -off delay are matched to +/-100 ps
    Allowance remains for shifts due to time and temperature

## Slide 10: Addressing the Driver Design Challenges (cont.)
FET reliability test: 3-FET switch was operated for 4 months 24/7
  500 V bias, 45 MHz for 550 ms at 20 Hz (Booster ave. switching rates)
  No evident timing variations
  Demonstrates GaN FETs are not overly stressed
Turn-off time reduced to <4 ns with compensation:
500 V on the plate assumes 100% efficient kicker
  Helices are 95-97% efficient
  3 V drop in the switch
  Required bias voltage is ~528 Vdc
  Our present limit is 500 Vdc bias voltage
High-Side Switch
Low-Side Switch

## Slide 11: Helical kickers
Load
Compensation
Water
Line
200 Ω Strip
Lines

## Slide 12: Dual-Helix Assembly
Strip line Construction
Dispersion compensation:
capacitive plates

## Slide 13: LLRF’s Arbitrary Waveform Generator
1’s/0’s in a file define kick/pass switching pattern are downloaded to the Generator
Phasing as well as turn on/off edge adjustments can be set with ~40 ps resolution
The arbitrary 550 ms Booster pattern was used at PIP2-IT:
The Arbitrary Kicking Pattern
The File

## Slide 14: Electric to Fiber Transmitter & Switch
Laser
SOA Driver
Laser optical
power
controller
Semiconductor
Optical Amplifier
6 dB
Optical
Splitter
1550nm optical pulses
Electrical
pulses
ARB Pulse
Generator
Photonic transmitter
-600 V Switch
Temperature controller
Photonic
receiver
Photonic
receiver
Photonic
receiver
Driver
& FET
Driver
& FET
Driver
& FET
3 dB
Optical
Splitter
RG-114 coax
To the + 600 V splitter and switch
To the kicker’s lower helix
-600 V
200V
200V
200V
LLRF

## Slide 15: Photonic Transmitter Chassis
Photonic transmitter:
0.6 V TRIGGER INPUT
1550 nm OUTPUT

## Slide 16: GaNFET Driver Circuit
Photo detector
1 GHz opamps: gain (x2)
280 MHz comparator
Detector Stage
Delay Tuning Stage
Turn-on &
Turn-off
delay adjustment
GaNFET Gate Driver
Common source +
source-follower circuit
GaNFET Driver Circuit PCB
Shields not installed
size: 2.5” x 1.75”

## Slide 17: GaNFET Driver Circuit: AC/DC Power
3.5 V, 500 kHz AC in
3 Well-regulated DC voltages out

## Slide 18: The Switch-Driver Chassis (Photonic Gate Version)
This Version has two switches +/- 600 Volts, in one chassis. Coax cables connected outputs to the feed-throughs.
Driver Cards
FETs
(3)
185 Ohm Coax Out

## Slide 19: Driver as installed now in the MEBT

## Slide 20: Driver as installed now in the MEBT

## Slide 21: First 200 Ohm Chopper Installed at PIP2-IT (Transformer Gate Version)
Drivers
185 Ω Loads
Assembly shown similar to intended final version
Switch Driver assembly bolted to the helix plate

## Slide 22: Switch performance
Switching at 81 MHz, 10 us bursts:
600 Vp-p, 4 ns / div
Switching at 45 MHz average rate for 600 us:
600 Vp-p, 100 us / div

## Slide 23: ±500V Bias at 81.25 MHz, 20 Hz Repetition Rate
Individual Helix Waveforms
Differential voltage
Photonics triggered driver version as operated at PIP2-IT

## Slide 24: ±500V Bias, Arbitrary Pattern

## Slide 25: Switching 1100 V, 45 MHz for 600 ms at 20 Hz
Horizontal:
100 μs /div
Vertical
≈ 220 V /div
Simulated beam bunches
Upper Helix
Difference Voltage
Lower Helix
Transformer-triggered Switches

## Slide 26: Switching at 81.25 MHz, ±600 V; kick every other bunch
Amplitudes are consistent up to 40 ms bursts at 81.25 MHz
Through-voltages
Horizontal:
10 ns /div
+1200 V
+600 V
-600 V
Simulated beam bunches
Vertical
≈ 220 V /div
Upper Helix
Difference Voltage
Lower Helix
Transformer-triggered Switches

## Slide 27: Switching at 40.625 MHz, ±600 V; kick 2 pass 2
End of pulse train
showing low reflections
Horizontal:
20 ns /div
Through-voltages
+1200 V
+600 V
-600 V
Vertical
≈ 220 V /div
Upper Helix
Difference Voltage
Lower Helix
Transformer-triggered switches

## Slide 28: Remaining Design Issues – all straight forward
Design MEBT Kicker instrumentation interface
Upgrade GaN FET gate driver stage
Improve GaNFET PCB layout
  In-line not in a loop
Mount switch driver circuits against the feed-throughs
  No coax
Design mechanical mounting
  Drivers
  Loads
Address operating voltage limitation
  Operating voltage now limited to 500 Vdc

## Slide 29: Upgrade GaN FET Driver Stage
Detector Stage
Delay Tuning Stage
GaNFET Gate Drive Stage
LMG1020 GaN FET Gate Driver
0.4 ns Trise/fall into 100pF
1 ns pulse width
7A source, 5A sink currents
60 MHz CW rep rate
Eliminates inductor performance compromise
Circuit power reduced from 1.25W to 0.1W
  Forced-air cooling needed to prevent turn-on and –off timing shifts
Enables reducing PCB size & decrease Driver Circuit parasitics-to-everything

## Slide 30: Operating Voltage Limitation
Problem is an average power dissipation issue
  Operating voltage envelope sags during the 550 ms
FET gate threshold voltage is temperature dependent
  Junction temperatures are not matched
  FET timing diverges at junction temperatures about 70 ºC (absolute)
Switches do not break; FETs recover

## Slide 31: Cooling enhancement options for >530 V operation
5% added to 528 V = 550 V providing desirable margin
Option 1: build 4-FET switches instead of 3-FET
  Total switch power dissipation remains roughly the same
  Per-FET power dissipation would be less
Option 2: mount GaN FETs on AlO2 ceramic substrate
  Cost estimate is ~$1800 for 10 substrates
Option 3: improve cooling on existing G10 PCB
  Increase air flow rate
  Added small radiators on PCB bottom side

## Slide 32: Summary
A 200 Ω kicker lowers power dissipation everywhere and made it possible to develop a switch-driver and achieve bunch-by-bunch chopping
  Even for only Booster delivery with its 550 ms macro bunches, 0.5 MHz average rep rates
  Current helix design will simply be replicated for two kickers
Both switch driver versions operated with beam at PIP2-IT demonstrated inherent multi-FET switch capabilities:
  Switching speed to kick and pass bunch-by-bunch
  Operation at and above 500 Vdc bias
  To switch at Booster average 45 MHz switching rate
  Operation at 81.25 MHz for 10’s of microseconds at 20 Hz
Photonic trigger system proved crucial
  Allows delivery of the arbitrary waveform for Booster injection
  Provides fine temporal adjustment of on/off delay as well as pulse width
4-month test proved GaN FET reliability despite junction thermal cycling
There are a number of options to improve cooling and allow operation >530 Vdc bias

## Slide 33: Acknowledgements
Management
  Sasha Shemyakin, et al.
  Dan Wolff, Chris Jensen
Engineering contributions
  Daniil Frolov
  Alex Chen
  Howie Pfeffer
  Mohammed
  Brian Chase
Technical assistance
  Jeff Simmons
  Kevin Roon
  Dave Franck
Vendors
  GaN Systems, Inc.
  Gary James, elabinc@mtnhome.com
  MPF Products, Inc.
  JFW Industries, Inc.

## Slide 34
END

## Slide 35: Issues regarding high rep-rate multi-FET switch
Switching losses at megahertz rates dominate FET dissipation
Solution: transition faster (for example: well below 2 ns rise/fall)
  Lowers FET dissipation
  Increases difficulty of setting and maintaining synchronous timing match
Reality of mismatched FETs
  FETs originally timed close (+/- 100ps)
    Tuned for ~2 ns turn-on time (5-95%)
    They will be sharing to a significant degree even if we can measure differences in temp.
  GaN FET rating is 650V
    They won’t break even if grossly mismatched (we’ve demonstrated this)
  Mismatch problem is timing shift not thermal melt-down
    Timing shifts occur at ~70ºC junction
  How many FETs in series to use?
    1 FET or 2 FETs not enough
    3 or 4 both work
Real issue is to provide enough substrate cooling for average power

## Slide 36: Switch turn-on/-off time difference without output compensation
Turn-on = 2.72 ns
Turn-off = 6.58 ns