## Slide 1: Algorithmic Enhancement of Reconstruction
Xin Qian
BNL
Wire-Cell Reconstruction

## Slide 2: Outline
Information content in a LArTPC
Wire-Cell tomographic event reconstruction
Journey to achieve accurate charge determination
  Thoughts on pixel readout
“Many-to-many” TPC cluster/PMT flash matching in MicroBooNE
  Is pixel readout a sufficient solution for high-multiplicity environment?
Summary

## Slide 3: Information Content from a LArTPC
Time Information:
  When charge arrive at anode plane
Geometry information:
  Where charge arrive at anode plane
Charge information:
  How much charge arrive at anode plane
Additional information:
  Particle (e.g. energy deposition should be continuous  connectivity, one of unique features for a fully active detector)
  Positivity (i.e., electrons only drift towards anode plane)
  Sparsity
time
Reconstruction is essentially information processing: converting measured information to particle information (kinematics and type)

## Slide 4: Wire-Readout LArTPC
For pattern recognition
  “Time” is more important than “Geometry”
    Two hits arrive at different time cannot come from the same energy deposition
    Two hits arrive at different wires that do not cross each other cannot come from the same energy deposition
  “Geometry” is probably more important than “Charge”
    Two hits with very different charge measurements may not come from the same energy deposition
    Statement depends on how accurate the charge can be measured
For particle identification and energy reconstruction
  “Charge” is obviously crucial (e.g. e/gamma separation)

## Slide 5: Wire-Cell Tomographic Event Reconstruction
Principle paper: “Three-dimensional Imaging for Large LArTPCs”, X. Qian, C. Zhang, B. Viren, M. Diwan, JINST 13, P05032 (2018)
“Time”
“Geometry”
“Charge”
“Sparsity”
“Positivity”
“Connectivity”

## Slide 6: Principle of Solving: Usage of “Charge”
The goal is to differentiate the true hits from fake ones by using the charge information
  ~ large charge  true hits
  ~ zero charge  fake hits

## Slide 7: L0 vs. L1 Compressed Sensing
The L0 regularization and is NP (non-deterministic polynomial-time) hard
  For the previous example, need to remove 2 out of the 6 possibilities to solve  15 combinations
  Imagine a case of removing “m” from “n” possibilities  n! / (m! (n-m)! )
L1 regularization  reduce computation to O(n k), k: number of zeros in the eigenvalues of matrix “ATV-1A”
Compressed sensing (or the usage of sparsity and positivity) is very powerful and well known in other communities
The procedure is revolutionized by the equivalent L1 regularization
  Candes, Romberg, Tao (2006)
Minimization can be achieved through the “coordinate descent” approach, in which “positivity” can be naturally included. “Connectivity” can be achieved through adjusting values of λ for each xi

## Slide 8: Wire-Cell on MicroBooNE Data
2015, after several hours of running
2018, 3 mins of running
Bee link
Bee link
Advanced algorithms (compressed sensing) significantly reduce the running time
New signal processing chain significantly enhances the efficiencies (thicker lines)
  Getting correct “Charge” is crucial  also for PID and energy reco.
Notes: Significant improvement in SP and … write something … why is better ??? Remove last line, more dots  more hits, high efficiency …

## Slide 9: Outline
Information content in a LArTPC
Wire-Cell tomographic event reconstruction
Journey to achieve accurate charge determination
  Thoughts on pixel readout
“Many-to-many” TPC/flash matching in MicroBooNE
  Is pixel readout an sufficient solution for high-multiplicity environment?
Summary

## Slide 10: Single-Phase TPC Signal Formation and Processing
Non-destructive induction wire plane is necessary for position identification in a detector with wire readout
Induction signal strongly depends on the local charge distribution
True number of ionized electrons
Signal on Wire Plane
Field Response
Signal to be digitized by ADC
Electronics Response
Reconstructed number of ionized electrons
(Charge Extraction)
vq: velocity
Ew: weighting field
q: charge
Ramo theorem
Example
Weighting Potential of a U wire

## Slide 11: Charge Determination: Field Response Function
Point Charge Topology
Parallel Track Topology
Long-range and position-dependent induction effect plays an important role in the signal shape
Without shielding from a grid plane, very long front porch in the induction U-plane signal
Collection plane wires also receive bipolar induction signals
These features are important for the integrated design of charge readout and zero-suppression in electronics
MicroBooNE, JINST 13, P07006
2D Garfield simulation

## Slide 12: Charge Determination: Electronics Response
Observed imperfect response due to “imperfect pole cancellation”
  Significantly reduced in the newer generation of ASICs
Developed a procedure to calibrate out imperfect electronics response in MicroBooNE
JINST 13 P07007 (2017)

## Slide 13: Charge Determination: Electronics Noise
While field and electronics responses are crucial for the accuracy of charge determination (systematics), electronics noise is crucial for the precision of the charge determination (statistics)
In the presence of excess noise, capability of noise filtering would be handy
JINST 12 P08003 (2017)

## Slide 14: Charge determination: ADC nonlinearity
For a cold ADC, a new challenge is the control of nonlinearity and stuck bits (known issues for protoDUNE P1 ADC)
  Not an issue in MicroBooNE using warm ADCs
A software calibration procedure is being developed based on MicroBooNE electronics response calibration
  Minimizing the spread of normalized calibration pulses
Stuck bits at 0
Stuck bits at 63
Overall
Nonlinearity
Local oscillation/jump and double peak

## Slide 15: Charge Determination: Signal Processing
With induced signals, the signal is still linear sum of direct and induced signals
  R1 represents the induced signal from i+1th wire signal to ith wire
  Si and Si+1 are not directly related
The inversion of matrix R can again be done with deconvolution through 2-D FFT  2D deconvolution
MicroBooNE: JINST 13 P07006 (2017)

## Slide 16: Evolution of Signal Processing in MicroBooNE
Drift time
Wire number
~ 2 years of effort
MicroBooNE: JINST 13 P07006/P07007 (2017)
Notes: Move into MicroBooNE … , Ehcho to Chao’s talk …

## Slide 17: Demonstration of Charge Matching  Wire-Cell Tomographic Reconstruction
1D, Old
2D, New
MicroBooNE: JINST 13 P07006/P07007 (2017)
Notes: One set of plots … First time ever in LArTPC to reach charge matching …

## Slide 18: Wire-Cell on MicroBooNE Data
New Signal Processing chain significantly enhances the efficiencies (thicker lines)  continuous energy deposition in fully active detector, which is crucial for the later pattern recognition tasks
2015, after several hours of running
2018, 3 mins of running
Bee link
Bee link
Notes: Significant improvement in SP and … write something … why is better ??? Remove last line, more dots  more hits, high efficiency …

## Slide 19: Induction Plane Signal Processing Challenge for “Prolonged” topology
Though “2D deconvolution” significantly reduce the inefficiency in induction-signal processing, there are still holes in the phase space for very-long induction signal
Drift Time
Wire number

## Slide 20
Quantitative evaluation of the signal processing chain  inefficiency for prolonged tracks (large-angle) track
  4-wire plane proposal for DUNE
Signal Processing Evaluation
MicroBooNE: JINST 13 P07006 (2017)

## Slide 21: Thoughts of Requirements on Pixel Readout
Statistical uncertainty of charge determination
  Control electronics noise  low ENC
  Ability to filter electronics noise is desired  scheme of zero suppression
Systematic uncertainties of charge determination
  Field response
    Scheme of zero suppression, grid plane
  Electronics response
    Uniformity and calibration
  ADC performance
    Nonlinearity and calibration
Charge readout must respect the fully-active detector design
  No gap is crucial for subsequent pattern recognition steps
Signal Processing can benefit collection plane signals as well

## Slide 22: Outline
Information content in LArTPC
Wire-Cell tomographic event reconstruction
Journey to achieve accurate charge determination
  Thoughts on pixel readout
“Many-to-many” TPC/flash matching in MicroBooNE
  Is pixel readout an sufficient solution for high-multiplicity environment?
Summary

## Slide 23: Wire-Cell on MicroBooNE Data
The damage of 10% dead channels can be sufficiently mitigated in the reconstruction for cosmic muons
A set of 3D clustering algorithms is developed based on data events
  Different TPC clusters represent separate physics interactions
MicroBooNE-PUB-tech-note-40

## Slide 24: Clustering and Neutrino Selection
A novel “many-to-many” TPC/flash matching algorithm is developed
~25 TPC objects vs. ~40 PMT flashes
  Combinatorial problem  compressed sensing
Cosmic removal after TPC cluster/ PMT flash matching
Recognized clusters based on 3D event image reconstructed with charge matching
CC νμ candidate
MicroBooNE-PUB-tech-note-40

## Slide 25: Example of CC νμ and νe candidates (all activities)
CC νe candidate
CC νμ candidate
Side view
Top view
Front view
Side view
Top view
Front view
MicroBooNE-PUB-tech-note-40

## Slide 26: Example of CC νμ and νe candidates
CC νe candidate
CC νμ candidate
Cosmic background can be sufficiently rejected with this technique in MicroBooNE
Same technique should benefit protoDUNE, SBND, and ICARUS
MicroBooNE-PUB-tech-note-40

## Slide 27: Is pixel readout an sufficient solution for high-multiplicity environment?
Pixel readout is certainly preferable for a high-multiplicity environment (such as DUNE ND)
  Ambiguity caused by wire-readout may not be sufficiently controlled even after including charge, positivity, sparsity information at extreme high rate in a 3-wire-plane setup
However, for neutrino energy reconstruction, clustering of disconnected pieces (neutrons, low-energy gammas, high energy gammas from πo) are important
  Experience from the MicroBooNE neutrino selection (rejection cosmic activities through many-to-many TPC/flash matching)
  With expected high statistics in a LAr ND, one can explore low-intensity beam spills (e.g. one low-intensity x1/20 spills in every 10 beam spills  lower the event multiplicity in the DUNE LAr ND)
    High-intensity spills can still be used to select simple event topologies

## Slide 28: Summary (I)
Event reconstruction in single-phase wire-readout LArTPCs has been significantly enhanced with implementation of advanced algorithms
  2D deconvolution, sparsity/positivity/connectivity information through compressed sensing, many-to-many TPC/flash matching, L1SP …
Accurate charge determination is not trivial, but essential
Prolonged signal in the induction wire plane still represents a challenge
  Problem can be reduced by adding a 4th wire plane with a different orientation or pixel readout

## Slide 29: Summary (II)
TPC readout design must respect the fully-active detector concept of LArTPCs (no gap  subsequent pattern recognition steps)
Accurate charge determination is the key to judge the success of pixel readout in LArTPCs
  Field response, electronics response, ADC nonlinearity, and electronics noise
  The power of PID and energy reconstruction
Low-intensity beam spill is essential to achieve accurate neutrino energy reconstruction for DUNE ND with a Pixel readout