## Slide 1: Highest Quality Information Extraction From the DUNE Far Detectors: Signal Capture Based on Low-Power Pixels with Free-running Clocks & Charge-Quantized Waveform Capture
David Nygren
University of Texas at Arlington
14 August 2018

## Slide 2: Far Detector Perspective - official
“The two current designs are good enough”
    “The scientific reach is maximized” !
    But, what about unplanned discovery potential?
“The plan is solid and fixed”
    “The time for new or better ideas is over!”
    But, has due diligence been exercised ?

## Slide 3: Far Detector Perspective – nonofficial
“A design with small pixels will be best”
    Does a pixelized TPC really provide better physics?
  Is a pixelized design technically possible?
    Probably yes; then:
      Can a pixelized design be demonstrated timely?
      Is a pixelized design affordable?
      What would a demonstration plan look like?
  “There isn’t time to do it right, but there is always time to do it over.”

## Slide 4: Axiomatic Starting points
  Electronics embedded in LAr forever… (SPF)
  Simplest possible system concept… (Einstein)
  Power dissipation must be ‘low’… (LAr heating)
  Information quality must be ‘optimal’
  follow the electronic principle of “least action”
  System concept is likely unconventional
  Take advantage of intrinsic resource: 39Ar decays

## Slide 5: The Charge Integrate-Reset (CIR)
charge-sensitive amplifier
Schmitt trigger
Reset switch
Input
‘Reset’

## Slide 6: Classical C-I-R Behavior
Current arriving at input is integrated on C
After integrating charge δQ on C, Vth is met
Comparator triggers, closing switch
Capacitor C is discharged, returned to baseline
Cycle begins again, ad infinitum
Classically, trigger augments a counter by one.
Number of counts is proportional to total Q

## Slide 7: The Advanced CIR Block
charge-sensitive amplifier
Schmitt trigger
Reset switch
Input
‘Reset’

## Slide 8: We do something different
38-bit Gray-code counter
38-bit latch
Oscillator
Reset trigger latches the contents of counter–
this action captures local time at instant of reset
~100 MHz
“Local Clock”
runs free
Notes: Oscillator only attached to Gray-code scaler – not distributed within ASIC –minimizes power dissipation

## Slide 9: Now what ?
Take the difference between sequential resets
This is the Reset Time Difference = RTD
Total charge for any RTD = ΔQ
RTDs are not generated at ASIC level;
RTDs are computed off-detector (GPU)

## Slide 10: Now what ?
RTD is a measure of average current
  Small average current (background): Large RTD
    Background current from 39Ar is ~40 aA (very small!)
  Large average current (signal): Small RTD
    Typical track current from min-I is ~1.5 nA
Background and signal are easy to distinguish

## Slide 11: The RTD patterns
Time
Background
Signal
Seconds
µs

## Slide 12: Leakage current
Critical for the success of this approach is that all extraneous leakage currents at the CIR input node are small compared to 39Ar current
At LAr temperatures, can extraneous leakage currents be shown to be <<40 aA ?
The background current from 39Ar decay provides an automatic charge calibration from histograms of RTD (highly bimodal spectrum)

## Slide 13: The Charge Integrate-Reset (CIR)
charge-sensitive amplifier
Schmitt trigger
Reset switch
Input
‘Reset’

## Slide 14: Signal Characteristics
Choose ΔQ such that Min-I track will cause several resets during one track arrival:
  Choose ΔQ = 1 fC
Signal: a contiguous sequence of small RTDs
A conventional current waveform of arbitrary length and complexity can be reconstructed from the RTD sequence.

## Slide 15: In other words…
RTD = inversely proportional to input current
Background: 39Ar decays lead to ‘heartbeat’
  heartbeat RTD ~20 seconds
  natural calibration available – form histograms
Signal: typically a few na,  RTD < 1 µs
  Five or more contiguous small RTDs
  Easy to recognize signal against background!
  No signal differentiation! (unlike induction wires)

## Slide 16: Precision
Remember:
    Charge resolution here is “exactly” δQ
    Time resolution is ~10 ns
The charge pump has good ‘resolution’ for small, short currents, e.g. soft electrons
How much dynamic range is really needed?
    proton decay within Ar  nuclear fragmentation
    not so clear what is needed …

## Slide 17: Waveforms
CIR waveform: varying time intervals between equal charge quanta.
Conventional: varying charges between equal time quanta.
Yuan Mei has performed simulations
  Encouraging!
  Much work remaining!

## Slide 18
180nm CMOS, 2.5V power supply. Front-end consumes 2.2uA current. Noise (ENC) is around 500e-. Schmitt trigger is still ideal (rise and fall time limited). Waveform from Dan Dwyer
Yuan Mei
LBNL

## Slide 19
ΔQ ~1.0 fC

## Slide 20
ΔQ ~0.3 fC

## Slide 21
Simulation of this idea at U Penn – Mitch Newcomer et al

## Slide 22: Time-stamping Waveforms ?
‘Time’ is kept by a local free-running oscillator
The local clock runs freely at f ~100 MHz
  No phase-locked loop
  But local time is unrelated to master clock…
How can a global time frame be established?
Requirement: Local clock must be stable:
  δf/f < 1 x 10–6 per second

## Slide 23: Time-stamping ?
Time-stamping routine:
  Once a second, ask ASIC “What time is it?”
  ASIC captures local time and sends it @ 1Hz
  Simple linear transformation: T = AF/f + B
  F is master clock synched to GMT
But we have seen this before!

## Slide 24: IceCube: Digital Optical Module Block Diagram
FPGA
CPU
CPLD
Flash
Flash
PMT Power
SDRAM
SDRAM
ATWD
ATWD
fADC
DAC
Monitor
& Control
LPF
LC
x16
x2
x0.25
Flasher
Board
Pulser
DACs & ADCs
Corning Frequency Ctl (was Toyocom)
4Mb 4Mb
16Mb
16Mb
+/-5V, 3.3V, 2.5V, 1.8V
64 Bytes
Delay
Trigger (2)
ADC
Oscillator
20 MHz
40 MHz
MUX
(n+1)
(n–1)
DOR
OB-LED
x 2.6
x 9
10b
10b
10b
10b
8b
32b
16b
8b
8b, 10b, 12b
DP Ram
1 megabaud
DC-DC
Configuration
Device
8Mbit
GTP, LBNL, 26 Mar, 2004

## Slide 25: Clocks…
IceCube: ±2 ns rms within 1 km3 of ice!
  works flawlessly and invisibly
Oscillator precision in IceCube is ~1 x 10 –10/s
  hard to measure!
DUNE: ±1 µs precision
  requires δf/f < 1 x 10–6 per second for local clock
  This is probably easy to achieve in LAr
“What works in IceCube can work in DUNE”

## Slide 26: 16-Pixel ASIC
The local clock serves 16 pixels in one ASIC
View from inactive side
Wire-bonds connect
each pixel to ASIC; via connects to small button on active side, minimizing capacitance and noise;
concern: parasitic triggers

## Slide 27
16 x 16 Tile of 256 ASICs, 4092 pixels
Tile size:
~250 mm x
~250 mm

## Slide 28
Local clock interrogation
signal enters at any corner of tile, and propagates as a wave to any neighbor
here…

## Slide 29
Local clock interrogation
signal enters at any corner of tile, and propagates as a wave to any neighbor
Or here…

## Slide 30: ASIC concept
16 pixels/ASIC – could be more, probably
1 free-running clock/ASIC
1 capture register for clock value, ASIC, pixel subset,
Buffer depth as needed to store beam, SN event…
Logic to manage:
  dynamic network,
  token passing,
  clock domain crossing,
  data transfer to neighbor in network
  exception states, including “kill switch”

## Slide 31: The pixel “button”
The pixel must be a small button exposed to LAr active volume, not a space-filling square
The dielectric surface exposed to LAr active volume will automatically ‘heal” to create the desired electrostatics: “all charge to button”
 Dielectric properties of first dielectric surface are important: teflon, …

## Slide 32: The 64-bit datum
Clock value 38 bits
ASIC location 8 bits
Pixel address 16 bits
Flags 2 bits
Total: 64 bits
Datum is always the same format

## Slide 33: Data Flow
Clock calibration: once per second
   16,384 bits/tile
Assume 20,000 tiles/10 kton module
  ~40 MB/s per module
Easily digestible locally by GPU to transform data to global time frame & prepare histograms.
Very little data corresponds to real event data

## Slide 34: No single-point failure ?
Flat architecture avoids clock distribution
Local clock interrogation ‘wave’ sweeps around any dead or troubled ASIC;
Any of edge or corner provides entry point for interrogation and for data recovery.
Wave mode seems fanciful, but I don’t see why it couldn’t work…

## Slide 35: Three Central Technical Issues
CIR Input:
  all extraneous leakage currents at the CIR input node are small compared to 39Ar current
    If not LAr, then a reproducible Ical must be supplied
Clock:
  Must be stable: δf/f < 1 x 10–6 per second
    I think this will be easy… –but at what power level?
Surface Charge Creep:
  Must be negligible relative to 39Ar current
    This can be tested, I think…

## Slide 36: Photon detection ?
Can the pixel surface also detect photons?
Wild speculation: coat surface with a-Se
  a-Se is a photoconductor (old copiers had it)
  VUV photon might liberate free electrons…
  Some avalanche gain will trigger some pixels that are near trigger point.
  Look for clustering of Hits in time  S1 signal
Far-fetched, but would be fabulous if real

## Slide 37: Perspective
IceCube demonstrated that it is rational to embed complex electronics in perpetuity
  care taken in design phase to avoid bleeding edge
  care taken in qualifying parts list
  care taken in fabrication & test
IceCube demonstrated that unorthodox time-stamp method meets high performance goals.

## Slide 38: Summary
The Charge-Integrate-Reset pixel extracts all energy, spatial and time information with high precision and appropriate dynamic range.
Several aspects are just assertions at this point
It seems plausible that an unorthodox scheme to realize a fully pixelized DUNE might work.
I would like to explore this technical approach as “Generic R&D”
Anybody interested?

## Slide 39: Summary
The Charge-Integrate-Reset pixel extracts all energy, spatial and time information with high precision and appropriate dynamic range.
Several aspects are just assertions at this point
It seems plausible that an unorthodox scheme to realize a fully pixelized DUNE might work.
I would like to explore this technical approach as “Generic R&D”
Anybody interested?

## Slide 40: Summary
The Charge-Integrate-Reset pixel extracts all energy, spatial and time information with high precision and appropriate dynamic range.
Several aspects are just assertions at this point
It seems plausible that an unorthodox scheme to realize a fully pixelized DUNE might work.
For me, this is “Why we are here”.
I would like to explore this technical approach as “Generic R&D”