## Slide 1
Title
CAPP-PACE experiment with a target mass range around 10 µeV
Doyu Lee
On be half of CAPP-PACE team
IBS/CAPP, KAIST
3rd Workshop on Microwave Cavities and Detectors for Axion Research
Slide 1

## Slide 2
Outline
Slide 2
Overview
CAPP-PACE(Pilot Axion Cavity Exp.)
  1st run
  2nd run(in progress)
  3rd run
  analysis
R&D and future plans
Summary
Overview
CAPP-PACE
R&D and future plans
Summary

## Slide 3
Slide 3
Axion Detection scheme
(CAPP-PACE)
axion
Virtual photon
photon
Axion Conversion Power (~10-24W):
Signal to Noise Ratio: Scan rate:
Low noise Amplifier
HEMT
or
Quantum limited noise device
MSA or JPA
High Field SC Magnet
8T now and 25T soon
BNL(HTS) Design
High Q Tunable Cavity
Copper split design cavity
Superconducting coating.
Cryogenics
<50mK
To RF Receiver
(Reverse) Primakoff Effect
P. Sikivie’s Haloscope:
Overview
Overview
CAPP-PACE
R&D and future plans
Summary

## Slide 4
CAPP Experimental Hall
Slide 4
Overview
Overview
CAPP-PACE
R&D and future plans
Summary

## Slide 5
CAPP-PACE
(Pilot Axion Cavity Exp.)
Slide 5
What is it?
The Very First complete axion experiment in Korea
First engineering run was done in Jan. 2018 (2.45 ~ 2.50GHz)
  Flawless operation of Freq. Tuning System(sapphire rod with Piezo tuning system)
  DAQ(Controls, Monitoring) is ready
  Target sensitivity : 10*KSVZ
The Second run (2.50 – 2.75 GHz) is running “NOW”
  Improved scanning speed with bigger cavity (x2)
  Improved scanning speed (x4)
  Tuning with sapphire and copper rod
  Fully automated DAQ (Controls, Monitoring and Emergency plan)
  Target sensitivity : 10*KSVZ
The Third run will have focus on ”KSVZ” axions
  Planned for two months, starting September
Quantum Amplifier Testbed
Preparing for CAPP25T
CAPP-PACE
Overview
CAPP-PACE
R&D and future plans
Summary

## Slide 6
The run parameters
Slide 6
parameter | value
Frequency | 2.45 – 2.76 GHz
Magnetic Field | 8 T
Tcavity | < 50 mK
Tamp | 1 - 1.5 K
Cavity Volume | 1.12(0.59) litter
Target Sensitivity | KSVZ, 10*KSVZ
DAQ efficiency | 0.45
Unloaded Q | ~ 80,000
Coupling | 1.5 – 2.0
Form Factor | 0.55
Target SNR | 5
CAPP-PACE
Overview
CAPP-PACE
R&D and future plans
Summary

## Slide 7
Experimental design
Slide 7
RF read-out chain & Controls
CAPP-PACE
Overview
CAPP-PACE
R&D and future plans
Summary

## Slide 8
Cavity & Frequency tuning system
Slide 8
“The first run”
Rotational Piezo
for frequency tuning
Linear Piezo for adjusting antenna coupling
10mm diameter sapphire tuning rod
for 2.45GHz – 2.5GHz searching
CAPP-PACE
Overview
CAPP-PACE
R&D and future plans
Summary
Notes: Mode was clear, thus even don’t need to put graph here. Split design

## Slide 9
Cavity & Frequency tuning system
Slide 9
“The second run” 2.5GHz – 2.6GHz
4mm diameter Cu rod
(Fixed to top and bottom)
“TM010 frequency of φ90mm cavity is 2.55GHz, thus neither conductor nor dielectric rod can searching axion between 2.5 – 2.6GHz.”
CAPP-PACE
Overview
CAPP-PACE
R&D and future plans
Summary

## Slide 10
Cavity & Frequency tuning system
Slide 10
“The second run” 2.5GHz – 2.6GHz
Chart: Angle (deg)
| 100 | 120 | 122 | 123 | 125 | 128 | 130 | 135 | 140 | 150 | 155 | 156 | 157 | 160 | 180 | 190 | 195 | 195.7 | 197 | 200 | 220 | 225 | 226 | 227 | 230 | 232.5 | 234 | 235 | 240 | 260
 | 2.4308 | 2.518 | 2.5248 | 2.525 | 2.5252 | 2.5255 | 2.5256 | 2.5258 | 2.5259 | 2.5257 | 2.5255 | 2.5255 | 2.5255 | 2.5253 | 2.5241 | 2.524 | 2.5238 | 2.5239 | 2.5239 | 2.5238 | 2.5232 | 2.5228 | 2.5228 | 2.5227 | 2.5223 | 2.5221 | 2.5219 | 2.5194 | 2.4969 | 2.3948
 | 2.522 | 2.5248 | 2.5261 | 2.5297 | 2.5372 | 2.5477 | 2.5521 | 2.5536 | 2.5545 | 2.5557 | 2.5563 | 2.5564 | 2.5564 | 2.5567 | 2.5579 | 2.5581 | 2.5582 | 2.5582 | 2.5582 | 2.5581 | 2.5571 | 2.5566 | 2.5549 | 2.5512 | 2.54 | 2.53 | 2.5237 | 2.5218 | 2.5212 | 2.518
 | 2.5445 | 2.5508 | 2.5513 | 2.5515 | 2.552 | 2.553 | 2.5559 | 2.5708 | 2.5843 | 2.6054 | 2.6128 | 2.6139 | 2.6147 | 2.6158 | 2.6163 | 2.6204 | 2.6158 | 2.6177 | 2.6187 | 2.6152 | 2.5742 | 2.5584 | 2.5565 | 2.5564 | 2.5559 | 2.5555 | 2.5553 | 2.5551 | 2.5541 | 2.548
 | 2.5728 | 2.609 | 2.6094 | 2.6083 | 2.6089 | 2.6114 | 2.615 | 2.6138 | 2.6138 | 2.6182 | 2.6146 | 2.6152 | 2.6154 | 2.6188 | 2.6278 | 2.6246 | 2.6204 | 2.62 | 2.6196 | 2.6194 | 2.6147 | 2.6158 | 2.617 | 2.6139 | 2.6127 | 2.6114 | 2.6103 | 2.6105 | 2.6065 | 2.5483
Chart: Angle (deg)
| 100 | 120 | 122 | 123 | 125 | 128 | 130 | 135 | 140 | 150 | 155 | 156 | 157 | 160 | 180 | 190 | 195 | 195.7 | 197 | 200 | 220 | 225 | 226 | 227 | 230 | 232.5 | 234 | 235 | 240 | 260
 | 0.42214 | 0.49011 | 0.071093 | 0.005688 | 0.0009247 | 0.00028049 | 0.00016171 | 8.2188e-05 | 5.4431e-05 | 2.7697e-05 | 2.9554e-05 | 2.47e-05 | 2.2852e-05 | 2.0781e-05 | 1.2184e-05 | 8.5882e-06 | 1.2114e-05 | 9.3415e-06 | 8.0164e-06 | 1.095e-05 | 1.0777e-05 | 1.4615e-05 | 1.6752e-05 | 2.1041e-05 | 3.2389e-05 | 0.00010239 | 0.0014017 | 0.49917 | 0.48503 | 0.40659
 | 6.3709e-06 | 0.0022107 | 0.42819 | 0.49671 | 0.50569 | 0.47385 | 0.10403 | 0.0034142 | 0.00098995 | 0.00027311 | 0.00018538 | 0.0001743 | 0.00016241 | 0.0001359 | 6.1151e-05 | 4.4132e-05 | 3.7972e-05 | 3.5982e-05 | 3.4724e-05 | 3.112e-05 | 1.4478e-05 | 0.010835 | 0.52111 | 0.5319 | 0.51855 | 0.50945 | 0.50237 | 0.00063724 | 1.5584e-09 | 2.0308e-06
 | 0.00021523 | 0.0014821 | 0.0023215 | 0.0030293 | 0.0062337 | 0.050279 | 0.4262 | 0.544 | 0.56178 | 0.58375 | 0.57348 | 0.49911 | 0.035388 | 0.010387 | 0.00016727 | 0.0018175 | 0.005719 | 0.004367 | 0.59711 | 0.59797 | 0.55225 | 0.53161 | 0.017223 | 0.0023451 | 0.00042849 | 0.00024805 | 0.00020408 | 0.00018084 | 0.00012776 | 1.2895e-09
 | 1.9032e-07 | 1.1515e-06 | 3.6153e-06 | 1.4881e-06 | 8.542e-06 | 2.323e-05 | 1.33e-06 | 9.7851e-08 | 2.5693e-05 | 4.3091e-05 | 0.023263 | 0.09471 | 0.55901 | 0.58753 | 0.60712 | 0.60144 | 0.59379 | 0.59433 | 0.00026424 | 0.00019332 | 2.6893e-06 | 3.8968e-06 | 2.0914e-09 | 5.1158e-07 | 2.0841e-10 | 7.7043e-07 | 1.3534e-07 | 2.3337e-06 | 1.7816e-08 | 7.5024e-05
Chart: Angle (deg)
| 100 | 120 | 122 | 123 | 125 | 128 | 130 | 135 | 140 | 150 | 155 | 156 | 157 | 160 | 180 | 190 | 195 | 195.7 | 197 | 200 | 220 | 225 | 226 | 227 | 230 | 232.5 | 234 | 235 | 240 | 260
 | 2.4308 | 2.518 | 2.5261 | 2.5297 | 2.5372 | 2.5477 | 2.5559 | 2.5708 | 2.5843 | 2.6054 | 2.6128 | 2.6139 | 2.6154 | 2.6188 | 2.6278 | 2.6246 | 2.6204 | 2.62 | 2.6187 | 2.6152 | 2.5742 | 2.5584 | 2.5549 | 2.5512 | 2.54 | 2.53 | 2.5237 | 2.5194 | 2.4969 | 2.3948
 | 0.42214 | 0.49011 | 0.42819 | 0.49671 | 0.50569 | 0.47385 | 0.4262 | 0.544 | 0.56178 | 0.58375 | 0.57348 | 0.49911 | 0.55901 | 0.58753 | 0.60712 | 0.60144 | 0.59379 | 0.59433 | 0.59711 | 0.59797 | 0.55225 | 0.53161 | 0.52111 | 0.5319 | 0.51855 | 0.50945 | 0.50237 | 0.49917 | 0.48503 | 0.40659
Chart: Frequency (GHz)
| 2.4307963936430981 | 2.5179907435587001 | 2.5261289217526999 | 2.5297441578402999 | 2.5372155918683998 | 2.5477297710323001 | 2.555852028690599 | 2.5708413126202001 | 2.5842946846713999 | 2.6053748419720999 | 2.6127548724256 | 2.6139492921667 | 2.6154397959806999 | 2.6188350960501001 | 2.6278102861698001 | 2.6245509667845002 | 2.6203921546961002 | 2.6199584722654001 | 2.6187010331943998 | 2.6152470876324001 | 2.5741745208303 | 2.5583939081569 | 2.554860975281299 | 2.5512042615738002 | 2.5399635805926999 | 2.5299600469255998 | 2.5237168843758 | 2.5194361931992981 | 2.496887230564198 | 2.3948162617015001
 | 0.42214 | 0.49011 | 0.42819 | 0.49671 | 0.50569 | 0.47385 | 0.4262 | 0.544 | 0.56178 | 0.58375 | 0.57348 | 0.49911 | 0.55901 | 0.58753 | 0.60712 | 0.60144 | 0.59379 | 0.59433 | 0.59711 | 0.59797 | 0.55225 | 0.53161 | 0.52111 | 0.5319 | 0.51855 | 0.50945 | 0.50237 | 0.49917 | 0.48503 | 0.40659
Frequency | 12987.0804 | 14047.5325 | 15182.0701 | 14361.1771 | 14480.2852 | 15263.7396 | 16253.9771 | 15301.6936 | 15724.4923 | 16514.0231 | 16117.976 | 14162.2073 | 15821.2435 | 16798.9732 | 17663.1095 | 17424.5033 | 17073.1682 | 17117.4941 | 17185.0767 | 17026.8885 | 15544.0644 | 15249.3932 | 15204.46 | 14964.6946 | 14701.0782 | 14510.4544 | 14425.595 | 14333.1733 | 13978.1146 | 13186.0244
19mm
27mm
10mm
C factor
Frequency
Q factor
C factor
CAPP-PACE
Overview
CAPP-PACE
R&D and future plans
Summary

## Slide 11
Cavity & Frequency tuning system
Slide 11
“The second run” 2.6GHz – 2.75GHz
4mm diameter Cu rod
“For searching in this frequency range, we introduced a copper rod.”
19mm
Chart: Angle (deg)
| 79 | 80 | 90 | 120 | 150 | 170 | 180
Frequency 1 | 2.7508 | 2.7463 | 2.7055 | 2.6236 | 2.586 | 2.5767 | 2.5756
Frequency 2 | 2.7559 | 2.7558 | 2.7514 | 2.7249 | 2.7035 | 2.6978 | 2.6971
CAPP-PACE
Overview
CAPP-PACE
R&D and future plans
Summary

## Slide 12
Analysis basic
Slide 12
The first run information
CAPP-PACE (Pilot Axion Cavity Experiment) at 01-19-18 ~ 02-11-18
Total frequency range : 2.457146 GHz - 2.500377GHz
Step size : 16kHz
Total number of spectra : 2847
Cavity bandwidth : ~80kHz
Parameters
-TMXC: 40mK
-Tnoise : <2.5K
-Magnetic field: 8T
-Bore size: 11.8cm
-Cavity volume: 0.59L
-Frequency: 2.45~2.50GHz
-Q unloaded: >90,000
-Low noise amplifier: HEMT (1K noise)
-C (geometrical factor) >0.55
-DAQ Efficiency: 0.45
-Target Sensitivity: 10*KSVZ
CAPP-PACE
Overview
CAPP-PACE
R&D and future plans
Summary

## Slide 13
Data & Analysis
Slide 13
The first run monitor
a
b
c
d
e
f
g
h
CAPP-PACE
Overview
CAPP-PACE
R&D and future plans
Summary

## Slide 14
Data & Analysis
Slide 14
The first run Data combining
If bins
a
b
c
SNR
d
d
e
CAPP-PACE
Overview
CAPP-PACE
R&D and future plans
Summary

## Slide 15
Data & Analysis
Slide 15
Fake Axion
CAPP-PACE
Overview
CAPP-PACE
R&D and future plans
Summary

## Slide 16
Data & Analysis
Slide 16
The second run monitor
CAPP-PACE
Overview
CAPP-PACE
R&D and future plans
Summary

## Slide 17
Data & Analysis
Slide 17
Emergency plan
CAPP-PACE
Overview
CAPP-PACE
R&D and future plans
Summary
”Every single parameter related to experiments is saved to our DB. If emergency situations happen(fridge fail, chiller fail, power out, etc.) , then DAQ script will automatically determine how serious it is and..
1. Let us know
2. Ask to us stop experiment or not
3. Immediate stop and ramp down the magnet

## Slide 18
Data & Analysis
Slide 18
The second run data combining
CAPP-PACE
Overview
CAPP-PACE
R&D and future plans
Summary
Notes: Will be changed to combined data

## Slide 19
The third run - KSVZ
Slide 19
CAPP-PACE
Overview
CAPP-PACE
R&D and future plans
Summary

## Slide 20
R&D and future plans
Slide 20
How to improve?
Maximize B2V
  25T 10cm bore HTS magnet by BNL (2020)
  12T 32cm bore LTS magnet by Oxford (2020)
Higher Frequency
  Multi-cell cavity
Scan faster (minimize Tamp  dominating factor)
  Quantum Amplifier - SQUID or JPA
  Optimize cryo-RF receiver chain
Others
  Improve Q-factor of cavity – pure metal or SC cavity
  Dead-time-less DAQ
Overview
CAPP-PACE
R&D and future plans
Summary
R&D and future plans

## Slide 21
25T magnet by BNL
Slide 21
  25T 10cm bore HTS magnet by BNL
  The first few (of 28) pancakes wound! - tests in progress
  5 km of SC tape will be delivered next 5 months
Overview
CAPP-PACE
R&D and future plans
Summary
R&D and future plans

## Slide 22
Noise temperature measurements
Slide 22
“Y factor method with two different temperature”
Overview
CAPP-PACE
R&D and future plans
Summary
R&D and future plans

## Slide 23
Noise temperature measurement results
Slide 23
Overview
CAPP-PACE
R&D and future plans
Summary
R&D and future plans

## Slide 24
Microstrip SQUID Amplifier
Slide 24
List of SQUID based amplifiers
SQUID from KRISS (Korea)
EZ SQUID (commercial, Germany)
CE1K2 SQUID (IPHT, Germany)
Tested by Dr. Andrei Matlashov
Sergey Uchaikin (from D-Wave) has joined the group in July to lead JPA effort
SQUID Leads
Input Coil Leads
New VC2 SQUIDs from IPHT, Jena
Overview
CAPP-PACE
R&D and future plans
Summary
R&D and future plans

## Slide 25
Introduce MSA
Slide 25
Overview
CAPP-PACE
R&D and future plans
Summary
R&D and future plans

## Slide 26
Timeline(CAPP-PACE)
Slide 26
Overview
CAPP-PACE
R&D and future plans
Summary
R&D and future plans

## Slide 27
Timeline(CAPP25T)
Slide 27
Overview
CAPP-PACE
R&D and future plans
Summary
R&D and future plans

## Slide 28
Summary
Summary
Slide 28
Axion experiment at IBS/CAPP is being carried out successfully.
Major R&D Efforts
  Higher B Field: HTS (18T, 25T…)
  Larger Volume: (12T 32cm LTS magnet)
  Adding MSA or JPA
  R&D for Higher Frequencies ( >10 GHz)
Quantum limited noise amplifier will be ready soon.
25T 10cm bore HTS magnet(BNL) will be ready as early as 2019.
Overview
CAPP-PACE
R&D and future plans
Summary

## Slide 29
Thank You!