## Slide 1: High Rate RPC for mu2e II CRV
Lei Xia
ANL - HEP

## Slide 2: Potential application for mu2e II CRV
Mu2e II challenge for CRV: neutron/gamma background scale with luminosity
  High counting rate due to neutron/gamma, especially in TS region
  Potential higher dead time due to fake veto from accidental coincidences
  Radiation damage to SiPM’s
  CRV readout bandwidth limitation
If we cover the limited hot region with high rate RPC’s
  Mostly immune to neutron/gamma background (eff < 1%)
  Signal similar to SiPM (same readout?)
What is the charged particle rate?
  (~kHz/cm2 ???)

## Slide 3: A rough rate estimate
From Mu2e simulation, in the highest rate region:
  4x di-counter gets average ~10 hits/µBunch, in the live window (~1µs)
  The high rate region is ~200cm long, and di-counter is 10cm wide
  The beam flash creates comparable hits as the in the live gate (say, ~20 hits)
  This is not bad at all!
    A substantial fraction would be neutral particles (not visible to RPCs)
    Hit rate used is for the entire counter
    Rate won’t be even, some region will see higher rates
    Beam variation
    But still, this is probably the upper limit
Supposedly, the Mu2e II will have x10 rate  ~20kHz/cm2
  This is within the limit of current high rate RPC technology
  Knowing the exact charged particle rate would be a great help!

## Slide 4: Efficiency requirement
Assuming 4 layers of RPC
From past experience with glass RPCs
  98% efficiency is achievable for the best chambers (1 gap, avalanche mode)
  >90% can be easily achieved in large scale production (1 gap)
  If very high efficiency is required, 2-gap/layer would be the solution
What is the requirement for the high rate region?
  We learned that in TS region, the CRV efficiency requirement is ~90%
RPC efficiency 2 / 4 veto efficiency 3 / 4 veto efficiency
90% 0.996 0.948
95% 0.9995 0.986
96% 0.9997 0.991
97% 0.9999 0.995

## Slide 5: High rate RPC options: bulk material
Low R glass: Tsinghua U., China
  Obtained sample, tested, good quality, readily available
  Used in timing RPC for real experiment(s)
  >10k/cm2
  Cost: a little bit high
Low R glass: Schott
  Tested samples, commercially available (?)
  > several k/cm2
  Cost: don’t know yet
Low R glass: ANL, COE College development
  Produced samples, tested
  > several k/cm2
Atom Layer Deposition (ALD) coated glass RPC
  New idea, prototype exist
Low R glass sample from COE College
Low R glass sample from Schott
Low R glass sample
from Tsinghua
ALD coated glass RPC

## Slide 6: Next steps
Simulation study to determine charged particle rate and safety factor
Test RPC with current CRV electronics to verify compatibility
Construction and testing of prototype high rate RPCs
(Construct small module to test in Mu2e TS region?)