## Slide 1
K. Badgley and A. Hocker
Mu2e-II
August 30, 2018
Solenoids Working Group

## Slide 2: Mu2e Solenoids
Detector Solenoid
  No upgrades
Transport Solenoid
  Modification of TSU
  Proton beam through upstream TSU
Production Solenoid
  Will need to replaced
  New conductor, larger bore, …
PS
TSU
TSD
DS

## Slide 3: Experimental Challenges
Radiation Effects on the Superconductor
  Peak Power Density
  DPA
Proton Beam Line
Heat and Radiation Shield Design
TSU Modification

## Slide 4: Superconductor Peak Power R&D
Increased Cooling- lower LHe temp
  With W shield, run at ~3.7 K to keep required temperature margin of 1.5 K
New Cable with internal cooling (Vadim)
  Easier to wind
  ~4-5 years to develop and verify
May be difficult to find cable vendor
LHe forced flow
Vadim

## Slide 5: Superconductor DPA R&D
Tungsten HRS would solve DPA issues (Vitaly)
Vitaly
Vitaly

## Slide 6: Proton Beam Line
Change incoming beam trajectory to hit target (Neuffer)
Bend outgoing beam to hit dump – additional dipole?
Requires TSU Modification
  How do we get the TSU out of the
  building
Neuffer
Neuffer

## Slide 7: TSU Modification
Top View TSU Upstream

## Slide 8: HRS
Materials
  Bronze only will not work( Vitaly)
  Tungsten option is heavy
  Consider a layered option with Bronze and Tungsten
    Reduce cost and weight
Geometry
  Consider asymmetric design to shield more in the areas needed
Vendor and Design
  Can we get full Tungsten or will
  it be in large sheets
Currently hot spot and high field are in the same location

## Slide 9: Summary- We can’t design in a vacuum
Peak Power Density (Heat Load On Target, Beam)
Heat and Radiation Shield Design
Magnet Design
Target Location
Superconducting Cable

## Slide 10: Backup

## Slide 11: Notes
Radiation Studies
  (limited beam entry, target heat deposition?,)Peak Power Density-> feeds into HRS design-> Magnet design
  DPA
    Tungsten HRS
Magnetic Modeling and Winding Method
New Cable Vendor or design
  Cooling limit on current design, set by LHe
  New design could eliminate this
  Other options?
Heat load on thermal shield in TS
Size limit in the existing building?
Can the TSU fit through the PS hatch?
Can the current feedbox cool this?
Heavy tungsten HRS- reduce cost and weight by using multi layers
Possible the peak power would not be in the location of the peak field
https://docs.google.com/spreadsheets/d/1K8et2APESzJiG1KM2ndy-xMq_N9LvFd7O6xOpn94fYQ/edit#gid=647684739

## Slide 12: Alternative Ideas
Muon cooling ring
Forward beam