## Slide 1: DATA COLLECTION AND HANDLING
Joseph F Muratore
Superconducting Magnet Division
Brookhaven National Laboratory
Review for the HL-LHC AUP Vertical Magnet Test Stand at BNL– August 1-2, 2018

## Slide 2: Outline
Data acquisition systems at BNL
Data files generated at BNL
How data files are shared
How test results are distributed
Examples of distributed test result formats
Charge 5b

## Slide 3: BNL Magnet Test Data
Fast data logger (quench) - All voltage tap, individual coil and layer main voltages, coil difference, all quench antenna signals, CLIQ signals, and all protection heater signals are included in one data file, along with cryostat and buffer pressures, power supply voltages, ground currents and magnet current, and others. Sampling rate is typically 10 kHz and time window 5 s; both can be adjusted as needed.
Slow data logger (monitor) - Includes select signals (a subset of fast logger signals) for monitoring during testing, and providing signals over longer periods of time, such as during cooldowns and warmups. The sampling rate during tests is usually 1 Hz; for cooldowns and warmups, sampling interval is typically 10 min. This can be adjusted as needed.
FPGA Quench Detector input signals – inputs to FPGA QD: total coil voltage, half coil voltage difference (filtered and unfiltered), magnet current, ramp rate, and splice voltages.
Power supply monitoring – This includes parameters such as current sharing and temperatures of IGBT devices, IGBT voltages, temperatures, etc.
Vishay (LARP) strain gauge measurements – 4 wire DC devices - bridge voltages, excitation currents, and magnet current.
HBM (CERN) strain gauge measurements – 5 wire AC devices – bridge excitation voltages, strains, magnet current
Data acquisition at BNL is separated into the following individual systems:

## Slide 4: BNL Magnet Test Data
Data from each of the previously listed DAQ systems are each written into separate data files
All data files (except for HBM strain gauge measurements) are generated using the LabVIEW programs that control the National Instruments modules for each of the DAQ systems
All data files are generated as tab-delimited text files
Each column in every file has a heading describing the signal data in that column; each row is a data record of all reads taken at specified time
There is a general heading at the top of each file that is used to describe the test and its parameters.
The text files can be opened in and saved as an Excel spreadsheet if wanted
Calculations, analysis, tables, and plots can be done in the Excel file
HBM strain data files are in a different format and are generated using a vendor-supplied program (Catman), compatible with the systems at CERN, LBNL, and FNAL
How data files are created and used at BNL

## Slide 5: BNL Magnet Test Data
Any of the data files (fast logger, slow logger, strain gauge, etc.) can be copied into a directory which has sharing privileges, and has been set up and maintained by G. Sabbi at LBNL
At present, the shared directory is a standard Google Drive or a Google Team Drive (this is still being reviewed)
Shared data files can be either in the original tab-delimited text format or in Excel spreadsheets, with or without the plots and analyses already done by me, as is requested
So far this scheme has worked OK, but could be a bit faster
Diadem (National Instruments) data analysis software is available at BNL and we will be looking into using that and TDMS-formatted data files in the near future
How BNL data files are shared

## Slide 6: BNL Magnet Test Data
For the previous tests of MQXFPM1 (single coil in mirror yoke) and MQXFAP1 (first full MQXFA quadrupole prototype), a summary of activity was sent to a prescribed list of collaborators and colleagues at the end of each test day
A detailed summary of quench tests and a quench plot is kept and updated over the course of the testing, and distributed when needed
An electronic test log is presently being discussed and designed in order to provide more frequent distribution of the test day’s results and events
Weekly AUP meetings feature a magnet test update presentation which includes a summary and/or updated plot, and any details/plots/tables of results to be discussed
Strain gauge data, magnetic measurement data, quench data, and quench summary list (in Excel file), to be uploaded into online folder within one week after vertical test is completed. Details can be found in Guidelines for MQXFA Test Data Organization US-HiLumi-doc-1325
This is to be used by the magnet acceptance committee led by G. Ambrosio, L2 manager for Magnet Integration WBS for AUP, as detailed in Interface Control Document WBS 302.2.01 – 302.4.01 US-HiLumi-doc-1151
Within one month after magnet test is completed a test report for each magnet is written, using a format requested by CERN (Example of magnet test report is available: US-HiLumi-doc-930)
How test results are distributed

## Slide 7: BNL Magnet Test Data
How test results are distributed – Quench Summary Table

## Slide 8: BNL Magnet Test Data
Thermal Cycles
How test results are distributed – Quench History Plot

## Slide 9: BNL Magnet Test Data
How test results are distributed – final magnet test reports
US-HiLumi-doc-930

## Slide 10: Summary
Provisions for data file generation are in place and have been used in previous MQXFA magnet tests
Mechanisms for sharing data files have been established and have been used successfully during the previous MQXFA tests
Data sharing mechanisms continue to be reviewed for changes to improve efficiency
Various means of reporting test results have been used successfully and meet the requirements of the collaboration
Thanks for your attention