## Slide 2: Status & Outlook for the LHC US-LHC User Association Annual Meeting 2018, 24 –26 October Fermilab – Batavia, Illinois - USA
Rende Steerenberg – CERN
On behalf of the LHC team

## Slide 3: Content
Looking Back at 2018
LHC Performance 2018
The Remainder of 2018
Some of the Challenges Ahead
Some Words on the LIU Project
Conclusion

## Slide 4: Looking Back at 2018

## Slide 5: A quick look back at 2018…
2018
Jan Feb Mar Apr May Jun Jul Aug Sep Oct Nov Dec
Mar. 29th
First 2018 beam
Apr. 17th
First Stable Beams
Apr. 23rd
1 day scrubbing
1st signs of 16L2 activity
Jun. 18th – 21st
TS #1
Mar. 5st
Start of powering tests
Sep 17th – 21st
TS #2
YETS
Sep. 6th
50 fb-1 reached
Dec 3rd
End of 2018 run
Partial heat up of sector 1 -2 to mitigate 16L2
May 12th
Record Peak Lumi: 2.07x1034
May 5th
Collisions with 2556 bunches
Apr. 28th
Collisions with 1200 bunches
Oct. 27th
End of 2018 p-p-run
Nov. 5th
Start Pb-Pb
run
Dec. 3rd – 9th
7 TeV Magnet Tests
Oct. 31th – Nov. 2nd
TS #3
May 14th & 15th
16L2 Storms with beam dumps
May 20th
16L2 Storms with beam dumps
May 31st
16L2 Storms Recovery strategy established
Aug. 7th
16L2 with successful recovery
Planned

## Slide 6: 16L2: Beam Dumps Due to Fast Losses
Accidental air Inlet in beam vacuum in half cell 16 left of IP2 (16L2) during 2016-2017 Year-End Technical Stop (YETS)
Initially mitigated by 8b4e beam and “home-made” solenoid that suppress e-cloud
Later (YETS 2017-2018) by partial warm-up an vacuum pumping
Not fully recovered yet, but no longer limiting performance

## Slide 7: 16L2 Storms & Recovery Strategy
“Classical” recovery as applied in 2017 (several days)
16L2 Storms
16L2 Storms recovery by intensity ramp up
Production
2556
bunches
987
bunches
1227
bunches
1551
bunches
1887
bunches
2556
bunches
16L2
16L2 recovery
Production
Production
Fast recovery as applied in 2018 (within the same day)
2556
bunches
2556
bunches
2556
bunches
2556
bunches
987
bunches
2556
bunches

## Slide 8: ATS Optics, since the start of 2018
ATS = Achromatic Telescopic Squeeze
  Increase 𝛽-function in the arcs to enhance effect of inner triplets around the experiments
  Baseline optics for the HL-LHC, to allow for 𝛽*=0.15 m
In addition, depending on the “telescopic factor” octupoles will have more effect for same current, thanks to larger 𝛽-functions in the arcs
Deployed as proof of principle and to gain operational experience
Further development continues during Machine Development sessions
S. Farthouk et al.
𝛽*=0.4 m
𝛽*=0.1 m

## Slide 9: Luminosity Levelling & Anti-levelling
In certain conditions and depending on the experiments request, it is desirable to adapt the luminosity dynamically with beams in collision – levelling
Beam offset / separation
crossing angle
b* (= beam size at IP)
Methods for Levelling

## Slide 10: Luminosity (Anti-)Levelling Operational
In 2017 step-wise crossing angle anti-levelling was introduced
  3 steps depending on the luminosity burn-off
Crossing angle anti-levelling
In 2018:
  The crossing angle anti-levelling is done continuously, down to 130 𝜇rad
  A step-wise 𝛽* anti-levelling has been added
  𝛽*=30 cm  27.5 cm  25 cm
𝛽* levelling tests during MD
Allows few % gain in integrated luminosity, but is a vital exercise for future (HL-LHC) levelling

## Slide 11: LHC Performance 2018

## Slide 12: LHC Machine & Beam Availability
Best production year ever for the LHC
Performance mainly through machine availability, but also thanks running close to twice the design (peak) luminosity and anti-levelling
  High brightness beams from the injector
  Various optimizations in LHC to minimize beam blow up and maximize life time
Preliminary
2018

## Slide 13: 2018 Luminosity Forecasted & Achieved
Data taken on: 09.09.2018@15:00 UTC
Average of ATLAS & CMS
LHCb
ALICE Luminosity is
levelled
LHCb luminosity
is levelled

## Slide 14: Run I + Run II Goals
The LHC goal up to LS2 was 150 fb-1 and has been achieved in Run II alone
The goal for 2018 was 60 fb-1, hence 6 fb-1 (10%) beyond target
Period | Int. Luminosity [fb-1]
Run 1 | 29.2
Run 2: 2015 | 4.2
Run 2: 2016 | 39.7
Run 2: 2017 | 50.2
Run 2: 2018 | 66
Total Run 1+ 2 | 189.3

## Slide 15: Peak Luminosity and its Evolution
2016: the LHC well beyond its design luminosity
  Despite a reduced number of bunches
  Thanks to the brighter injectors beam
Every year:
  The peak luminosity is higher than previous years
  The time in which the peak luminosity is reached is shorter
Design
Luminosity
Thanks to a combination of:
Continuous improvement of beam brightness from the injectors
Good understanding of LHC and experience in re-commissioning
After Long Shutdown 2, many things will have to be “learned” again

## Slide 16: Peak Luminosity during 2018
Bunch intensity is not really pushed to avoid issues with 16L2
Steadily cruising close to 2 x 1034 cm-2s-1 (twice the LHC design value)
Achieved record peak luminosity 2.2 x 1034 cm-2s-1

## Slide 17: 2018 Machine/Beam Parameters
Parameter | Design | 2018
Bunch population Nb [1011 p] | 1.15 | ~1.1
No. bunches per train | 288 | 144
No. bunches | 2780 | 2556
Emittance 𝜀 [mm mrad] | 3.5 | ~2.2
𝛽* [cm] | 55 | 30  27.5  25
Full crossing angle [𝜇rad] | 285 | 300  260
Peak luminosity [1034 cm-2s-1] | 1.0 | ~2
Integrated luminosity [fb-1] |  | 66
The “CMS bump” to compensate ground movement was increased from -1.5 mm to -1.8 mm

## Slide 18: The Remainder of 2018

## Slide 19: Remainder of 2018
Pb-Pb ions run
Magnet training tests to aiming for 7 TeV after LS2
The Proton luminosity production run has been completed
The Special Physics run at low energy and high beta has been completed
Presently an extended MD period is ongoing
The Pb-Pb ions run is upcoming and prepared
LS2 will start with a magnet training test campaign to learn more on the magnet training quenches to be expected for running at 7 TeV after LS2

## Slide 20: Summary Table 2018 - 2017 - 2016
 | 2018 |  | 2017 |  | 2016 | 
Phase | Days | Ratio [%] | Days | Ratio [%] | Days | Ratio [%]
Comm. & Intensity ramp up | 33** | 13.4 | 35 | 16.1 | 28* | 11.3
Scrubbing | 1 | 0.4 | 7 | 3.3 | 2 | 0.8
25 ns Proton Physics | 130 | 52 | 127 | 58.5 | 139 | 56.3
Special Physics Runs | 14 | 6.5 | 18 | 8.3 | 10 | 4
Setting up Pb-Pb ion run | 4 | 1.6 | - | - | 6 | 2.4
Pb-Pb ion run | 24 | 9.8 | - | - | 23 | 9.3
Machine Developments (MD) | 24 | 9.8 | 18 | 8.3 | 21 | 8.5
Technical Stops (3x) | 12 | 4.9 | 8 | 3.7 | 12 | 5
Technical Stop Recovery (3x) | 4 | 1.6 | 4 | 1.8 | 6 | 2.4
Total | 246 | 100 | 217 | 100 | 247 | 100
Integrated luminosity [fb-1] | 66 |  | 50.2 |  | 39.7 | 
* Did not fully include intensity ramp up – interleaved commissioning and interleaved intensity ramp up was as of 2017
** With 1200 bunches per beam, previously with 3 bunches
Based on the 2018 LHC Schedule Version 1.6

## Slide 21: Some of the Challenges Ahead

## Slide 22: Reaching 7 TeV after LS2
All dipole magnets were trained for 6.5 TeV operation since 2015. Just over 150 quenches were required to reach 6.5 + 𝛆 TeV
  Spread in number of quenches between the sectors is due to the mixture of producers
  Two sectors were pushed to 6.75 TeV in December 2016
Magnet training campaign to 6.5 TeV (2015)
Estimate for 7 TeV:
One very slow sector  ~110 quenches
3 slow sectors  75-85 quenches
3 fast sectors  ~60 quenches
One very fast sector  ~25 quenches
Considering 2 quenches/day, the training for each sector will be between 10 days and ~2 months

## Slide 23: Electron Cloud
Running with small bunch spacing provokes an avalanche-like process, e-cloud, due to the Secondary electron Emission from the chamber’s wall
Consequences:
  degraded vacuum
  impact on beam quality (instabilities, emittance growth, losses)
  excessive energy deposition
Controlled and prolonged electron bombardment of the surface has proven proved to reduce drastically the secondary electron yield (SEY)
Scrubbing provides a mean to mitigate e-cloud build-up, resulting in a clear improvement of beam quality

## Slide 24: Heat Load and e-Cloud
  Measuring the thermodynamic properties of helium, it is possible to know the heat load on the beam screen
The heat load represents a limitation as it challenges the cryogenic system and can eventually lead to beam dump (beam screen warm-up)
  8 kW/arc (~160W/hcell)
e-cloud in quadrupoles
e-cloud in dipoles
e-cloud in drifts
Impedance
Synchrotron radiation

## Slide 25: Heat Load Around the Machine
S12
S81
S23
S78
S34
S67
S45
S56
Heat loads are distributed unevenly.
  High-load sectors (S12, S23, S78, S81)
  Low-load sectors (S34, S45, S56, S67)
This division appeared after LS1, but presently unclear why
The only sector that was warmed-up (S12) and vented after LS1 was conditioned back to the high level of heat load
Good sectors
Bad sectors

## Slide 26: Some Words on the LIU Project

## Slide 27: Luminosity, the Figure of Merit
More or less fixed:
Revolution frequency
Number of bunches
High-Luminosity LHC
X 2
LHC
Intensity per bunch
Number of bunches
Geometrical
Correction
factors
Beam dimensions
Parameters to optimize:
Intensity per bunch
Transverse beam dimensions
Geometrical correction factors

## Slide 28: The Aim of HL-LHC
Levelled luminosity of Llevelled = 5×1034 cm-2s-1,
This should allow for:
  An integrated luminosity of 250 fb-1 per year, with the goal of Lint = 3000 fb-1 twelve years after the upgrade.
This luminosity is more than ten times the luminosity reach of the first 10 years of the LHC lifetime
Two projects to realize this:
LHC Injector Upgrade
HL-LHC upgrade

## Slide 29: Present Injectors Performance Limitation
LHC Beam | Nb [x1011 ppb] | εx,y [μm]
Present | 1.3 | 2.7
HL-LHC target | 2.3 | 2.1
Increase brightness limit for PSB and PS with H- injection and increase of injection energy
Reduce longitudinal dipolar coupled bunch instability in PS that limits bunch intensity (Longitudinal damper/feedback)
Increase RF power in the SPS and reduce coupled bunch instability that limits bunch intensity (add 800 MHz RF and impedance reduction)

## Slide 30: LIU Performance Ramp-up Run III
However, the LHC will not yet be able to benefit fully from the Injector performance, but some performance increase is to be expected
The “LHC Run III Working Group” investigates limitations and opportunities and will try to establish an optimum run scenario
2020 - 2021
Commissioning of 1.2x1011 ppb with LINAC 4 & LIU
Re-produce all pre-LS2 beams
Pb ions with LIU performance and slip stacking in SPS
Commissioning of 1,8x1011 ppb with design brightness and loss budgets out of SPS
2022
2023
Commissioning of 2.1x1011 ppb up to SPS extraction and tests of higher intensity at least up to the SPS injection
2024
Commissioning of 2.3x1011 ppb up to SPS extraction with the desired brightness and loss budgets

## Slide 31: The CERN Long-Term Planning
LIU Deployment
HL-LHC Civil engineering
HL-LHC deployment
HL-LHC Running
Injector Performance Ramp up

## Slide 32: Conclusion

## Slide 33: Conclusions
The LHC had its best production year ever with rather stable running and high machine availability
  ATLAS/CMS integrated 66 fb-1
  LHCb integrated 2.46 fb-1
  ALICE integrated 27.3 pb-1
Methods and principles for future HL-LHC running are being tested and deployed
  ATS optics
  Various types of luminosity levelling
Aiming at 7 TeV for after LS2, requiring magnet training
Electron Cloud and heat load differences are still a challenge to be tackled
During LS2 the LIU project will be deployed followed by a performance ramp-up of which the LHC can partially profit

## Slide 34: HL-LHC is under way..., much will change

## Slide 36: Effect of Civil Engineering on Lumi
Ground compacting on the surface is visible on the luminosity signal

## Slide 37: Running with 2556 bunches
Contrary to 2017, steady running with 2556 bunches per beam
In 2017 we ran for large part with the 8b4e beam due to the 16L2 issue

## Slide 38: Towards High Luminosity LHC

## Slide 39: LHC Injectors Upgrade
Main ingredient is LINAC 4 with H- injection
  Higher beam brightness after injection into the PSB than with the present proton LINAC 2
Majority of the other injectors changes are focused on:
  Ability to accelerate intense and bright beams
  Maintaining the brightness until injection into the LHC, minimize blow up
  Improving diagnostics to be able to measure beam characteristics precisely

## Slide 40: Intensity and Density With LINAC2
With the present multi-turn proton injection the intensity is increased with about constant density
Injection from LINAC4 with H- will allow increasing phase space density when injecting into the PSB

## Slide 41: LINAC4 & Charge Exchange Injection
Use H- beam from LINAC 4
x’
x
+
-
+
+
+
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
-
-
Before stripping foil
x’
x
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
Behind stripping foil
Phase Space Painting is possible (various particle distributions)

## Slide 42: LIU Performance Ramp-up Run III
However, the LHC will not yet be able to benefit fully from the Injector performance, but some performance increase is to be expected
The “LHC Run III Working Group” investigates limitations and opportunities and will try to establish an optimum run scenario
2020 - 2021
Commissioning of 1.2x1011 ppb with LINAC 4 & LIU
Re-produce all pre-LS2 beams
Pb ions with LIU performance and slip stacking in SPS
Commissioning of 1,8x1011 ppb with design brightness and loss budgets out of SPS
2022
2023
Commissioning of 2.1x1011 ppb up to SPS extraction and tests of higher intensity at least up to the SPS injection
2024
Commissioning of 2.3x1011 ppb up to SPS extraction with the desired brightness and loss budgets

## Slide 43: HL-LHC: What will be changed ?
New IR-quads (inner triplets)
  New 11T short dipoles
  Collimation upgrade
  Cryogenics upgrade
  Crab Cavities
  Cold powering
  Machine protection
  …
Major intervention on more than 1.2 km of the LHC
These are only the main modifications and this list is not exhaustive
Just a very few selected items in the next slides

## Slide 44: 11 Tesla dipoles
To be installed in Point 7 already during LS2 :
11 Tesla Dipole
11 Tesla Dipole
15.66 m
2.16 m
6.75 m
6.75 m
collimator

## Slide 45: Crab Cavity Tests Stand in SPS
Increased beam-beam effect in LHC with higher beam intensity
  Requires increase of the crossing angle, hence reduction of the geometrical factor
World’ s first crabbing on a proton beam
(23 May 2018)

## Slide 46: LHC & HL-LHC Parameters
Parameter | LHC | LHC 2018 | HL-LHC | HL-LHC
Beam type: | Design | BCMS | Design Stand. | Design BCMS
Energy [TeV] | 7 | 6.5 | 7 | 7
Number of bunches per ring | 2808 | 2556 | 2748 | 2604
Bunch spacing [ns] | 25 | 25 | 25 | 25
Bunch population Nb [1011 p/b] | 1.15 | 1.1 | 2.2 | 2.2
Transv. norm. emittance SB n [mm mrad] | 3.75 | 2 | 2.5 | 2.5
Betatron function at IP1 and IP5 b* [m] | 0.55 | 0.3/0.25(2) | 0.2 (0.15) | 0.2 (0.15)
Half crossing angle in IP1/5 [μrad] | 142.5 | 160/130(1) | 260 | 260
Geometrical factor w/o crab cavities at min. b* | 0.836 | - | 0.369 | 0.369
Geoetrical factor with crab cavities at min. b* | - | - | 0.715 | 0.715
Peak Luminosity w/o crab cavities [1034 cm-2s-1] | 1 | 2.1 | 6.52 | 6.18
Peak luminosity with crab cavities [1034 cm-2s-1] | - | - | 12.6 | 11.9
Levelled luminosity [1034 cm-2s-1] | - | - | 5.32 | 5.02
Expected levelling time [h] | - | - | 5.23 | 5.23
Events/crossing μ (with levelling & crab cavtities) | ~25 | ~60 | 140 | 140
Stored beam energy [MJ] | 360 | 320 | 675 | 640