## Slide 1: Active ganging status July 2018
Dante Totani, Ken Treptow, Gustavo Cancelo

## Slide 2: 72 SiPM active ganging board: 12 x 6 matrix
Each row has 6 MPPCs in parallel.

## Slide 3: Mean signal 72 MPPCs at -70C and Vb=47
Rise time 100ns, Fall time 660ns, slow undershoot recovery.
SSP time constant has not been modified.

## Slide 4: Noise spectrum
Noise is 10nV/sqrt(Hz)
1/f at lower frequencies.
It does not vary much with T and Vb

## Slide 5: Simulations
Simulations are in agreement with results from data.

## Slide 6: Mean signal 72 MPPCs at LN2 and Vb=47
Noise is about 7 ADUs FWHM

## Slide 7: Filtering the signal with a matched filter (50 taps long)
Good reduction of noise by filtering.
The 1st, 2nd PE spectrums do not change.
Histograms of
σnoise
Histograms of
Noise and 1st , 2nd PE

## Slide 8: 72 MPPCs vs 48 MPPCs
72 MPPCs: noise is higher and signal is smaller. S/N=5.
48 MPPCs: S/N=10.
S/N measured as the fit of the 1st PE peak to the σnoise.

## Slide 9: Effect of bias voltage on 48 MPPC
48 MPPCs Vb=47v: S/N=10.
48 MPPCs Vb=45v: S/N=5.
S/N measured as the fit of the 1st PE peak to the σnoise.
For Vb=45v the 1st and 2nd PE histograms are better defined. Probably due an effect of Vb in the relative gains.

## Slide 10: Peak minus baseline vs integrated charge (0.6usec)
Very similar S/N.

## Slide 11: Mean signal 48 MPPC
Rise time increases from 10% from 48 MPPCs to 72

## Slide 12: Conclusions
Board operates correctly with 48 and 72 MPPCs.
Noise is low
Simulations and measurements are in agreement.
Characterization will continue.
NIU will probably help.