## Slide 1
Jessica Thompson, University of Alabama
SIST Final Presentation
6 August 2018
Simulation of Conduction Cooled SRF Cavity

## Slide 2: Radio Frequency (RF) Cavities
Heavily used in research and industry
Elliptical geometry resonates at a particular frequency
Particles are accelerated as they move through each cell
Accelerating gradient quantifies energy particles gain

## Slide 3: Superconducting RF (SRF) Cavities
Superconductors have very low energy losses
Cavity must be kept below critical temperature (9.25 K for niobium)
Liquid helium coolant is a major complexity

## Slide 4: Conduction Cooling with a Cryocooler
Replace liquid helium with a cryocooler
Conduction cooling is a possibility due to technological advancements
  Cryocoolers are commercially available and can cool to 4 K or below
  Nb3Sn coating reduces cavity heat dissipation
Cryomech PT420 Pulse Tube Refrigerator
stage 1
stage 2

## Slide 5: Cryocooler Measurements
Measured the temperature of stage 2 as a function of heat input to stage 1 (H1) and to stage 2 (H2)
Measured amplitude of cryocooler temperature oscillations
Frequency of oscillation is about 1 Hz

## Slide 6: Simulated Geometry
single cell cavity
welded rings
thermal link
cryocooler plate
Thermal link connects cavity to cryocooler
Must have good thermal contact with cavity
Must conduct heat well at low temperatures in vacuum
Must be flexible to isolate mechanical vibrations of cryocooler
Expected Heat Flow

## Slide 7: Simulation Procedure
Geometry
Material Properties
Cryocooler Measurements
Heat Transfer Across Thermal Link
RF Fields Inside Cavity
Cryocooler Oscillations
Heat Transfer Across Cavity
Heat Transfer Across Full Geometry
Find the temperature difference between the cryocooler and the welded rings
Find the amplitude of cavity temperature oscillation
Find the dissipated power of the cavity
Find the spatial temperature distribution of the cavity
Find the temperature of the full system

## Slide 8: Heat Transfer Across Thermal Link
Heat flux is applied at weld faces of rings
Constant temperature is applied at cryocooler plate
  Used cryocooler measurements to determine this temperature
Temperature at weld faces is measured
Dissipated heat
Cryocooler

## Slide 9: Heat Transfer Across Thermal Link
Cavity temperature rises with dissipated power
Dissipated power i
= length of cell
= surface resistance
= known factors

## Slide 10: Cryocooler Oscillations
Apply heat flux at weld faces
Apply time-varying cryocooler temperature
Measure time-varying temperature at weld faces
Oscillations dampen before reaching cavity

## Slide 11: RF Fields Inside Cavity
Electric field
Magnetic field

## Slide 12: Heat Transfer Across Cavity
Data courtesy of Sam Posen
Use magnetic field H to find dissipated power on cavity walls
Model heat flow from cavity walls to notches at constant temperature
vacuum
cavity walls
notches

## Slide 13: Heat Transfer Across Cavity
Spatial temperature variations across cavity are small compared to across cooling link
Average temperature of cavity and maximum temperature of cavity are close to equal
Temperature

## Slide 14: Heat Transfer Across Full Geometry
Model heat flow from cavity walls to cryocooler plate
Temperature difference is sum of difference from previous simulations

## Slide 15: Conclusions
At an accelerating gradient of 12 MV/m or less, the cavity temperature is less than 7 K
The temperature across the cavity is nearly spatially uniform
Temperature oscillations in cryocooler dampen before reaching the cavity
Conduction cooling this geometry with a cryocooler is viable

## Slide 16: Acknowledgements
Thanks to Ram Dhuley, Mike Geelhoed, Charles Thangaraj, Oleg Prokofiev, Ivan Gonin, Andrei Lunin, Aaron Sauers, Sandra Charles, Judy Nunez, Laura Fields, and the SIST Committee