## Slide 1
Adrian Orea, FNAL SIST Intern
Supervisor: Minerba Betancourt
UIUC Mechanical Engineering
3 August 2018
SBND Electronics Data Analysis

## Slide 2: Outline
Objective
Background
  LArTPC and test beam
  Purity
Purity Calculation
Multi-Channel FFT and Waveform plotting framework
Noise RMS Analysis
Raw Digit Event Display
Future work
Conclusion

## Slide 3: LArTPC
Time Projection Chamber (TPC)
  Filled with Liquid Argon
  Two Planes
    Collection and Induction
  High electric field
  Used at several detectors
    SBND, MicroBooNE, Icarus, and DUNE
1

## Slide 4: TPC at Fermilab Test Beam Facility (FTBF)
FTBF used to test detectors with a beam of protons
  Beam for this project was a mixture of protons, pions, and kaons
Beam is pulsed
  SBND TPC placed in Cryostat
  Boards and wiring secured
Data was collected for several days at a time
  Cosmic muon data could also collected

## Slide 6: Purity Calculation
Free electrons can easily travel through liquid Argon
  Some get recaptured by Argon Ions
Although a tank of pure Argon is ideal, it’s not
  Potential contamination during various filling and boiling phases
  Innate contamination from source
Electronegative contaminants capture free electrons
  Oxygen, water, etc
Ar
Ar
Ar
Ar
Ar
Ar
Ar+
Ar
Ar
Ar
Ar
Ar
Ar
Ar
Ar+
Ar+
Ar+
Ar+
Ar+
Ar+
Ar+

## Slide 7: Purity Calculation
Apply first cut on number of hits and unique wire numbers
  Plot Peaktime vs wire number, acts as a track reconstruction
    Induction and collection planes
  Remove points farther than 2 ticks from fit line
Collection Plane
Induction Plane
Notes:   , for a solid angle
  , for the transversal and z-direction momentum
  𝑑𝜎/𝑑𝛺, for a solid angle
  (𝑑^2 𝜎)/(𝑑𝑝_𝑡 〖𝑑𝑝〗_(||) ), for the transversal and z-direction momentum

## Slide 8: Purity Calculation cont.
  Plot integral (charge) vs peak time
    Fit with exponential, normalized based on geometry

## Slide 9: Purity Calculation cont.
  Create histogram of difference between fit and data
    Fit with Landau function to get sigma

## Slide 10: Purity Calculation cont.
  Refit with sigma cuts
    Keep values and store into file that is used as input for a minimizer of a maximum likelihood estimator (MLE)
    Lifetime is extracted
Notes: Include the lifetime on here 

## Slide 11: Event Display
Current event display works great
  However, is loaded with features
  Using for small checkups such as thresholds is slow
    For changing Collection and Induction planes separately
Created a fast Event display that uses the output of Purity.cc
  “Lite version”
    Fast and reliable

## Slide 12: Multi-Channel Analysis
Current Plotting scripts analysis works
  However, per event and per channel basis
Need a script to gather all of the channel data to analyze on an event basis
  FFT and waveform plotting
Notes: Change to simulation

## Slide 13: Data
Data was not correct
Malfunction in wires
  Collection had inverted peaks
  Induction had noisy wires and a broken motherboard

## Slide 14: Data cont.
Ignored because of high noise
Collection Plane
Induction Plane
Notes: Include picture of event display that I sent to Minerba. She will email me those slides

## Slide 15: Multi-Channel Analysis cont.

## Slide 16: Noise RMS
From the purity calculation, values away from the linear fit are used to calculate the RMS of the noise
Currently exits on an event basis
  Now averages over the entire set of events in a file
  Induction and Collection plane are separate

## Slide 17: RMS Plots

## Slide 18: Results
Purity is added to framework
  Part of VST git repository
Noise RMS is finished
  Useful for analyzing the channels
    Pinpointing bad channels
FFT & Waveform vs Channel is finished
  Part of VSTAnalysis git repository
Event display is done
  Operates as long as Purity.cc operates

## Slide 19: Future Work
Tune the Purity.cc code for data from simulation
  Modifying “sigma” cuts
RMS used to set threshold based on the event
  To eliminate general settings
Finalize a script for analyzing the general trend of lifetimes
Notes: Next part is to tune all of the model parameters

## Slide 20: Acknowledgments
I would like to thank the following people for their patience and help as they were always available to answer my many questions.
  Minerba, Gray, Thomas, Dominic
Thank you to my Fermilab mentors for helping me with general work at Fermi and with my education path
  Donovan, Javier, and Elliot
Finally, I would also like to thank Fermilab and the SIST committee, for such an amazing summer experience
  Sandra, Judy, Laura

## Slide 21: Distance from linear fit

## Slide 22: Data Induction Plane Noise

## Slide 23: Data analysis
Notes: Change to simulation

## Slide 24: Beam Composition