## Slide 1
Leonardo Ristori – on behalf of the SSR1 team
Slides by Mattia Parise
International Workshop on Cryomodule Design and Standardization
BARC, Mumbai 4-7 September 2018
SSR1 Cryomodule String Assembly

## Slide 2: Outline
String overview
Rail system
Beamline bellows
Assembly of solenoid-BPM group
Nitrogen purging studies
Recent improvements

## Slide 3: SSR1 cryomodule for PIP-II
SSR1 cryomodule
SSR1 cavity string
PIP-II Linac
SSR1

## Slide 4: SSR1 string overview – Rail system
Completed string ready to roll out of cleanroom
Rail system is new design adapted for SSR and new facility
Load, deflection and moving tests all successful

## Slide 5: SSR1 string overview – Assembly oriented design
Interconnection cavity-cavity
Solenoid-BPM subassembly
Solenoid
BPM
Gate Valve
20
mm
Gate Valve
Movable rail system
Vacuum-end coupler
Type
A
Type
B
Type
A
Type
B
Type
A
Type
B
Type
B
Type
A
Edge-welded bellows

## Slide 6: SSR1 string assembly dry-run
Dry-run of SSR1 string assembly is carried out on a half cavity string
The goal is to assess the feasibility of a cleanroom-compatible assembly

## Slide 7: SSR1 string assembly dry-run
Solenoid-BPM-Bellows
Cavity connection
Cavity-cavity connection
Dry-run of SSR1 string assembly is carried out on a half cavity string
The goal is to assess the feasibility of a cleanroom-compatible assembly

## Slide 8: SSR1 string assembly dry-run – Movable Rail System
Rail system with string weight can be successfully moved to the desired location. The process has been repeated 5 times and final position can be achieved with an uncertainty of ~ 5 mm

## Slide 9: SSR1 string assembly dry-run
Cavity to solenoid bellows
Solenoids
BPMs
Cavity to BPM bellows
Cavity to cavity bellows

## Slide 10: Edge welded bellows particle counts
3 cycles compression and extension (10 liters sample) |  |  | 
Time [s] | > 0.3 μm | > 0.5 μm | > 1 μm
7 | 2 | 0 | 0
14 | 2 | 1 | 0
21 | 3 | 1 | 0
28 | 1 | 0 | 0
35 | 3 | 0 | 0
42 | 1 | 0 | 0
49 | 1 | 0 | 0
56 | 1 | 0 | 0
63 | 1 | 0 | 0
70 | 1 | 0 | 0
77 | 1 | 0 | 0
84 | 0 | 0 | 0
91 | 2 | 1 | 0
Edge welded bellows was cleaned and brought inside class 10 cleanroom:
  30 min Liquinox (1%) + DI water ultrasonic cleaning at 50 °F
  30 min Citranox (2%) + DI water ultrasonic cleaning at 50 °F
  30 min DI water ultrasonic cleaning at 50 °F
  Handheld HPR
Particle counts of the nitrogen dried bellows approach 0 particles > 0.3 μm in less than 1 minute
Particle counts during contraction are acceptable

## Slide 11: SSR1 string assembly dry-run
Bellows cage is disassembled once the cavity-cavity connection is completed

## Slide 12: SSR1 string assembly dry-run
Edge welded bellows can be successfully assembled and bellows cage can be removed

## Slide 13: SSR1 string assembly dry-run
Bellows cages provides 2 rotational degrees of freedom at the end flange
Can be splitted in 2 halves so that can be removed prior cryomodule assembly

## Slide 14: Solenoid-BPM Group
Vertical assembly facilitates handling of components
Sub-assembly can rotate 360 degrees for an easy assembly
The movable cart allows easy handling of the heavy sub-assembly

## Slide 15: Assembly of Solenoid-BPM Group

## Slide 16
Assembly of Solenoid-BPM Group

## Slide 17: Assembly of Solenoid-BPM Group
Diamond aluminum seal

## Slide 18: Assembly of Solenoid-BPM Group
BPM

## Slide 19: Assembly of Solenoid-BPM Group
Cavity to BPM bellows

## Slide 20: Assembly of Solenoid-BPM Group

## Slide 21: Assembly of Solenoid-BPM Group

## Slide 22: Preparation of the SSR1 string assembly dry-run
Link

## Slide 23: Preparation of the SSR1 string assembly dry-run
Link
Sub - millimeter precise and reliable alignment
Easy to use system

## Slide 24: Nitrogen purging studies
Link

## Slide 25: Nitrogen purging studies
No Nitrogen purging applied
Nitrogen purging at 4 SLPD purge flow speed 0.1 m/s

## Slide 26: Nitrogen purging studies
No Nitrogen purging applied
Nitrogen purging at 4 SLPD purge flow speed 0.1 m/s
Back flow inside the beam pipe

## Slide 27: Experimental setup for purging studies

## Slide 28: Nitrogen purging line
Shut-off valve
Pressure regulator
High pressure gauge
Pressure relief valve
Shut-off valve
Shut-off valve
Metering valve
Low pressure gauge
High purity filter
To vacuum cart
Nitrogen purging line can provide up to 20 SLPM
Filter is located on the cavity as last element to avoid cavity contamination
Can be manually operated
Mass Flow Controller can substitute the metering valve for a reliable soft start

## Slide 29: Gate valves particle counts: all metal vs Viton sealed
Viton sealed
Pneumatic actuation (<1 sec for opening and closing)
Viton may degrade due to radiation
All metal construction
Manual actuation (~ 5 min for opening and for closing)
Radiation resistant
SSR1 Gate Valve
LCLSII All-Metal Gate Valve

## Slide 30: Gate valves particle counts: all metal vs Viton sealed
Chart: Opening - Closing cycles from side 1
| Counts 0.3 μm | Counts 0.5 μm | Counts 1 μm
Opening 1 - Side 1 | 94 | 42 | 8
Closing 1 - Side 1 | 177 | 88 | 19
Opening 2 - Side 1 | 180 | 60 | 8
Closing 2 - Side 1 | 164 | 77 | 24
Opening 3 - Side 1 | 142 | 65 | 17
Average Opening | 138.6667 | 55.6667 | 11
Average Closing | 170.5 | 82.5 | 21.5
Average total | 151.4 | 66.4 | 15.2
Chart: Opening - Closing cycles blowing from side 1 (string side)
| Counts 0.3 μm | Counts 0.5 μm | Counts 1 μm
Opening 1 - Blowing from string side | 803 | 439 | 129
Closing 1 - Blowing from string side | 73 | 27 | 6
Opening 2 - Blowing from string side | 230 | 94 | 30
Closing 2 - Blowing from string side | 211 | 88 | 34
Opening 3 - Blowing from string side | 138 | 43 | 12
Average Opening | 390.3333 | 192 | 57
Average Closing | 142 | 57.5 | 20
Average total | 291 | 138.2 | 42.2
SSR1 Viton sealed pneumatic actuated gate valve performed better than the all-metal gate valve in terms of particle counts
SSR1 cryomodule is located at the early stage of the LINAC
Damaging of the Viton due to beam radiation is limited at this stage
SSR1 Viton sealed gate valve is compact, generate less particulate, reliable (does not depend on the operator to be actuated) and can be opened/closed in <1 sec
SSR1 Gate Valve
LCLSII All-Metal Gate Valve
2x better!

## Slide 31: Low-Temp bake with Space Heaters: a new approach
Infrared
heaters
to
vacuum
cart
Able to reach 120°C in 2 hours
90% energy efficient
Can reach 815°C
Output power can be controlled through cavity temperature
Cavity never leaves the cleanroom facility
Quartz fabric Faced Heater

## Slide 32: Avoid active pumping: burst disk
Connection to the vacuum cart was done in a portable glove box
2 days required
Environment is not ideal for a clean connection
Avoid potential contaminations during the connection and from the vacuum cart
Installation time into the test cave is substantially reduced
With active pumping:
Without active pumping: Burst Disk

## Slide 33: Right Angle Valve (RAV) to cavity connection
Gravity
RAV was directly located on top of the cavity beam volume
High risk of particles generated during valve actuation. Gravity force or bad venting procedure can move such particles inside the cavity beam volume

## Slide 34: Summary
SSR1 String designed with assembly in mind
String is segmented in sub-systems for particle-free assembly
Edge-welded bellows a necessary and understood risk
6 degree supports for all components
Nitrogen purging optimized for SSR1 reentrant walls
Several improvements adopted during R&D and dry-run
String assembly of pSSR1 CM to start soon!