## Slide 1: Searching for 10meV-1GeV Dark Matter with Athermal Phonon Detectors
Matt Pyle
UC Berkeley
CPAD 18/12/09

## Slide 2: Outline
Experimental Design Drivers for Light Mass Dark Matter
Other interactions: Getting Around Kinematic Constraints
  Offshell 2-phonon production
  Optical phonons
Athermal Phonon Detectors
  Proposed Experiments That Use Athermal Phonon Readout
    Small volume semiconductor detectors
    GaAs based scintillator
    Al2O3 and other polar crystals
    Molecular Vibrational/Rotational Excitation
    Superfluid Helium
  Detector Physics
  R&D Progress
  Future R&D Needed

## Slide 3: 10 Years Ago: A Focus on WIMPs
(Planck)
Relic DM density suggests weak-scale cross sections
New physics (and particles) at the weak scale could solve the hierarchy problem
10-22 eV
keV
1019 GeV
10 GeV
WIMPS
Notes: Main idea: 10 years ago the majority of the experimental community was searching for WIMPs
DM Constraints:
10^-22 eV: size of the galaxy
< 100 eV: Fermions are degenerate
< 3 keV: warm DM limit
WIMPs: 10GeV < M < 100TeV (above 100TeV WIMP won’t freeze out)
Hiearchy problem:
- Why do different forces have such enormously different strengths
- Why is the Higgs mass so much lighter than the plank scale

## Slide 4: Today: Search for DM Everywhere
US Cosmic Visions: New Ideas in Dark Matter: 1707.04591
Many Well Motivated DM Models at Light Mass
10-22 eV
keV
1019 GeV
10 GeV
WIMPS
Dark Sectors: DM + New Mediators

## Slide 5: Light Mass Dark Matter Experimental Design Drivers

## Slide 6: Light Mass DM Design Drivers: Exposure
Interaction Rate scales with 1/MDM
LZ needs 10 tons to get to 10-47 cm2 at 100GeV, Light Mass DM searches only needs 10kg to reach the same level at 100MeV

## Slide 7: Elastic Nuclear Scattering
DM
Transfer of DM kinetic energy inefficient when Mn >> MDM for elastic scatters
<v>
The primary design driver for Light Mass DM Experimental Searches is Energy Sensitivity!

## Slide 8: Nuclear Recoils from MDM<200 MeV: No Ionization
DM
<v>
For 200 MeV DM Characteristic Recoil Energy
He: Er ~10eV
Si: Er ~2eV
Ge: Er ~ 700 meV
Elastic Nuclear Recoil Scattering will not produce ionization for <200 MeV DM
(actual threshold may be much higher due to Lindhard suppression)

## Slide 9: Low Z vs High Z Absorbers: Threshold vs Rate Tradeoff
Higher Z absorbers have smaller characteristic recoil energies 
Higher Z absorbers have more coherent rate enhancement 

## Slide 10: Light Mass Design Drivers: Energy Sensitivity
The primary design driver for Light Mass DM Experimental Searches is Energy Sensitivity

## Slide 11
Can we use other DM interactions that more efficiently transfer kinetic energy to target for MDM<100MeV?
?

## Slide 12: Trick 1) Use Bandgaps! Inelastic e- Recoils in Semiconductors
E= ½ vDM P
vDM ~ O(10-3 c)
E=1eV P~2keV/c
Energy [eV]
Momentum
4.5x10-10 m
P
1/4.5x10-10 m= 3 keV/c
Band Diagram for Si
Crystal e- Momentum and Energy Scales Match MeV DM
DM
<v>
vesc
Essig et al: 1108.5383

## Slide 13: Smaller Excitation Energies are Better
(Ultra-light Mediator)
Essig et al
1108.5383

## Slide 14: Sensitivity depends on Threshold
(Ultra-light Mediator)
Essig et al
1509.01598

## Slide 15: Ultralight Vector Boson Absorption
Pc = Mc2 (v/c)
Momentum << Energy
Semiconductors are a great target material for low energy dark photon absorption searches due
direct gap semiconductors (GaAs) preferable to indirect gap
Intuition -> photon absorption

## Slide 16: Trick 1b: Optical Phonon Production
Acoustic:
Optical:
An optical phonon excitation has a bandgap too … it kinematically matches light mass DM
Knapen, Lin, Pyle, & Zurek: 1712.06598
Momentum
Energy [meV]
Sapphire

## Slide 17: Dark Photon Couplings: Polar Crystals
In ionic crystals, optical phonons are oscillating electric dipoles!
Very large coupling to photons (black in the IR)… Very large coupling to the dark photons
Sapphire

## Slide 18: Sapphire: Lot’s of Optical Phonon Bands
To search for thermal DM down to keV masses via scattering and ultracold bosonic DM to 30 meV, we need a detector sensitive to a single optical phonon
Sapphire is a complex crystal with 10 atoms in its unit cell. Dark Matter can interact with lots of different modes

## Slide 19: Trick 1b: Bandgaps: Optical Phonons
Knapen, Lin, Pyle, & Zurek:
1712.06598
Acoustic:
Optical:
Optical phonon excitations kinematically match light mass DM

## Slide 20: Trick 2: Offshell 3 body scatters
Mn
MDM
Mn
Offshell
DM can scatter via production of 2 nearly back to back excitations
1604.08206: Schutz and Zurek
rate somewhat suppressed since offshell
Calculated for superfluid He only so far …
Hertel/McKinsey
Helium Coherent
Vibrational Modes

## Slide 21: Proposed Experiments Using Athermal Phonon Readout
Superfluid Helium
GaAs
Scintillation
1cm3 Polar &
Semiconducting Crystal
SuperCDMS SNOLAB
Upgrade
1607.01009
1802.09171
1712.06598
Molecular Absorption and Scattering
1709.05354

## Slide 22: Athermal Phonon Sensor Technology
Collect and Concentrate Phonon Energy into W TES
(Transition Edge Sensor)
R
T

## Slide 23: Step 1)Make An Ultra-Sensitive TES
Build and test simple TES test structures for noise is performance
  small volume TES more sensitive to both DM and environmental backgrounds (RF and vibrations)
Tc =68mK (a bit high)
Didn’t run the smallest TES … we were too conservative

## Slide 24: 50um x200um TES Characterization
TES Power vs TES Bias Voltage
TES Response to Square Wave Jitter
Bias Power: 0.25 pW
Time Response:
Simple 2 pole TES dynamical model perfectly fits response
TES falltime: ~20us (8kHz)
  we need to slow this down by x10 to match phonon collection bandwidth

## Slide 25: 50um x200um TES Noise
Noise matches theory to within x1.4
  Sptot = 2x10-18 W/rtHz
𝝂sensor ~ 8kHz
𝛔E = 72 meV (without collection losses …~20%)

## Slide 26: TES R&D
R&D Work Plan
  Lower Tc from 40mK -> 10mK. Since intrinsic theoretical noise, Sp= 4kbT2G ∝T6, energy sensitivity should improve by x43= x64
  Decrease TES linewidth
  Decrease environmental noise susceptibility
Energy Sensitivity: 40meV -> 1meV

## Slide 27: Step 2: Make the Athermal Phonon Sensor
Measured Phonon Collection Efficiency = 20% -> 40% (theoretical limit)
R&D Work Plan
  Optimize Collector/TES (W/Al) interface
  Improve quasi-particle trapping in collector fin

## Slide 28: Step 3: Fabricate Sensors on Crystal

## Slide 29: Current Progress: Large Area Photon Detector
  3” diameter Si wafer (45.6 cm^2)
  1mm thick
  Distributed athermal phonon sensors minimize phonon collection time (as fast as it can be for its size)
    Athermal Phonon collection time estimated to be ~20us
    2.5% sensor coverage

## Slide 30: Measured Performance: Tc & IV
  Tc= 41.5mK
  IV curves show that the detector and electronics are behaving well
    Rn = 88 mOhms (300mOhm Expected … TES too wide!)
    Rp = 8 mOhms
    Bias Power (P0) = 3.9 pW (1.4pW expected)
    Rn does not vary as a function of QET bias
Bias power flat in transition

## Slide 31: Measured Performance: dIdV
TES sensor pretty fast @ 60us. However, it’s not as fast as the estimated athermal phonon collection (20us)
Therefore, we expect phonon signals to have a 20us rise time (athermal phonon collection) and a 60us fall time. Seen for low energy comptons in average pulse shape!
Pulse shape varies with energy due to local TES saturation.

## Slide 32: Measured/Theoretical Noise
Noise ~x1.5 worse than theoretical expectations
Lots of lines from pulse tube and turbo pump
TFN seems too large …

## Slide 33: Integral Estimators for relative 55Fe calibration
Since pulse shape has significant variation with energy, we must use noisy but minimally biased DC estimators to fit the 55Fe calibration lines
Al Fluoresence @ 1.49 keV
55Fe K𝛼
@5.9keV
17% Athermal Phonon Collection Efficiency

## Slide 34: Calibrating Pulse Shape Dependent Energy Estimators to the DC estimator (Pulse Tube On)
Significantly Surpasses all Neutrinoless Double Beta Decay Performance Requirements of 10-20eV
𝜎E =3.5 ± 0.25 eV (stat)-0.7 (sys)
Baseline Resolution
+0.0

## Slide 35: Prototype Design Estimated Sensitivities
# TES | 100
TES Dimensions | 50um x 2um x40 nm
TES Rn | 320mOhm
Fin Length | 125um
W/Al Overlap | 15um
Fractional Al Coverage | 1%
Tc | 40mK
Bias Power | 48fW
Power Noise | 5.1e-19 W/rtHz
Phonon absorption time | 106us
Sensor fall time | 97us
Collection efficiency | 19%
σE | 219 meV
New 1cm3 Prototype Test Design
With a Si Absorber: single e/h sensitivity without Luke-Neganov gain. Can be used for inelastic electronic recoil DM
World Leading Elastic Nuclear Recoil DM search potential

## Slide 36: Excitation Detectors & Volume Scaling
PMT
Scintillator
Reflector
Will these detectors have the same energy sensitivity?
Yes, if:
Lifetime of the athermal excitation (photon) is really long
Excitation absorption dominated by sensor
Position Sensitivity
PMT
Scintillator

## Slide 37: Optimizing the Athermal Phonon Excitation Detectors
TES
Absorber
TES
Absorber
Minimize the number/volume of the TES sensors instrumented on the surface to the point that you begin to see the bare surface thermalization rate

## Slide 38: Athermal Phonon Thermalization at Surfaces
Athermal phonon surface thermalization probability found to depend upon
  Crystal
  Surface roughness
  Surface cleanliness
(W. Knaak et al, Phonon Scattering in Condensed Matter V,1986)
0.1%-1% of the crystal surface covered with athermal phonon sensors … 1/1000-1/100 thermalization probability needed

## Slide 39: Crystal R&D
Fabricate phonon sensors on variety of new substrates:
  Sapphire
  Niobium
  ?
Measure phonon themalization probability vs surface roughness

## Slide 40: Summary:
Athermal Phonon Detectors are a promising technique to search for 10meV-1GeV Dark Matter
Current Progress:
  3” large are photon detector 3.5eV resolution
  100x400um TES test chip: 40meV resolution
R&D Plan:
  Increase TES sensitivity: lower Tc
  Improve Collection efficiency: optimize W/Al interface
  Fabricate on a variety of crystal substrates
  Study how phonon surface themalization depends on surface roughness.

## Slide 41: Backup

## Slide 42: Calorimeter Sensitivity
~ Intrinsic Thermal Noise of Calorimeters

## Slide 43: Calorimeter Optimization
Minimize T
  Dilution Refrigerators can cool detectors to 5mK
Minimize C
  Small Volume
  Low T
  Insulators
Freeze out
}

## Slide 44: Engineering Blunder: Decoupling between the Sensor and Absorber
As T is decreased, it’s harder and harder to keep the sensor thermally coupled to the absorber
Energy leaks out of the absorber through Gab before its measured
TES sensitive to power fluctuations through Gtb
Physical clamps that support the absorber
e-/phonon thermal conductance scales as T4
Kapitza boundary conductance scale as as T3