## Slide 1: Summary Argonne workshop 14 August 2018
Marcel Demarteau & Dave Nygren
University of Texas at Arlington Argonne High Energy Physics Division
September 29, 2018 Fermilab, Batavia

## Slide 2: Background
LBNF/DUNE is the flagship program for the US with a significant capital investment that promises to make definitive measurements in the neutrino sector
Dave and I asked ourselves the question: Is the current technology optimized for DUNE to be a discovery machine, given that much is likely to be known in the neutrino sector when DUNE starts to take data?
We answered, for ourselves, that question in the negative.
A Brief Historical Perspective

## Slide 3: Background
LBNF/DUNE is the flagship program for the US with a significant capital investment that promises to make definitive measurements in the neutrino sector
Dave and I asked ourselves the question: Is the current technology optimized for DUNE to be a discovery machine, given that much is likely to be known in the neutrino sector when DUNE starts to take data?
We answered, for ourselves, that question in the negative.
Enter CPAD meeting at Caltech on October 13, 2017: “Must think out of the box! (perhaps over the cliff … )” Proof of Concept in IceCube: Clocks ±2 ns rms within 1 km3 of ice, with oscillator precision ~1 x 10–10/s
Decided to have a small ‘brain-storming’ workshop ….
A Brief Historical Perspective

## Slide 4: Workshop agenda
Aspirations of the Workshop
What are the current performance metrics ?
  single-phase, dual-phase, …
What are the limitations and challenges of the current technologies ?
What is needed to know whether pixelization is beneficial for FD optimization ?
Is it conceivable that FD pixelization is both technically possible and affordable?
What is the status and promise of current approaches to pixelization of LAr TPCs?
What is the sense of overall feasibility including schedule and demonstrators?
What actions should / should not be undertaken to understand opportunity ?

## Slide 5: metrics…
Defining The Metric for Pixel Readout (Jonathan)
For the Far Detector, to be able to move forward, the metric that demonstrates the scientific advantages of pixelated readout will have to be demonstrated quantitatively.
What other quantitative measures can we define for discovery science?
5-7 April 2017
5 years !

## Slide 6: Evolution of Signal Processing in MicroBooNE
Algorithmic Enhancement of Track Reconstruction (Xin)
MicroBooNE: JINST 13 P07006/P07007 (2017)

## Slide 7: Thoughts on Pixel Readout
Statistical uncertainty of charge determination
  Control electronics noise  low ENC
  Ability to filter electronics noise is desired  scheme of zero suppression
Systematic uncertainties of charge determination
  Field response
    Scheme of zero suppression, grid plane
  Electronics response
    Uniformity and calibration
  ADC performance
    Nonlinearity and calibration
Charge readout must respect the fully-active detector design
  No gap is crucial for subsequent pattern recognition steps
Requirements for Reconstruction (Xin)

## Slide 8: Event reconstruction
Comparing 2D vs 3D Reconstruction using ML (Roxanne)
Parameters of the study:
  BNB energy spectrum; peak at 800MeV, lower than DUNE
  No signal digitization for the pixels
  Noise not included
  2D: 3mm x 3mm; 3D 1.2cm x 1.2cm

## Slide 9: System aspects
Readout, Rates, Data Volume, … (Rick)
Assume 5 mm x 5 mm pixel → 500 x 1200 for DUNE APA = 600,000 pixels
10 MBq/cavern → 50,000 39Ar / APA volume / sec
  Pixel # - 20 bits
  Time – 32 bits (if 2 MHz clock, rolls over in ~ .5 hour)
  Charge – 8 bits
  → 8 B / hit → 400 kB/sec (peanuts!)
Take 64 channels per chip, ~10,000 chips per APA
Cheap circuit boards want to be < 22” x 22” so 0.5m x 0.5m PCB
  10,000 pixels per board → 156 chips/board and 60 boards per APA
Energy sensitivity down to near 39Ar level –so “trigger” at a few MeV or less, which sets a noise level of << 1,000 e-
Rate capability:
  assume nearby SN, >106 events in 10 sec so >> 1 hit per second per pixel
  Or, if track perpendicular to pixel plane ~ 100 hits in 0.5 ms
Required deep first stage buffer or readout at hundreds of kHz / hit – shared buffers in front end chip probably best but need simulation

## Slide 10: Photodetection
A Non-trivial Issue (Vishnu)
Light yield for Arapuca like design
Simulated dark matter density in a large cluster of galaxies, using ALCF

## Slide 11: Photodetection
A Non-trivial Issue (Vishnu)
SiPM possibilities
Xe doping, amorphous Se, … ?
Simulated dark matter density in a large cluster of galaxies, using ALCF

## Slide 12: conclusion
A Theory Program Poised for the Next Decade
We carry a responsibility as a community to optimize the DUNE detector for discovery
All current LAr projects are very informative and form the foundation for our current efforts looking into advanced technologies that may offer unanticipated advantages
There is a lot of common ground between the pixelated readout efforts for both the Near and Far detector
One of our goals today is to continue on the path set by the Argonne workshop to develop a coherent plan that advances pixelated readout for LAr as a pathway for maximum sensitivity to new physics at the threshold of detection