## Slide 1: Q-Pix: Pixel-scale 3-D Signal Capture for the DUNE Far Detector
David Nygren
University of Texas at Arlington
29 September 2018

## Slide 2
Available yesterday

## Slide 3: Q-pix
Goal: Optimized discovery potential !
LAr TPC: information quality is very high
  Technical pathway must:
    capture information without compromise !
    maintain intrinsic 3-D quality !
Aspiration: complete pixelization of DUNE FD
Immense FD scale  unorthodox solution
  Electronic principle of “Least Action”
  New approach: measure time-to-charge: ΔQ

## Slide 4: Q-pix
A genuine innovation for signal capture:
  Detailed waveforms provide:
    track profiles, track continuity, dE/dx, …
  Exploit 39Ar decays to provide:
    automatic absolute charge-energy calibration
High intrinsic single-point-failure resilience
   Electronics permanently immersed in LAr
  Allows maximal functional devolution
Novelty does not automatically confer benefit!
  Much remains to be explored…

## Slide 5: The Charge Integrate-Reset (CIR) Block
A = Charge sensitive amplifier
S = Schmitt trigger
Vth = threshold
“reset” switch
ΔQ = CfVth
Out = “reset”

## Slide 6: The “Advanced” (CIR) Block
A = Charge sensitive amplifier
S = Schmitt trigger
Vth = threshold
“reset” switch
ΔQ = CfVth ~ 0.7 fC
Out = “reset”

## Slide 7: Measure time of “reset”
Clock: local (within ASIC) oscillator free-running at 50 – 100 MHz
Basic datum is 64 bits: 32 bit time, pixel addresses, ASIC ID, …

## Slide 8: What’s new here?
Take the difference between sequential resets
This is the Reset Time Difference = RTD
Total charge for any RTD = ΔQ
RTDs are not generated at ASIC level;
RTDs are computed off-detector (GPU)

## Slide 9: RTDs capture the waveform !
RTD measures instantaneous current
  Small average current (background): Large RTD
    “Background” current from 39Ar is ~100 aA
  Large average current (signal): Small RTD
    Typical track current from min-I is ~1.5 nA
S/B ~ 107
Background and signal are easy to distinguish

## Slide 10: The two RTD patterns
Seconds
µs

## Slide 11: Signal Characteristics
Choose ΔQ such that Min-I track will cause several resets during one track arrival:
  Choose ΔQ = 0.7 fC
Signal: a contiguous sequence of small RTDs
A conventional current waveform of arbitrary length and complexity can be reconstructed from the RTD sequence.

## Slide 12
ΔQ ~1.0 fC

## Slide 13
ΔQ ~0.3 fC

## Slide 14: Signal capture: summary
RTD = inversely proportional to input current
Background: 39Ar decays lead to ‘heartbeat’
  heartbeat RTD ~11 seconds
  automatic absolute charge calibration
Signal: typically a few na,  RTD < 1 µs
  Five or more contiguous small RTDs
  Easy to recognize signal against background!
  No signal differentiation! (unlike induction wires)

## Slide 15: Time-stamping: how does that work?
One clock per ASIC, runs freely at f ~50 - 100 MHz
  No phase-locked loop
Requirement: Local clock must be stable:
  δf/f < 1 x 10–6 per second
Time-stamping routine:
  Once a second, ask ASIC “What time is it?”
  ASIC captures local time and sends it @ ~1Hz
  Simple linear transformation: T = AF/f + B
  F is master clock synched to GMT

## Slide 16: This method is proven to work !
Where has this idea been realized?

## Slide 17: This method is proven to work !
Where has this idea been realized?
IceCube: ±2 ns rms within 1 km3 of ice!
  works flawlessly and invisibly
Oscillator precision in IceCube is ~1 x 10 –10/s
  hard to measure
DUNE: ±1 µs precision
  requires δf/f < 1 x 10–6 per second for local clock
  This is probably easy to achieve in LAr

## Slide 18: IceCube: Digital Optical Module Block Diagram
FPGA
CPU
CPLD
Flash
Flash
PMT Power
SDRAM
SDRAM
ATWD
ATWD
fADC
DAC
Monitor
& Control
LPF
LC
x16
x2
x0.25
Flasher
Board
Pulser
DACs & ADCs
Corning Frequency Ctl (was Toyocom)
4Mb 4Mb
16Mb
16Mb
+/-5V, 3.3V, 2.5V, 1.8V
64 Bytes
Delay
Trigger (2)
ADC
Oscillator
20 MHz
40 MHz
MUX
(n+1)
(n–1)
DOR
OB-LED
x 2.6
x 9
10b
10b
10b
10b
8b
32b
16b
8b
8b, 10b, 12b
DP Ram
1 megabaud
DC-DC
Configuration
Device
8Mbit
GTP, LBNL, 26 Mar, 2004

## Slide 19: ASIC concept
16 -32 pixels/ASIC
1 free-running clock/ASIC
1 capture register for clock value, ASIC, pixel subset,
Buffer depth as needed to store beam, SN event…
State machine to manage:
  dynamic network,
  token passing,
  clock domain crossing,
  data transfer to neighbor in network,
  exception states (devils in the details)

## Slide 20: 16-Pixel ASIC
The local clock serves all pixels in one ASIC
View from inactive side
Wire-bonds connect
each pixel to ASIC; via connects to small button on active side, minimizing capacitance and noise.
Pixels are 4 x 4 mm2

## Slide 21
16 x 16 Tile of 256 ASICs, = 4092 pixels
Tile size:
256 mm x
256 mm

## Slide 22
Local clock interrogation
signal enters at any edge of tile, and propagates as a wave to any neighbor
here…

## Slide 23
Local clock interrogation
signal enters at any corner of tile, and propagates as a wave to any neighbor
Or here…
or any edge

## Slide 24: DAQ Concept
Once per second, introduce “time token” at one ASIC somewhere on the tile periphery
ASIC accepts token & offers it to all neighbors
ASICs remember who gave them a token
Wave propagates across tile and establishes a network for reverse data push
Dead or defective chips are bypassed by encircling wave of DAQ
  No master clock distribution + flat architecture
 Very high resilience against single-point-failure

## Slide 25: DAQ Concept
Once per second, introduce “time token” at one ASIC somewhere on the tile periphery
ASIC accepts token & offers it to all neighbors
ASICs remember who gave them a token
Wave propagates across tile and establishes a network for reverse data push
Dead or defective chips are bypassed by encircling wave of DAQ
  No master clock distribution + flat architecture
 Very high resilience against single-point-failure

## Slide 26: Data Flow
Clock calibration: once per second
   16,384 bits/tile
Assume 20,000 tiles/10 kton module
  ~40 MB/s per module
Easily digestible locally by GPU to transform data to global time frame & prepare histograms.
Very little data corresponds to real event data

## Slide 27: Three Central Technical Issues
CIR Input:
  all extraneous leakage currents at the CIR input node are small compared to 39Ar current
    This must be tested in a realistic setup…
Clock:
  Must be stable: δf/f < 1 x 10–6 per second
    I think this will be easy…
Surface Charge Creep:
  Must be negligible relative to 39Ar current
    This may require surface physics expertise…

## Slide 28: Perspective
IceCube demonstrated that it is rational to embed complex electronics in perpetuity
  care taken in design phase to avoid bleeding edge
  care taken in qualifying parts list
  care taken in fabrication & test
IceCube demonstrated that unorthodox time-stamp method meets high performance goals.

## Slide 29: Summary
Q-pix extracts energy, spatial and time information with high precision, exquisite detail and appropriate dynamic range.
The unorthodox Q-Pix scheme to realize a fully pixelized DUNE FD might provide advantage for discovery at the threshold of detection.

## Slide 30: Summary
Q-pix extracts energy, spatial and time information with high precision, exquisite detail and appropriate dynamic range.
The Q-Pix scheme, however unorthodox, to realize a fully pixelized DUNE FD might offer a unique advantage for discovery of new physics at the threshold of detection.

## Slide 31
Thank you

## Slide 32: Photon detection ?
Can the pixel surface also detect photons?
Wild speculation: coat surface with a-Se
  a-Se is a photoconductor (old copiers had it)
  VUV photon might liberate free electrons…
  Some avalanche gain will trigger some pixels that are near trigger point.
  Look for clustering of Hits in time  S1 signal
Far-fetched, but would be fabulous if real

## Slide 33: The 64-bit datum
Clock value 38 bits
ASIC location 8 bits
Pixel address 16 bits
Flags 2 bits
Total: 64 bits
Datum is always the same format

## Slide 34
Simulation of this idea at U Penn – Mitch Newcomer et al

## Slide 35: The pixel “button”
The pixel must be a small button exposed to LAr active volume, not a space-filling square
The dielectric surface exposed to LAr active volume will automatically ‘heal” to create the desired electrostatics: “all charge to button”
 Dielectric properties of first dielectric surface are important: teflon, …