Top Quark Mass and Cross Section Results from the Tevatron
Ford Garberson, UCSB
On Behalf of the CDF and D0 Collaborations

---
The Tevatron
Collides pp at 1.96 TeV
  - Still world's highest energies!
  - Two multipurpose detectors, CDF and D0
Beam luminosity has been steadily improving
  - Total of ~4 fb-1 has been delivered to each detector
    - About 80% data acquisition efficiency
    - Recent analyses use about 2 fb-1
  - Recently accumulated more than 50 pb-1 in one week!
[Speaker Notes: Can probably scale this out mostly.]

---
The Detectors
Both detectors have a similar design
  - Geared to study and search for all kinds of different phenomena
  - Tracking inside of calorimetry inside of muon systems
Specialties
  - CDF has very good central tracking
  - D0 has very good muon coverage
Muon Systems
Calorimetry
Tracking
[Speaker Notes: CDF detector: lead/scintillator CEM, FE/scintillator CHA, gas Cherenkov luminosity detector D0 detector: silicon microstrips surrounded by scintillating fiber tracker. Carlorimeter is uranium metal in liquid argon (argon produces electrical signal). Plastic scintillator used to measure luminosity.]

---
The Top Quark
Have produced thousands of tt events at the Tevatron
  - Are they all Standard Model top?
  - Measure cross section: check for consistency & SM deviations
The top quark mass can teach us about the Higgs
  - The top quark and the Higgs both couple to the W boson
  - Top mass and W mass determine SM Higgs mass
    - Measure to constrain Higgs mass
    - Test of standard model
1-Sigma Constraint on
Higgs mass (2006)
Higgs and top quark couplings to W boson

---
tt Production
The top ~always decays to Wb
  - W can decay leptonically or hadronically
  - Usually focus on electron or muon lepton decays
Signature:
  - Dilepton Channel: two leptons, two neutrinos, two b-quarks (5 %)
  - Lepton+Jets Channel: one lepton, one neutrino, four quarks (two b's) (29 %)
  - All Hadronic Channel: six quarks (two b's) (44 %)
  - Look for the appropriate particles to find ttbar events

---
Identifying tt
In practice we might see something like this
  - Is it tt?

---
b-Identification (Tagging)
Identify b's to understand events
Many possible approaches
  - Displaced vertices (use long lifetime of b's) (favored by CDF)
  - Neural Network (favored by D0)
    - Uses displaced vertex and other track and jet information
  - Look for “soft” leptons
    - Electrons or muons often in b-decay chain
    - Less efficient, but complementary information
Can identify b's from displaced secondary vertex

---
Identifying tt
This event can be b-tagged by eye (soft muon tagging)
  - So this is probably an electron+jets tt event

---
Cross Section/Mass Connection
Measure cross section from excess of events in data
  - Normalize by efficiency, acceptance, luminosity
A more massive top quark is harder to produce
  - Expect cross section of ~6.7 pb for top mass of 175 GeV/c2
Can indirectly determine mass from a cross section measurement
  - And vice versa
  - D0 results with 0.9 fb-1 of data
D0 With world average top mass
(172.6 GeV/c2)
D0 Measured vs theoretical cross sections:

---
Cross Section in Dilepton Channel
Dileptons channel statistically limited so can loosen cuts
  - Loosen cuts on one lepton: “lepton plus track analysis”
  - Can choose not to b-tag
Have to contend with Drell Yan and W+fake lepton backgrounds
  - For no b-tag with lepton+tracks cuts signal fraction ~60-70%
  - With b-tagging and dilepton cuts background fraction can drop to ~10% with loss of half of statistics
CDF Lepton + Track Results
One Jet Events only allowed for e+mu case
D0 Dilepton Results

---
Using Alternate/No b-tagging in LJ Channel
Using no b-tagging:
  - D0: kinematic likelihood fit using angles, momentum sums, and event shapes
    - Better systematic, worse statistical error than for b-tagging
  - CDF: neural network based on similar kinematic variables
Using soft lepton tagging
  - Electrons or muons inside of jet
  - Veto if consistent with dilepton decay from Z, J/Psi, or double semileptonic decay
D0 Likelihood Discriminant (0.9 fb-1)
D0 Likelihood+b-tag Combination (0.9 fb-1)
CDF Neural Network (no b-tagging) (0.8 fb-1)
CDF Soft muon tagging (2.0 fb-1)
CDF Soft electron tagging (2.0 fb-1)
[Speaker Notes: D0: fit based on likelihood discriminant involving sphericity, aplanarity, angles between jets, leptons and missing energy, and momentum sums.]

---
Tauonic Cross Sections
Can also study tauonically decay channels
  - Much larger backgrounds
  - Cross section excess: possibly a sign of charged Higgs decays
  - Consider all hadronically decaying tau types
  - Analyses with 1.0 and 1.2 fb-1 performed and combined
D0 Lepton+Tau Channel: (2.2 fb-1)
Taus separated from jets and electrons with neural networks depending on ...
  - Shower shape, cluster energies, track-calorimeter agreement
D0 Tau plus Jet channel: (0.4 fb-1)

---
All Hadronic Cross Section
Have to contend with enormous QCD background
  - B-tagging essential
Also use Neural Network event selection to reduce background
  - sum ET, event shape information, parton angles
  - Measure angles based on center of mass frame of all jets
  - Extract backgrounds based on b-tag and mistag rate parameterization from 4-jet control region
CDF Neural Network Output
CDF Results, 1.0 fb-1
D0 Results, lifetime b-tagging, 0.4 fb-1

---
Cross Section Summary
Both collaborations find results consistent with standard Model expectations

---
Determining the Mass
Event reconstruction challenges:
  - Which partons came from which top and which W?
Jet reconstruction challenges:
  - Are you reconstructing the complicated data in your calorimeter towers correctly?
  - Does your Monte Carlo reconstruct jets consistently?
  - Left with the Jet Energy Scale (JES) uncertainty of ~3-4 GeV on top mass
    - Largest uncertainty on world average top mass
Which jets belong to which invariant mass?
Calibrated JES Uncertainties

---
Controlling the JES Uncertainty
Option 1: Perform “in-situ” JES calibration
  - Require the W mass to reconstruct correctly
  - Assume all other jets have same Jet Energy scale uncertainty
  - Do simultaneous fit to top mass and JES
    - Uncertainty becomes statistical
Residual systematics remain (~0.8 GeV)
  - JES for b-jets vs light flavor jets
  - JES variation based on jet properties
MT Dependence on JES
Example of a Simultaneous Fit

---
Controlling the JES Uncertainty
Option 2: directly measure top mass using quantities unrelated to jet energy
  - Decay length of b-tagged jets
  - Transverse momentum of leptons
  - These measurements should have minimal correlation to other mass analyses
  - Statistical limitations will be no problem at the LHC
    - Systematic uncertainties should also improve with statistics
Only JES dependence is through jet energy event selection cuts
  - Methods could easily be applied to dilepton channel
CDF Lepton Transverse Momentum Results
Results with 1.9 fb-1
in Lepton+Jets Channel:
CDF Decay Length
CDF Lepton Transverse Momentum
Combined

---
Template Based mT
Template Method
  - Make probability distribution functions (templates) for signal and backgrounds
    - Fit data, integrating over all allowed jet and lepton combinations
Signal chisquare for CDF Lepton+Jets analysis
Unclustered Energy Constraints
Measurement Constraints
mT Constraints
mW Constraints

---
CDF Template Method Results
In-situ JES calibrations performed
All-hadronic channel: CDF uses same neural network as for cross section measurement
  - Parameterize templates with Gaussian+Lorentzian fits
CDF Combined Dilepton
and L+J Results (1.9 fb-1)
CDF All Hadronic Results (1.9 fb-1)
CDF Combined Dilepton L+J
Likelihood Results
CDF All Hadronic Mass
Templates
[Speaker Notes: All Hadronic channel uses same event selection as for cross section]

---
Dilepton Template Mass
Template Method (Neutrino Weighting)
  - Integrate over unknown pseudorapidities of neutrinos
  - Weight solutions by agreement with Missing ET
Template Method (Matrix Weighting):
  - Weight solutions by consistency with lepton energies and PDF
  - D0: Smear momenta within detector resolution
CDF Dilepton Neutrino Weighting
D0 Matrix and Neutrino Weighting Combined (1.0 fb-1)
CDF Neutrino Weighting (1.9 fb-1)
D0 Matrix Weighting Results
[Speaker Notes: All Hadronic channel uses same event selection as for cross section]

---
Matrix Element mT
Attempt to extract more information from each event
  - Find mass likelihood event by event based on signal probability from theoretical Matrix Element calculation and background probability
  - Integrate over all unknowns with probabilistic weighting
  - Example: D0 Lepton plus jets measurement
Signal Probability Proportional to ...
Transfer Functions: Probability of observing momenta x given real momenta y and JES
Parton Distribution
Functions
b-tagging probability
Sum over jet and flavor combinations
Matrix Element from theory

---
Matrix Element mT
Evaluate total mass probability simultaneously with JES and signal fraction
  - In-situ JES calibration performed where possible
  - Expression for background probability uses different Matrix Element (no mass dependence)
D0 Lepton+Jet Results
CDF Dilepton (1.9 fb-1)
D0 Lepton+Jets (2.1 fb-1)
CDF Lepton+Jets (1.9 fb-1)
CDF All Hadronic (1.9 fb-1)
CDF All Hadronic Results
[Speaker Notes: All Hadronic channel uses same event selection as for cross section]

---
Mass Combinations
D0 Mass Combination
CDF Mass Combination
D0 Results since Combination

---
D0+CDF Combination
Using Best Linear Unbiased Estimator technique
  - Correlations estimated between 12 types of uncertainties
Electroweak fits: SM Higgs mass now < 160 GeV/c2 at 95% confidence level!
  - With LEP lower limit of MH>114 GeV/c2: upper limit rises to 190 GeV/c2

---
Future Improvements
Cross section results will continue to improve with statistics
  - All channels stand to benefit
Mass results are now more systematically limited
  - But even without systematic improvements will have better than 1% precision at both experiments
  - Work on improving systematics still ongoing
    - Have a good track record of success: already far ahead of where we projected we would be at this luminosity!
Past Expectations and Future MT Projections at CDF

---
Summary and Outlook
Cross section results are precise in some channels
  - But others could still be hiding non tt physics
  - Can push these uncertainties down with higher statistics
Top mass known to high precision, but work remains
  - Understanding the Higgs will take further improvements
  - With higher statistics can greatly reduce the jet energy scale uncertainty in all channels
    - Using in-situ calibration and alternate variables
  - QCD radiation uncertainties will play a larger role
  - New, subtle uncertainties will have to be understood
  - Are we really measuring the pole mass?