## Slide 1: DSS Update
Victor Guarino

## Slide 2: DSS Feedthrough Diameter
Currently 250mm outside dia crossing tube – proposed to go to ~150mm dia
Sizing of the DSS tube depends on:
  Stiffness/strength of tube to resist lateral loads
  Space available to accommodate shrinkage and location adjustment
Small Tube (~125mm dia) has less stiffness but feedthrough has been lowered which decreases moment arm.
  Smaller/shorter tube can resist 700 lbs with 3mm deflection so is ok

## Slide 3: DSS Feedthrough Diameter Clearance for Shrinkage and Adjustment
Need 17mm clearance for shrinkage
Currently have +/- 25mm adjustment to accommodate Feedthrough placement
If clevis is extended outside of tube it might be possible to keep adjustment. Constraint block has to be extended.
Loose hole for installation

## Slide 4: Changes
S8 beam changed to W10 beam
APA weight increased from 1048kg to 1241kg
Analysis re-run
Detector Layout redone (see docdb 6260)

## Slide 5: Weights

## Slide 6: Impact of larger beam
DSS is closer to ceiling in order to maintain detector height
Greater DSS weight
Greater margin on strength:
  Allowable moment 62.5 kip-ft
  Load factor of 1.4 results in a Max moment is 24.2 kip-ft so a margin of 3.2
Smaller deflections

## Slide 7: Deflections
Chart: APA Center Support Deformations
Dry | -4.892 | -2.7328 | -0.60935 | -4.3129 | -0.97892 | -1.8946 | -3.9688 | -0.05207 | -3.6281 | -4.0985 | 0.008128 | -3.5334 | -2.3338 | -0.46228 | -4.2809 | -1.1689 | -1.7226 | -4.077 | -0.12522 | -3.4402 | -4.2174 | -0.035306 | -3.3584 | -2.445 | -0.53746
Wet | -3.8809 | -2.1011 | -0.43586 | -3.0739 | -0.6985 | -1.35 | -2.8245 | -0.047498 | -2.5999 | -2.9367 | -0.017272 | -2.509 | -1.6607 | -0.33198 | -3.051 | -0.83388 | -1.2281 | -2.903 | -0.097028 | -2.4651 | -3.0216 | -0.053848 | -2.382 | -1.7384 | -0.41453
Chart: CPA Center Support Deformations
Dry | -2.4331 | -3.2642 | -2.5291 | -0.59715 | 0.30023 | -1.1788 | -2.3592 | -2.4534 | -1.3927 | 0.16561 | -0.29566 | -2.129 | -2.9606 | -2.3693 | -0.63043 | 0.32664 | -1.1242 | -2.3282 | -2.4684 | -1.4425 | 0.12675 | -0.23647 | -2.0752 | -2.951 | -2.4094 | -0.69723 | 0.34976 | -1.0693 | -2.2941 | -2.4798 | -1.491 | 0.086106 | -0.17831 | -2.0196 | -2.9378 | -2.4463 | -0.76378 | 0.36982 | -1.0145 | -2.257 | -2.4879 | -1.5375 | 0.043942 | -0.12167 | -1.9616 | -2.921 | -2.4803 | -0.82931 | -0.55702 | -0.25756
Wet | -2.4087 | -3.1435 | -2.398 | -0.55118 | 0.26238 | -1.0226 | -2.047 | -2.1285 | -1.208 | 0.14478 | -0.25654 | -1.8435 | -2.5634 | -2.0516 | -0.54635 | 0.28575 | -0.97511 | -2.0198 | -2.1415 | -1.2512 | 0.11074 | -0.20523 | -1.7968 | -2.555 | -2.0861 | -0.60427 | 0.30632 | -0.92735 | -1.9903 | -2.1516 | -1.2934 | 0.075438 | -0.15469 | -1.7485 | -2.5436 | -2.1184 | -0.66192 | 0.3241 | -0.87986 | -1.9586 | -2.1587 | -1.3338 | 0.038608 | -0.10566 | -1.6988 | -2.5293 | -2.1478 | -0.71882 | -0.46152 | -0.28346

## Slide 8: Detailed FEA
Solid Model of Beam/clevis/rod/swivel for greatest loaded beam
  Detailed

## Slide 9
1.16m

## Slide 10
Axial
Shear
Moment