## Slide 1: Obtaining a Single Electron in IOTA
Aleksandr Romanov
9 November 2018

## Slide 2: IOTA accelerator complex
IOTA gets electrons from the FAST, 1.3 GHz superconducting RF electron linear accelerator
  Beam energy to IOTA: 40-200 MeV
  Bunch charge: 1e- to 3 nC (160 pC nominal)
  Injection frequency: up to 5 Hz

## Slide 3: IOTA layout

## Slide 4: Parameters
Momentum | < 200 MeV
Perimeter | 40 m
RF voltage | <1 kV
RF frequency | 30 MHz & 7.5 MHz
3 Experimental gaps | 2x180 cm, 1x150 cm
Main vacuum chamber aperture (R) | 25 mm
Lambertson and kickers aperture (R) | 20 mm
Electrons | 109 e, 1.2 mA
Protons | 1011 p, 35 mA
Vacuum | 6x10-10 torr

## Slide 5: Main components
Lambertson magnet |  | 1 | Horizontal, injection in vertical plane
Kickers |  | 1 hor. & 1 vert. | Horizontal for studies only
Main dipoles |  | 4x60 deg & 4x30 deg | Powered in series with Lambertson
Quads |  | 39 | Powered in pairs with individual shunts
Trims | Hor. | 8 | In main dipoles
 | Vert. | 2 | For injection bump
 | Hor. | 20 | Combined correctors
 | Vert. | 20 | 
Skew-quads |  | 20 | 
Pickups |  | 21 | Turn-by turn position
Sync. light monitors |  | 8 | Shape and position
RF |  | 1 | Dual frequency
Solenoid |  | 1 | For electron and McMillan lenses
Sextupoles |  | 12 | In six families

## Slide 6: Lattice configuration: one nonlinear magnet (1NL)
Momentum | 150 MeV
Tunes, x,y | 5.3, 5.3
Mom. comp. | 0.032
Emittances, x,y | 1.65 E-6 cm
Bunch length @1kV | 7.5 cm
Energy spread | 1.35 E-4
Sync. Tune @1kV | 3.7 E-4
Damp. times (x,y,s) | (0.8,0.8,0.3) s

## Slide 7: Lattice configuration: one nonlinear magnet (1NL)
Momentum | 100 MeV
Tunes, x,y | 5.3, 5.3
Mom. comp. | 0.032
Emittances, x,y | 0.74 E-6 cm
Bunch length @1kV | 4.1 cm
Energy spread | 0.90 E-4
Sync. Tune @1kV | 4.5 E-4
Damp. times (x,y,s) | (2.8,2.8,1.0) s

## Slide 8: Lattice correction
Extended LOCO method of beam based model dependent analysis and correction using Sixdsimulation will allow to have online correction capabilities.
  Fit model so that it best describes measured experimental data using multiple iterations of SVD based inverse task solver.
Simulations shows that with BPMs precision of 1um and better lattice can be corrected to required levels.
Recent work demonstrated that it
should be possible to correct lattice
parameters to required precision
(THPOA24, NAPAC 2016)
Parameter | Max error
Betas at the insertion | 1%
Beta beating | 3%
Dispersion | 1 cm
Phase adv in T-ins | 0.001

## Slide 9: Injection
Protons fill all injection channel (d=15 mm)
Aperture limitations
  20 mm radius in Lambertson
  20 mm radius for plates in kickers
Kicker strength limited to equivalent of 70 G for electrons and around 500 G for protons
Field in combined correctors limited to 120 G
Field in bump correctors limited to 1 kG

## Slide 10: Injection: electrons
Clearance (Y): | 3.8 mm | 18 sigmas

## Slide 11: Matching beam from FAST into IOTA
Several iterations of the following steps are necessary to achieve desired parameters:
  Manual propagation of the beam as far as reasonably possible
  Measurement of the beam parameters
  Adjustment of the nominal lattice to get desired beam parameters at specified location
  LOCO based correction of the focusing elements
  Centering of the trajectory in focusing elements
  Verification of the beam parameters close or at the point of interest

## Slide 12: FAST beam characterization
Beam conditions after CC2
  Slits
  Single quad scan
  Beam phase space tomography
Beam parameters before D600 (close to IOTA):
  Multi-quad scan

## Slide 13: Tuning quads in FAST
LOCO integrated with ACNED by Sixdsimulation
Fit model to measurements
Implement correction

## Slide 14: Betatron capture into IOTA
Model lattice and corresponding sample responses compared to measured
First correction iteration made stable betatron lattice
Fitted model has clear instability in X plane
Measured data: 21 BPMs x 20 trims
Model adjusted to match measured data by tuning 39 quads

## Slide 15: Single electron injector
Block laser with shutter to get only dark current
Insert several OTR foils in LE and HE lines
Decrease last injection quadrupole to stretch phase volume and distort incoming trajectory
x
x

## Slide 16: Single electron capture probability
To test selected method of intensity attenuation 53 injections were done with interval of 21 seconds
Resulting probability of single electron injection: 32%
  For purely Poisson distribution maximum probability is 36.8%

## Slide 17: To be continued…
Technical goal of reliable injection of a single electron into IOTA is achieved.
Diagnostics tools are in good shape and continue being developed
A lot of interesting experiments are imminent!

## Slide 18: Single electron in IOTA: “Rectangular” beam
Real time footage from M2R camera after specially developed noise cancellation algorithms
  Clearly visible “stopping” points due to integration time of less than damping time

## Slide 19: Planned experiments
1,2,3… electron tomography in 3D using 8 cameras
  Knowing exact number of particles will allow to recover their amplitudes in 6D phase space from 2D images
    May be possible to recover phase by adding fast diagnostics tools
Looking at correlations
  Random walk due to synchrotron radiation
  Gas scattering
  Intrabeam scattering for 2,3... electrons