## Slide 1: Detector Component packaging for underground transport
J Stewart

## Slide 2: DAQ
The DAQ consists primarily of servers and other commercial off the shelf electronics that fit in electronics racks. At present I assume these will be transported underground in stacked pallet boxes.
Cables will be transported underground on pallets.
Fibers may be transported in crates

## Slide 3: Detector Support
DSS Feedthru will be packaged on pallets. Roughly 11 pallets are needed. These will not be reused
I-Beams: These are 6.4m long and must be slung loads. Present thought is that the beams will be bolted to a frame used to transport underground. The frame will be re-used for the 8 trips needed.
Misc: Pallets will be used for miscellaneous parts.

## Slide 4: End Wall
The 32 endwall field cages panels will be transported underground in painted wood crates. 4 trips are needed. The crates will not be reused.
Miscelaneous equipment will be brought down on pallets.

## Slide 5: APA
APA will be brought underground two at a time in a custom transport box as a slung load.
Yoke, linkage, and miscellaneous will be transported on pallets

## Slide 6: Field Cage Modules
The FC top/bottom modules will be transported underground in custom crates as sling loads. 50 trips total are needed. The crates will be painted wood.
The ground planes have not yet been decided.

## Slide 7: Cathode Planes
The cathode plane panels will be vacuum packed inside custom painted wood crates. These will be sling loads.

## Slide 8: SP Cold Electronics
The cables will be transported underground on pallets. The pallets can b re-used.
Cable trays will come underground crates.
WEC will be transported on pallets.
Miscellaneous equipment will come underground on pallets or in pallet boxes.
The large Tees will be transported on pallets.

## Slide 9: SP Photon
The photon detector paddles will either be installed at the ITF or underground. If they are installed underground they will be transported in custom dark transport crates.
The readout electronics and cables will be transported in stacked pallet boxes.
Installation and test equipment will be transported in crates.

## Slide 10: CISC instrumentation
The equipment will be transported underground on pallets or in stacked pallet boxes.
Some longer pieced will need crates.

## Slide 11: CRP
Will be transported underground in custom transport crates. The crates fit in the cage.
Misc test equipment will be transported underground on pallets or in stacked pallet boxes.

## Slide 12: DP-Slow Control System
The system consist primarily of rack mounted electronics modules. These can be transported underground in stacked pallet boxes.

## Slide 13: DP-FC
Parts will be transported underground in crates and the FC assembled underground.
I-Beams will need transported as slung loads similar to the SP.
Most crates will fit in the cage.

## Slide 14: DP PD
The DP photon sensors will be brought underground in custom dark crates.
DP electronics will be brought underground the same as the DP electroncis

## Slide 15: DP electronics
Chimneys will be brought underground in crates that fit in the cage.
The ATCA crates will be brought underground on pallets.
The power supplies will be brought underground either on pallets or in stacked pallet boxes.