## Slide 1: LBNF cryostat structure qualification strategy
O. Beltramello – 23.08.2018

## Slide 2: Reminder … October 2015 - MoU signed between CERN and Fermilab, EDMS 1554082 - Design, Fabrication, Installation and Testing of the LBNF/DUNE and SBND Membrane Cryostats
Reference for the design, manufacturing and testing of all membrane cryostats of LBNF/DUNE and SBND programs. The main points are: - US ANSI/AISC 360 (latest edition) “Specification for Structural Steel Buildings” applies to the design and construction of the support structure. - the warm steel supporting structure design is performed per the European standard for steel structure design and construction EN1993 - EUROCODE 3 (equivalent to ANSI/AISC360). - the design approach is to generate a detailed FEA model of the vessel and to perform a detail stress analysis of each component. - The level of safety per ASME Boiler and Pressure Vessel Code, Section VIII, Div. 2. is demonstrated to comply with the U.S. DOE 10 CFR 851.

## Slide 3: Reminder … October 2015 - MoU signed between CERN and Fermilab, EDMS 1554082 - Design, Fabrication, Installation and Testing of the LBNF/DUNE and SBND Membrane Cryostats
Prior to each testing campaign:
a risk assessment is performed to verify personnel and equipment safety during the tests.
the respective authorities of the host laboratory performs an internal review. Their approval is mandatory prior to each test. 1. Destructive tests for the weakest structural part of the steel frame in order to validate the FEA model and the structure mechanical behavior. 2. Prior to the Liquid Argon filling process, a pneumatic test is performed at a testing pressure PT: PT = 1.15 x Maximum Allowable Working Pressure = 1.15 x 350 mbarg. 3. Fill of the cryostat with liquid argon in incremental steps until the service level.

## Slide 4: LBNF cryostat qualification strategy
We plan to proceed for LBNF warm structure qualification with the same strategy than for the ProtoDUNEs.
1.Warm structure design (see design review August 2017)
The structural analysis of the vessel have been performed following the MoU requirements.
Validation performed per Eurocode 1993 (equivalent to AISC360)
The sizing loads are:
  operational : self weight + LAr hydrostatic load + 350 mbar overpressure
  exceptional : seismic load case
Verification done for ASME VIII division 2

## Slide 5: LBNF cryostat qualification strategy
2. Cryostat warm structure will be manufactured and assembled following EN1090 - 2 providing requirements for the execution of steel structures, to ensure adequate levels of mechanical resistance and stability, serviceability and durability.
NP04 warm vessel structures follows a strict QA / inspection / testing plan as per EN1090 (i.e. quality of the welds execution attested by an authorized independent inspection agency) .
3. GTT containment system is designed following EN 14620 parts 1 to 5
4. An extensive leak testing campaign will be performed for the primary and the secondary membrane including penetrations as per the ProtoDUNEs.
5. The most loaded structural elements have been tested under design loads (and above). See Dimitar talk.

## Slide 6
Before start of cryogenics commissioning phase: Pressure test @200 mbarg
(estimated stored energy equivalent - 40 Kg of TNT).
Based on NP04 experience, an exceedance of :
  200 mbarg (set pressure of the automatic vent valve)
  and 350 mbarg (safety valve)
is considered very low probability for all commissioning and operation phase.
The cryogenics of NP04 has shown an impressive stability.
This test will validate :
    the cryostat structure for 200 mbarg
    the FEA model for the gas load case.
The cryostats will be instrumented with displacement sensors and strain gauges.
The plan of instrumentation will be based on the experience from NP04, NP02, ICARUS, SBND and DarkSide in collaboration with Coimbra University.
Dedicated FEA models will be created based on the knowledge from NP04 testing campaign.
Qualification steps during LBNF Cryogenics Commissioning

## Slide 7
2. As per NP04 and NP02 the cryostat will be filled in steps, with a maximum
overpressure set at 50 mbarg (which corresponds to 9.5 Kg of TNT).
A continuous monitoring of the SG and displacement sensors will be required.
This will be part of the safety measures to be put in place for people working in the vicinity of the cryostat.
3. Specific overpressure tests can be envisaged at certain level of filling (for example half filling) in order to check the FEA models for the filling case.
Overpressure should not exceed 200 mbarg.
4. A final test will be performed for the LBNF cryostats full of LAr at around 200 mbarg.
5. The FEA models will be validated and as per NP04, an estimation of the maximum loads and stresses will be done for the design case and a final verification of the
EU and US regulation will be performed.
Qualification steps during LBNF Cryogenics Commissioning