## Slide 1
US-JP Collaboration Memory
&
Silicon-On-Insulator Pixel R&D
April 15, 2019 @ Univ. of Hawaii
Yasuo Arai
High Energy Accelerator Research Organization (KEK)
yasuo.arai@kek.jp, http://rd.kek.jp/project/soi/
The 40th Anniversary Symposium of the US-Japan Science and Technology Cooperation Program in High Energy Physics

## Slide 2
Preamble
US-JP Collaboration

## Slide 3
My First Memory of the US-JP Program
1982 Visit Mark-II group at SLAC for studying FASTBUS system
Martin Breidenbach
Mark-II Control Room

## Slide 4
Roommate at SLAC
Andy Lankford
Nigel Lockeyer
Marc Ross
Success in TRISTAN FASTBUS DAQ System
MC68000 FASTBUS Master Module

## Slide 5
1986~1994 (SSC Era)
R&D for High Rate Tracking Detector & Readout LSI
Brig Williams
Jay Chapman
G. Hanson
H. Ogren
1990 visit NTT LSI Lab.
Time Memory Cell (TMC) LSI
Used in ATLAS Muon Readout

## Slide 6: Development of Advanced Pixel Detectors in SOI Technology
Japanese Central Researcher: Yasuo Arai High Energy Accelerator Research Organization (KEK)
and
US Central Researcher: Marco Battaglia University of California at Santa Cruz & LBNL
US-JP program: FY2009-2014

## Slide 7
Silicon-On-Insulator Pixel Detector (SOIPIX)
Monolithic Detector having fine resolution of silicon process and high functionality of CMOS LSI by using a SOI Pixel Technology.

## Slide 8
2008 US members visited OKI Electronics Co. fab. (currently Lapis Semiconductor Co.)
Marco Battaglia
Peter Denes

## Slide 9
[JAPAN]
KEK, Tsukuba Univ., Osaka Univ., Tohoku Univ., Kyoto Univ., JAXA/ISAS, Univ. of Tokyo, Riken
[US]
LBNL, FNAL, U. of Hawaii
Collaboration meetings
Mar. 2012 @LBNL
Mar. 2010 @Fermilab

## Slide 10
MPW (Multi Project Wafer) run
~Twice / year.
Louvain-la-Neuve Univ.
INP Krakow
U. Heidelberg
IHEP China
U. of Hawaii
U. Tohoku
Kyoto Univ.
Tsukuba Univ.
JAXA/ISAS
AIST

## Slide 11
FWHM 200 eV
(Kyoto U. , Shizuoka U., …
X-ray Astro Physics
XRPIX (SOIPIX-PDD)
High Gain (70 mV/e-)
Good Energy Resolution (Noise = 11.0 e-)
High Charge Collection Efficiency (No X-ray tail)
No tail
X-ray Energy Spectrum
Notes: This 55Fe X-ray spectrum is obtained with the SOIPIX-PDD detector. This is old spectrum obtained in previous SOI detector. By comparing the spectrum, you can find there is no tail below the peak. This implies the charge collection efficiency is almost 100%.

## Slide 12: Silicon-On-Insulator PHoton Imaging Array Sensor (SOPHIAS)
○
Higher Peak Signal Density
World highest peak signal density is obtained.
Pixel Size[mm2]
Peak Signal[phs@6keV]
0.008 nm-1
３ｍｍ

## Slide 13
scint.
(view from downstream)
Vertex Detectors: High-Energy Beam test @Fermi Lab.
Two kinds of SOIPIX-DSOI detectors are used:
FPIX2 x 4: 8 mm square pixel detector
SOFIST(v.1 & 2) x 2: 20 mm square pixel detector
Proton Beam (120 GeV/c)
Proton
Notes: For high-energy charged particle tracking, we have performed beam test by using 120 Gev/c Proton beam at Fermi National Laboratory at Chicago. We put 4 FPIX2 detectors and 2 SOFIST1 detectors in a line.

## Slide 14
Less than 1 mm Position Resolution for high-energy charged particle is achieved first in the world !
(K. Hara et al., Development of Silicon-on-Insulator Pixel Detectors, Proceedings of Science, to be published)
Tracking Resolution
FPIX
SOFIST
Detector | Pixel size | Resolution
ATLAS Pix | 13.75 mm | 1.1 mm
DEPFET | 24 mm | 1.4 mm
SOFIST | 20 mm | 1.2 mm
FPIX | 8 mm | 0.65 mm
FPIX2
Notes: By subtracting track position in DUT from obtained track from other detector we can make residual plot. This corresponds to position resolution of the detector. We could get less than 1 micron track resolution first in the world.

## Slide 15
ILC Vertex Detector R&D : SOFIST
(SOI sensor for Fine measurement of Space & Time)
Gain: 32 mV/ke- (@Cf=5fF)
Analog signal memories: 3 for signal or 3 for time
Column-ADC: 8 bit
Zero Suppression Logic
3 kinds of multiple memories in a pixel: Hit, Charge, Time

## Slide 16
Lower
Upper
 | Ver. 3 (2D) | Ver. 4 (3D)
Chip Size | 6mm x 6mm | 4.45mm x 4.45mm
Pixel Size | 30mm x 30mm | 20mm x 20mm
Pixel Array | 128 x 128 | 104 x 104
Circuits | CSA + Comp.+ 3 Analog Mem + 3 Time Stamp Mem | 
Wafer | FZ p-type (3~10 kW•cm) Double SOI | 
New SOFIST Chips (Ver. 3 & 4)
Designed at the same time.
Same circuits.
2D
3D

## Slide 17: Position and Time Measurement
β –ray track from 90Sr
Threshold: Vth = 950 mV, VRST = 900 mV
HV = -100 V
Successfully measured Charge and Time simultaneously!
SOFIST Ver. 3

## Slide 18
3D Vertical Integration (SOFIST Ver. 4)
Lower Tier
Upper Tier
Micro Bump

## Slide 20
High R-Si
Upper Tier
Lower Tier
High R-Si
Back gate adjust electrode
Passivation
Bond Pad
3D Integration
T-Micro
Upper and Lower Tier chips are produced in a same wafer and bonded chip to chip.
SOFIST Ver. 4

## Slide 21: SOFIST Bump
Pixel array
Dummy bump
COMP
SIGNAL
GND
VDD
bump
under bump metal
Pixel
Cylinder bumps are successfully fabricated
3.5mmf

## Slide 22
Summary
Most of my R&D works could not be completed without support from the US-JP program. * FASTBUS  successfully used in TRISTAN * TDC VLSI  successfully used in ATLAS
My present challenge is developing SOI monolithic pixel detector for electron colliders and X-ray applications.
3D integration is promising technology for the future high-energy experiments.
Finally, I could get many US friends through US-JP program.

## Slide 23
Thank You!