## Slide 1
Kevin Martin
Final Design Review
27 September 2018
PIP-II HWR and SSR1 QPM Software

## Slide 2: HWR & SSR1 QPM Software
Agenda
System Specification Parameters
Computer Hardware/Software Logical Diagram
Software Quench Algorithm
Misc. Details

## Slide 3: HWR & SSR1 QPM Software
Design Specification:
 | HWR solenoid | HWR correctors | SSR1 solenoid | SSR1 corrector
# of supplies/circuits | 8 | 16 | 4 | 16
Min/Max current | ±80 | ±10 | ±80 | ±50
Inductance(mH) | 1083 | 80 | 2.64H + 0.16H = 2.83H | 2
Ramp rate (A/s) | ±3.5 | ±10 | ±1.5 | ±25
LdI/dt (load) | 3.8 | .8 | 4.92 | .3
V-LdI/dt limit | 1 | 1 | 1 | .5
SW PS Voltage trip limits | ±8.3 | ±2.84 | ±9.4 | ±5.76
SW PS Current trip limits | ±65 | ±5 | ±65 | ±50
Ripple (% Max I) | <= +- .2 | <= +- .2 | <= +- .2 | <= +- .2
ADC lsb (% Max I) | +- .07 | +- .07 | +- .07 | +- .07
Quench I | 85 | >50 | 89(2.15K) 72(4K) | >50
Current Abs Accuracy | <1% | <1% | <1% | <1%
Current Stability | <1% | <1% | <1% | <1%
PS to Load Cable Lengths | 200’ Max | 200’ Max | 200’ Max | 200’ Max
Cable Type | #2 | #10 | #2 | #3
Cable R/400ft | .064 | .408 | .064 | .084
Voltage to Ground Limits | 350 | 350 | 500 | 500
Quench Detection Time (mS) | 55 | 55 | 55 | 55

## Slide 4: HWR & SSR1 QPM Software
Computer Hardware/Software Logical Diagram
Linux v2.6.32.11 PREEMPT i586 GNU/Linux
Tri-M vdx104+ CPU Board
RTAI v3.8
QPM Application
Diamond Systems Ruby-MM-816A DAC
Diamond Systems DMM-32-DX-AT ADC, DIO
ISA Bus
PEP Server
Controls ACSYS/FE
Ethernet (Consoles / LabVIEW Apps)

## Slide 5: HWR & SSR1 QPM Quench Algorithm
25Hz Low Pass
FIR Filter
Iraw
ADC Ch. #((qpc*5)+0)
10V = 65A
Scale Factor
I
25Hz Low Pass
Differentiating
FIR Filter
Scale Factor
dIdt
C2
Term2
25Hz Low Pass
Differentiating
FIR Filter
Scale Factor
d2Idt
C3
Term3
Quench
Heartbeat
Loopback
ADC Ch. #31
10V = 10V
Check that the Digital
Heartbeat is seen coming
back in this analog channel
else cause Quench.
This a check of the ADC.
Vqabs = (Term1 + Term2 + Term3) - Vcell
100Hz Low Pass
IIR Filter
Vquenchabs
Compare against Absolute Quench Thresholds
+Vqt
-Vqt
Absolute Quench
and/or
Anti-Quench Trip
No Heartbeat
Trip
No Quench Heartbeat
Digital Out Port C
Bit #5
Term1 = -( L2abs / R2 )dVdt
Term2 = ( L1abs + L2abs )dIdt
Term3 = ( (L1abs * L2abs) / R2 )d2Idt
Vcell = Vload - ( R1 * I )
Vquench(n) = K1 * Vq(n) + K2 * Vquench(n-1)
where
K1 = 1 / ((fs / fc) + 1)
K2 = (fs / fc) / ((fs / fc) + 1)
fs = sample frequency = 1000Hz
fc = Cutoff Frequency = 100Hz
R1 = series circuit resistance
R2 = Resistance in parallel with L2
NOTE: This algorithm is executed at 1000Hz.
25Hz Low Pass
FIR Filter
Vload_raw
ADC Ch. #((qpc*5)+1)
+/-10V = +/-10V
Scale Factor
25Hz Low Pass
Differentiating
FIR Filter
Scale Factor
dVdt
C1
Term1
Vload
Vcell = Vload - ( R1 * I )

## Slide 6: HWR & SSR1 QPM Software
The software resides in a GIT software code repository
The following command will get you a copy of the source code: git clone ssh://p-uqpm_hwr@cdcvs.fnal.gov/cvs/projects/uqpm_hwr
The source code is written in C/C++
All operational control/monitoring of the QPMs will be done via ACNET parameters
Trip/Quench data will be plottable using the D25 console application