## Slide 1: Synchronizing protoDUNE-SP and Beam Instrumentation Time-stamps
David Cussans
3rd October 2018

## Slide 2: Hardware

## Slide 3: Status
WR-LEN module in DAQ barracks
  Produces 10MHz and IRIG-B time-stamp
  ProtoDUNE-SP timing system (PDTS) locked to clock from WR-LEN
    Can verify this by looking at interval between WE pulses issued by BI
      Done – see message by Dave Newbold on “timing_hell” Slack channel
Status
  Have timestamp of WE pulses in PDTS time-base.
  BI and PDTS clocks locked
Need a way of double checking synchronization and relating BI time-stamps to PDTS time-stamps

## Slide 4: Status
WE pulse echoed back to BI by PDTS TLU
  LVDSTTL converter
  Current status – can’t see pulses with ‘scope.
Can see time-stamp SPS cycles in TIMBER
  Does the interval match the WE interval?
    i.e. is there a 1:1 mapping
  How is the time-stamp of “Cycle/Extraction” in TIMBER related to the time at which WE signal issued?

## Slide 5: Outstanding Tasks
Record both BI data and PDTS data
  Match WE timestamps in PDTS with Extraction timestamps in TIMBER
Debug output of WE pulses from PDTS
Analyze BI timestamps of WE pulses produced by PDTS
Provide algorithm for converting timestamps in PDTS with timestamps in BI
  Mapping with change run by run
    PDTS not yet able to decode IRIG timestamp from WR-LEN
      Setting PDTS timestamp to Unix time (obtained from s/ware) at start of each run.
Convert to online monitoring task.