## Slide 1: MQXFA Mechanical Design Criteria Setting the context: The magnet structure and load cases
Soren Prestemon, Lawrence Berkeley National Laboratory
LBNL Coordinator & L3 Control Account Manager for Structures
LHC AUP Project
LBNL – October 5th, 2018

## Slide 2: Agenda
Project introduction & Charge to the review team [SP; 15 minutes]
Setting the context: the magnet structure and load cases [SP; 40 minutes]
Structure design criteria – overview [EA; 35 minutes]
Design Criteria for Al-7075-T65 components [EA; 30 minutes]
Discussion [30 minutes]
Closed session [30 minutes]
Closeout [30 minutes]

## Slide 3: Charge to the review committee
1. Are the Design Criteria used for Al-7075-T65 appropriate to specify the design guidelines and develop a methodology to assess components for the MQXFA magnets
2. Are safety factor levels applied to Al-7075-T65 appropriate for the MQXFA Magnets
3. Are data and/or sources of information related to the use of Al-7075-T65 properly documented in the definition of the Design Criteria
Review committee members:
Raymond K. Yee, Ph.D., P.E. Professor and Associate Chair
Director of Product Design Lab Mechanical Engineering Department San Jose State University
Dr. Manuchehr Shirmohamadi
Professor (Part-time)
San Francisco State University

## Slide 4: Outline
Short overview of project
Overview of structural components in the magnet
General considerations:
  Loading cases and anticipated cycles
General Analysis analysis considerations
Process for plastic failure modes
  Grade 1
  Grade 2
  Grade 3
Analysis process for fracture failure modes
  Grade 4
Documentation

## Slide 5: Exploded views of the MQXFA magnet structure

## Slide 6: Primary MQXFA Structure Subassemblies
Shell-Yoke Structure
  Half-length subassemblies
  Joined shell-yoke subassembly, full-length
Coilpack
  Coil pack subassembly
    Load pad stacks
  Collar pack subassembly
    Collar stacks
    Instrumented and GPI wrapped coils
Master Key packages
  Alignment keys
  Load keys
  Bladders
Axial load
  Axial rods, [end plates, wire guides]
Splice Connection box
Magnet support ring
  Instrumentation connector skirt

## Slide 7: Shell –based support structure concept Shown here on HQ
Shell-based support structure often referred as
“bladder and keys” structure developed at LBNL for strain sensitive material
coil
pad
shell
yoke
Slide by Helene Felice

## Slide 8: Shell-based support structure Concept
Shell-based support structure often referred as
“bladder and keys” structure developed at LBNL for strain sensitive material
Slide by Helene Felice

## Slide 9: Shell-based support structure Concept
Displacement scaling 30
Shell-based support structure often referred as
“bladder and keys” structure developed at LBNL for strain sensitive material
Inflated Bladders
Bladder
Slide by Helene Felice

## Slide 10: Shell-based support structure Concept
Shell-based support structure often referred as
“bladder and keys” structure developed at LBNL for strain sensitive material
Displacement scaling 30
Shimming of the load leys
Keys
Bladder
Slide by Helene Felice
Load case 1a
Load case 1b

## Slide 11: Shell-based support structure Concept
Shell-based support structure often referred as
“bladder and keys” structure developed at LBNL for strain sensitive material
Displacement scaling 30
Cool-down
Cool-down
Keys
Bladder
Slide by Helene Felice
Load case 2

## Slide 12: Shell-based support structure Concept
Displacement scaling 30
Energized
Shell-based support structure often referred as
“bladder and keys” structure developed at LBNL for strain sensitive material
Lorentz forces
Cool-down
Keys
Bladder
With shell structure
Support structure allowing fine tuning of the pre-stress
Slide by Helene Felice
Load case 3
Area under consideration today

## Slide 13: Summary of load cases
Load case | Load description
1 | Assembly loading (1a) and room-temperature load (1b)
2 | Cool-down to cryogenic temperature, typically 4.2K or 1.8K
3 | Operation, i.e. the system is subjected to full Lorentz forces during normal operation
4 | Fault Loads, i.e. loads outside of usual fabrication and operation
Note:
“operation” load cycle results in negligible change in stress state of components beyond coilpack subassembly
1
2
3
4

## Slide 14: The graded approach
Concept is to use a consecutively more advanced and detailed analysis as the component and load case are found to result in reduced margin with respect to relevant mechanical figures of merit
Analysis should report the primary stress and the peak stress
  either maximum principle stress or von Mises stress depending on criteria
Plastic collapse failure mode will be analyzed using grades I-III, essentially analytic formulae or FEA
  Most MQXF components will be subjected to FEA
Linear elastic failure mode (grade IV) will be analyzed using the “Load Factor”, which is a function of the critical stress intensity K1c
Failure modes that consist of a combination of the above will be analyzed using the Failure Assessment Diagram

## Slide 15: General considerations
Material properties must be obtained either by measured data on representative material samples, or from documented literature from material of the same composition
Analysis should use material strength data at the temperature of the load case where possible
  Conservative material properties data is allowed when data at actual temperature is not available, as long as documentation is provided verifying they are conservative
Analysis should always err on the conservative side
  For analysis at intermediate temperatures, a linear interpolation of properties is deemed acceptable as that is generally considered conservative
The analysis process described in our document is tailored to the general design process that has been successfully used to date for LARP, with some important stipulations:
  Application of specific criteria is required
  Materials properties used in the analysis must be fully documented and based on the specific chemistry of the material used for the component
  Submodeling is expected under specific conditions, and the validity of the submodel size and boundary conditions must be demonstrated

## Slide 16: Analysis process: grade I
Use analytic or approximate formulae under appropriate conditions to estimate stresses
Compare to criteria for grade I analysis
  If necessary, determine if mitigation is possible/desired or proceed to grade II
If design criteria are satisfied, proceed to document the analysis in a design report
This grade of analysis will only be applied to a few components of MQXFA

## Slide 17: Analysis process: Grade II
Assumes FEA is applied to the component under study
Boundary conditions must be properly applied and fully documented
Proper convergence of the FEA model must be demonstrated
  Local stress concentrations in other components do not need to be resolved if it can be shown that their resolution will not impact the stress state of the part under consideration (effectively applying a variant of St. Venants principle)
Most structural elements of MQXFA are subjected to at least a grade II analysis
Mitigation measures can be applied

## Slide 18: Analysis process: Grade III
For components exhibiting stress concentrations that cannot be resolved via routine mesh refinement studies
  “Advanced” FEA is applied to the component under study: stress concentrations are resolved via sub-modeling
Boundary conditions must be properly applied and fully documented
Mitigation measures should be pursued where necessary
  Component modification to reduce stresses (e.g. fillets)

## Slide 19: Submodeling approach
Identify a local region of the model containing the stress concentration
  Region should extend some multiple of the characteristic length of the concentration zone in order for St. Venant’s principle to be applicable
Identify the displacements and/or tractions from the original FEA model on the sub-model boundary surface
Apply the displacements/tractions as boundary conditions on the submodel
  Good practice: Evaluate the submodel with original mesh size and verify that original stress distribution is found
Refine the submodel mesh until convergence is obtained
  Convergence monitored by ||σvm||max
Monitor submodel interface stresses to verify St. Venant’s principle remains valid, using following FoM:

## Slide 20: Analysis process: Grade IV
For materials that exhibit fracture failure modes a systematic and sufficiently conservative approach must be taken
We apply the ”R6” formulation*:
  Use the mode I stress intensity
  Flaw size (a) is a “variable”; goal is to have a design that meets criteria with a dimension (a) that can be achieved in inspection
  Approach: identify critical flaw size “ac”, e.g. where KI just meets criteria
  Verify that component inspection will identify flaws smaller than “ac”
*British Energy Generation Limited, "Assessment of the Integrity of Structures Containing Defects", 678 R6 Revision 4, Amendment 7, April 2009.
“Influence Coefficients” Gi are tabulated

## Slide 21: Example clarifying notation
Where possible it is recommended to modify the design to either avoid stress concentrations resulting in plastic deformations, or limit the size of the plastic region for subsequent analyses.
Take into consideration stress distribution in component to 3rd order (beyond membrane and bending)

## Slide 22: Determination of load point in the Failure Assessment Diagram
For a given component & load:
  Evaluate critical intensity Kic
    Measured data
  Evaluate flow stress σc
  Evaluate/estimate KI and σ,
  Find (S’r,K’r)
  Evaluate (Sr,Kr)
  Determine the Load Factor:
  The Load Factor is then used for design criteria assessment

## Slide 23: Grade IV analysis – additional elements
If there is stress concentration that exceeds yield strength
  Perform bi-linear (i.e. conservative) elasto-plastic simulation and verify that plastic region (defined by 3% coincidence definition) is not larger than the critical flaw size identified by the FAD process
Any allowed KI must be in the elastic regime
  Mitigation measures must be implemented to address this criteria

## Slide 24: Documentation
Each structural component of the MQXFA magnet is expected to have a document detailing application of the design criteria
  A single document may address more than one component
  The document must address the following elements:
    Design Data – e.g. material properties used in the analysis, and how they were obtained
    Graded Analysis - application of the graded approach, e.g. equations used, boundary conditions applied, transition from one grade to the next, etc
    Assessment of Analysis – application of any mitigation measures, details of FEA, demonstration of convergence, etc
    Application of Design Criteria - confirmation that final design meets criteria

## Slide 25: MQXFS – Magnet Powering Courtesy Giorgio Vallone
Shell azim. stress variation during powering:
  Very small/negligible until pole/coil unloading
  At ultimate current, lower than 10 MPa (<5% of the stress after C.D.)
Rod long. stress variation during powering:
  Function of the structure (thin/thick iron laminations)
  At ultimate current, equal to about 5 or 7 MPa.
  Strain signals can be used to extract the coil elongation (<0.01%)
Delta of stress: shell
Delta of stress: rods
~2-5% of σφ,max

## Slide 26: Application of Paris Law integration suggests negligible crack growth in Al-7075-T65 shells
Paris law is applied to verify that crack growth is negligible for the 5000 cycles required by the Functional Requirements (suggestion from a reviewer)
ΔK for the 7075-T65 Al shell under cyclic loading from 0<I<Iult
=> Below threshold (~2.3)
 | M (MPa) | B+M (MPa)
B=0 | 319 | 382
Norminal | 330 | 401
Ultimate | 337 | 409
M-- Membrane stress;
B+M --- Bending + Membrane stress
Note: Values are in stress concentration region;
In main shell area the values are 171MPa & 181MPa
Note: measured yield strength at 4.2K is ~635MPa
(469MPa at RT)
At this growth rate, 5000 cycles results in 0.15mm growth

## Slide 27: Extra - Shell